## Slide 1: EMFCAMP 2012
Internet to a field
Nat Morris and Will Hargrave
UKNOF23 9th October 2012

## Slide 2
3 day festival – Fri 31st Aug to Sun 2nd Sept
Ran by volunteers
Geeks / hackers / makers
500 licensed capacity – sold out
What was EMFCamp 2012?
Photo: Russ Garrett

## Slide 3
Site location

## Slide 4
Site location
Rented from Milton Keynes Parks Trust - £1,900

## Slide 5
Festival site
Talks and presentations
Photo: Kitty Wong

## Slide 6
Festival site
Photo: Lionel Montrieux
Balloon launch

## Slide 7
Festival site
Photo: Graham Morris
Radio station and video streaming

## Slide 8
Festival site
Photo: Nottinghack
Workshops

## Slide 9
Festival site
Photo: Russ Garrett
Licensed bar under M1 bridge

## Slide 10
Festival site
Photo: Russ Garrett
Licensed bar under M1 bridge

## Slide 11
Festival site
Photo: Andy Brockhurst
Retro gaming tent

## Slide 12
Badge
Atmega328
Microcontroller
2.4ghz radio
MicroUSB
IR rx
IR tx
Photo: Lionel Montrieux
Sponsored by UCL

## Slide 13
Requirements:
100mbit+
Site-wide wireless
Ethernet + power to every tent
Fully dual stack
Visibility of the whole network
Multicast video
Infrastructure
Photo: Andy Brockhurst

## Slide 14
Infrastructure
Jasper
Benny
David
Will
Claire
Nat
Mat
Graham

## Slide 15
Attempted to apply for temporary address space from RIPE NCC, sponsored by Goscomb.
Issued ASN, v4 + v6 PI then retracted by hostmaster after they realized they could only issue it 7 days before the event. Far too late – equipment was already configured and boxed by then.
RIPE-526 – broken 
Going back to address-policy-wg to alter the policy.
Address space

## Slide 16
CCC / Chaos Computer Club to the rescue!
Loaned us:
AS13020
2001:067c:20a1::/48
94.45.224.0/19
But now Google is in German and BBC website carries adverts – never mind.
Address space

## Slide 17
Backhaul
No existing copper or fibre
BlueSquare Milton Keynes (now Pulsant)
2.9km away

## Slide 18
Backhaul

## Slide 19
Hired two 30m mobile masts / VersaTowers
  £1,440 for 7 days inc delivery + collection
Backhaul
Photo: David Croft

## Slide 20
Backhaul
Jasper’s cycling jacket
Photo: Jasper Wallace
27m cherry picker

## Slide 21
Backhaul
Spotting
Photo: Mat Burnham
17m cherry picker

## Slide 22
Backhaul
Photo: Rapid Wireless
Looking from the site towards Pulsant
Frank + Mervyn

## Slide 23
Primary link
DragonWave Horizon Compact
400mbit/s full duplex
18ghz OFCOM licensed
Hired from RapidWireless - £2,300
Backhaul
Photo: Nottinghack

## Slide 24
Secondary link
Ubiquiti Nanobridge M
100mbit/s
5.4ghz
Bought from Linitx - £112 (for 2)
Backhaul
Photo: Nottinghack

## Slide 25
Backhaul
2 x Cisco 7206 NPE-G2
Installed in June / July

## Slide 26
Goscomb
Transit
Pulsant
Transit
MK L3 Switch
ME3400
DragonWave
Ubiquiti
Ubiquiti
DragonWave
Core 1
3750G
Core 2
3750G
OOB
OOB
MK Router
7206 NPE-G2
Backhaul
LONAP
V4 + V6
Peering
V4 Multicast
THDO Router
7206 NPE-G2
1G
100M
100M
1G
1G
1G
1G
1G
1G
1G
Telehouse East
Pineham Park

## Slide 27
http://tinyurl.com/emfcore
Backhaul

## Slide 28
NOC
£25 donation to the Scouts
Photo: David Croft

## Slide 29
NOC
Network required power so ended up running that

## Slide 30
NOC

## Slide 31
NOC
Food / work / social area

## Slide 32
NOC
Data centre partitioning!

## Slide 33
NOC
Core rack

## Slide 34
NOC
Nagvis

## Slide 35
NOC
Bandwidth monitor

## Slide 36
Automation
Google Spreadsheet
Schedule
Budget
IP Plan
DHCP Scopes
Monitoring
Google Data API
DNS Zones
Forward
Reverse
DNSSEC Signing
DHCP Scopes
- dhcpd.conf
Nagios
- Services per host
Rancid
https://github.com/emfcamp/emfnoc
Switch IOS config

## Slide 37
Distribution

## Slide 38
Distribution
http://tinyurl.com/emfdistro

## Slide 39
Distribution
SFP’s sponsored by FlexOptix

## Slide 40
Distribution
Staging from June in Nat’s loft
GRE tunneled back to MK
Config, document + monitoring

## Slide 41
Distribution
£60/wk hire
Photo: Paul Miller

## Slide 42
Distribution
Photo: David Croft

## Slide 43
Distribution

## Slide 44
Distribution
Typical Datkenklo

## Slide 45
Distribution
Raspberry Pi colo

## Slide 46
Distribution
Multicast video
BBC R&D trial over LONAP
On wired + wireless
Local SAP server
http://support.bbc.co.uk/multicast/

## Slide 47
Wireless
Dual Cisco WLC 4402 Controllers

## Slide 48
Wireless
WCS AP mapping

## Slide 49
Wireless
Luke’s AP association hack
http://stats.emfcamp.org/luke/
Luke Brookes
Twitter: @propuke

## Slide 50
Stats

## Slide 51
Stats
More at http://stats.emfcamp.org

## Slide 52
Feedback

## Slide 53
What next?
Photo: Andy Davidson
EMF will return in 2014
Aiming for ~1500 capacity
We need your help!
Telcos with clue who can help with fibre
Network engineers who can brave the sunshine 

## Slide 54
Questions?
Photo: Russ Garrett