## Slide 1: Akamai & ISPs
Patrick W. Gilmore, Chief Network Architect
UKNOF25
April 18, 2013

## Slide 2: Agenda
Disclaimer
Rules
What is a CDN, types of CDNs
Akamai’s topology
Peering, from both sides
Mapping

## Slide 3: Disclaimer
I was asked to give a talk about Akamai’s CDN, not CDNs in general
While some of the information may be general enough to apply to all CDNs, I made no effort to generalize the information
In Other Words: Your Mileage May Vary

## Slide 4: A Few Simple Rules
There are exceptions to every rule
    When I say “X == Y”, please hear “except for these few corner cases” even if I do not say it
This is very high level
    We only have 30 minutes, I need to gloss over some details
Questions are welcome & encouraged
    This is for you, be sure you get the most out of it

## Slide 5: What is a Content Distribution Network?
The RFCs and Internet Drafts define a Content Distribution Network, “CDN”, as:
  Content Delivery Network or Content Distribution Network. A type of CONTENT NETWORK in which the CONTENT NETWORK ELEMENTS are arranged for more effective delivery of CONTENT to CLIENTS.

## Slide 6: What is a CDN - In English? (Or at least American?)
A CDN is an overlay network, designed to deliver content from the optimal location
Very Generally: Users in Tokyo go to a server in Tokyo, users in Frankfurt go to a server in Frankfurt
This obviously over-simplifies things, as “optimal” is frequently not equivalent to “geographically close” – topology matters
  Obviously serving users in Beijing from Johannesburg is unlikely to be optimal for a global CDN no matter the topology

## Slide 7: To Network Or Not To Network
Some CDNs have a network (i.e. backbone)
  E.g. Level 3, Limelight
  Typically CDNs owned by a network will have a network (shocker)
Some CDNs do not
  E.g. Akamai, EdgeCast, CloudFlare
Network-based CDNs have most of their servers in their own CDN
Non-Network CDNs can place servers directly in other ASNs
  Which means you cannot find their traffic with NetFlow

## Slide 8: Akamai’s CDN (Requisite Marketing Slide)
Akamai is the largest CDN in the world
  3rd party estimates show Akamai’s traffic equal to or greater than all other CDNs combined
Delivering:
30+ million hits / second
1.7+ trillion hits / day
Double-digit Tbps
The Akamai EdgePlatform:
130,000+
Servers
~2,200
POPs
81
Countries
~1,200 Networks
800+ Cities

## Slide 9: Akamai’s CDN
Akamai’s CDN is comprised of distinct, geographically & topologically disparate nodes
We believe having lots of nodes in lots of places gives us better performance than a few large sites
[…]
London
New York
Tokyo

## Slide 10: No Backbone
It is important to realize there is no network between Akamai nodes
[…]
London
New York
Tokyo

## Slide 11: No Backbone
It is important to realize there is no network between Akamai
Even if they are in the same city
[…]
Telehouse
Redbus
HEX8/9

## Slide 12: No Backbone
It is important to realize there is no network between Akamai
Even if they are in the same city
In fact, Akamai nodes in the same building do not share traffic
[…]
THN floor 3
THN floor 4
THN floor N

## Slide 13: Origin GETs
Since each node is an island, there is no way for Akamai to deliver content to a node ourselves
Origin Server
Origin GET ?

## Slide 14: Origin GETs
Since each node is an island, there is no way for Akamai to deliver content to a node ourselves
Akamai’s “backbone” is the Internet
  Also used for log delivery, SSH’ing to servers, etc.
Origin Server
Origin GET
Internet

## Slide 15: Origin GETs
Since each node is an island, there is no way for Akamai to deliver content to a node ourselves
Akamai’s “backbone” is the Internet
  Also used for log delivery, SSH’ing to servers, etc.
Each node goes back to the origin independently
Origin Server
Origin GET
Internet

## Slide 16: Large Akamai Nodes, up close & personal
Large nodes have a mix of content types
Some servers will serve Flash streaming, others serve HTTP, etc.
Different content types typically require separate physical machines
  Flash works best on Windows (ugh), HTTP runs on unix (yay), etc.
  But also because different software requires different hardware, does not play well with others, etc.
Flash
HTTP

## Slide 17: Small Akamai Nodes, up close & personal
Small nodes have a single server type (HTTP)
Each content type requires a minimum number of machines (usually 3-5), ruling out multiple content types on some nodes
Even nodes with enough machines may only serve HTTP
HTTP
HTTP

## Slide 18: Small Akamai Nodes, up close & personal (2)
In addition to only serving HTTP, small nodes cannot serve all HTTP content
The fact there are only a few servers limits the amount of storage, meaning not all content can be cached
Because very few networks have enough traffic to require nodes large enough to carry all content types and all customers, it is important to peer with Akamai even if you have an on-net node

## Slide 19: Why Akamai peers with ISPs - performance
The first and foremost reason to peer is improved performance
  Since Akamai’s entire reason for existence is to improve performance, peering directly with networks (over non-congested links) obviously helps
Traffic served over peering typically performs better than over transit
  Sometimes there is no difference or (rarely) peering is worse, but no one here is like that, right?
Removing intermediate AS hops allows higher peak traffic for the majority of end user Ases
    I cannot prove why this is true, but we have hard data showing it is
    Anyone have ideas? (I have a few, but would like to hear yours)

## Slide 20: Why Akamai peers with ISPs (2)
Lots of other reasons:
  Redundancy
  Burstability
  Network Intelligence
  Backup for on-net servers
  Serving additional content types
While all those are important, they really all are related to performance
So the real second reason to peer is cost (duh)

## Slide 21: Why you should peer with Akamai
Why not?
  CDNs and ISPs are in the same business, just on different sides - we both want to serve end users as quickly and reliably as possible
Cost Reduction
  Transit savings
  Possible backbone / backhaul savings
Because you are nice
  Doesn’t everyone want to be nice?

## Slide 22: Akamai at IXPs
Transit
Peer Network
Origin Server
IX
Content
Peer Network
[ . . . ]
Remember each node is an island
  The CDN uses transit to pull content into the servers
  Content is then served to peers over the IX
This is designed specifically to appear exactly like any other peer

## Slide 23: Akamai & Private Peering
Peer Network
Transit
Content
Origin Server
Private peering is just the degenerate case of an IXP – i.e. an IX with one peer

## Slide 24: Akamai & Private Peering
Peer Network
Content
Private peering is just the degenerate case of an IXP – i.e. an IX with one peer
Of course, Akamai usually sets up more than one peer per node to get economies of scale
Peer Network
Peer Network

## Slide 25: Akamai’s traffic control
Akamai also has (IMHO) amazing control over our traffic
This is an actual graph of an Akamai IX port over a week
  Time for an upgrade maybe?

## Slide 26: Mapping
Most people think of Akamai as a caching company
Caching objects is something Akamai does, but the Akamai’s core business is Mapping the Internet
Akamai makes these decisions in near-real time, adjusting to performance changes in 10-30 seconds
Deciding which end users should go to which web (streaming, whatever) servers is hard

## Slide 27: Mapping & DNS
Akamai maps end users through DNS
Specifically, querying the same hostname from different locations will return different A records
Traffic is still routed to the end user directly
  No transparent caching
  No WCCP
  No HTTP redirects
  Etc.

## Slide 28: Mapping Decision Steps
Akamai’s Mapping has a few steps:
  User types www.customer.com into browser
  User’s machine goes to ISP’s recursive name server
  ISP’s RNS goes to [roots, GTLDs] customer’s NS and asks for A record
  Akamai responds with CNAM to a1.g.akamai.net
  ISP’s RNS goes to [roots, GTLDs] Akamai’s NS and asks for a1.g.akamai.net
  Akamai responds with a delegation for g.akamai.net
  ISP’s RNS asks Akamai’s second level NS for a1.g.akamai.net
  Akamai responds with at least two IP addresses
  ISP’s RNS answers user’s machine

## Slide 29: Akamai’s DNS mapping visual aid
TLNS == Top Level NS
  I.e. IP address handed out by the GTLDs
LLNS == Low Level NS
  I.e. IP address delegated by the TLNS
“Ghosts” (should be “GHost”) is Akamai’s code name for our web servers: “Global Host”

## Slide 30: Users vs. Name Servers
Note at no time during the Mapping decision, did the Akamai name server ever speak directly to the user
Even if we wanted to map by user IP address, we could not as we do not have it when we make the Mapping decision
Moreover, even if we did, the ISP’s RNS caches the answer and hands the same IP address to the next end user without asking Akamai again

## Slide 31: Users vs. Name Servers (2)
This means if a user configures an off-net name server Akamai will map the user where the name server is, not where the user is
If you dig an Akamai hostname against a name server in Tokyo or San Jose from a machine, you will get an Akamai server in Tokyo or San Jose
  Ignoring the fact there shouldn’t be any open recursive name servers…
The most obvious examples of this are OpenDNS and Google DNS
  Yes, we are working on fixes, but they will not work for all ISPs
  Easier just to assure your users are configured with a local name server

## Slide 32: Example of Mapping
Example of CDN mapping
  Notice the different A records for different locations:
[London]% host www.symantec.com
www.symantec.com CNAME a568.d.akamai.net
a568.d.akamai.net A 207.40.194.46
a568.d.akamai.net A 207.40.194.49
[Boston]% host www.symantec.com
www.symantec.com CNAME a568.d.akamai.net
a568.d.akamai.net A 81.23.243.152
a568.d.akamai.net A 81.23.243.145

## Slide 33: Mapping Selection Criteria
Akamai uses many metrics for Mapping, including the standard latency, packet loss, throughput
Akamai also includes things like CPU load, available storage, network utilization, where content is already cached, etc.
Geography still counts
  That whole speed-of-light thing
  100G Ethernet solves that, right … ?

## Slide 34: Example of bad Mapping
Tracing from IAD to www.facebook.com
pgilmore@prod-unix-shell01:~> nsh 72.246.30.12 mtr -d www.facebook.com
HOST: a72-246-30-12.deploy.akamai Loss% Snt Last Avg Best Wrst StDev
1. a72-246-30-1.deploy.akamaite 0.0% 10 0.4 0.4 0.3 0.5 0.1
2. dc5.pr01.iad2.tfbnw.net 0.0% 10 0.3 0.3 0.2 0.5 0.1
3. ae1.bb02.iad2.tfbnw.net 0.0% 10 16.9 3.0 0.5 16.9 5.5
4. ae11.bb02.sjc1.tfbnw.net 0.0% 10 80.0 82.9 78.0 89.3 3.3
5. ae2.dr01.snc5.tfbnw.net 0.0% 10 82.8 87.2 82.6 127.2 14.0
6. po510.csw02a.snc5.tfbnw.net 0.0% 10 82.1 81.9 81.7 82.1 0.1
7. www-11-02-snc5.facebook.com 0.0% 10 72.4 72.9 72.4 76.7 1.3

## Slide 35: Example of bad Mapping
Tracing from SJC to www.facebook.com
pgilmore@prod-unix-shell01:~> nsh 173.223.232.110 mtr -d www.facebook.com
HOST: a173-223-232-110.deploy.aka Loss% Snt Last Avg Best Wrst StDev
1. a72-246-53-1.deploy.akamaite 0.0% 10 4.3 3.3 0.4 9.7 3.8
2. paix.br01.pao1.tfbnw.net 0.0% 10 0.2 4.7 0.2 45.3 14.3
3. ae8.bb02.pao1.tfbnw.net 0.0% 10 0.4 5.0 0.4 44.8 14.0
4. ae8.bb02.iad1.tfbnw.net 0.0% 10 78.6 76.5 76.2 78.6 0.8
5. ae1.dr02.ash4.tfbnw.net 0.0% 10 76.1 77.7 76.1 91.9 5.0
6. po509.csw01a.ash4.tfbnw.net 0.0% 10 78.5 78.5 78.4 78.6 0.1
7. www-11-01-ash4.facebook.com 0.0% 10 76.3 76.4 76.3 77.0 0.2

## Slide 36: Example of good Mapping
Tracing from SJC to www.symantec.com
pgilmore@prod-unix-shell01:~> nsh 173.223.232.110 mtr -d www.symantec.com
HOST: a173-223-232-110.deploy.aka Loss% Snt Last Avg Best Wrst StDev
1. a173-223-232-105.deploy.akam 0.0% 10 0.1 0.2 0.1 1.6 0.5
OK ,that was cheating 

## Slide 37: Example of good Mapping
Tracing from a server in ORD to www.symantec.com
inv2824# traceroute www.symantec.com
traceroute: Warning: www.symantec.com has multiple addresses; using 64.211.144.66
traceroute to a568.d.akamai.net (64.211.144.66), 64 hops max, 40 byte packets
1 fe0-23.aggr3004.ord2.us.scnet.net (75.102.4.185) 0.629 ms 0.535 ms 0.661 ms
2 v1503.ar1.ord1.us.scnet.net (216.246.94.209) 21.738 ms 1.778 ms 0.513 ms
3 ae0-81.cr1.ord1.us.nlayer.net (69.31.111.1) 0.282 ms 0.389 ms 0.292 ms
4 ae1-30g.ar1.ord1.us.nlayer.net (69.31.111.134) 12.214 ms
ae1.ar2.ord1.us.nlayer.net (69.31.111.146) 0.517 ms
ae1-30g.ar1.ord1.us.nlayer.net (69.31.111.134) 16.753 ms
5 te9-3.ar3.CHI2.gblx.net (69.31.110.233) 0.699 ms
te6-3.ar2.CHI2.gblx.net (69.31.111.201) 1.000 ms
te9-3.ar3.CHI2.gblx.net (69.31.110.233) 1.203 ms
6 ge9-1-10G.ar2.CHI2.gblx.net (67.17.109.117) 0.687 ms 0.710 ms
64.211.144.66 (64.211.144.66) 0.514 ms

## Slide 38: Questions?
patrick@akamai.com