## Slide 1
Cube Optics
100G Metro Networks - It’s here!
13th September 2013
05.08.2010

## Slide 2: Why 100G in Metro?
  Not all traffic is long haul
  Higher speeds, low latency
  Switch / Router vendors need to reduce port count
  High density with lower power consumption
August 2011

## Slide 3: 100Gbps Metro Networks
Requirements:
  100Gbps DWDM CFP transceiver module
    Transports 4x25Gbps.
    Four single mode duplex fibers.
    Employs tunable lasers in the 50GHz ITU-T channel grid (DWDM) with four receivers.
  96 Channel DWDM multiplexers/demultiplexers
    Passive DWDM mux/demux with 50GHz grid over a single mode fiber pair.
    Up to 24 "differently colored" 100Gbps DWDM CFP transceivers can be transported via a 96 channel
Ch .1
Ch .2
Ch .3
Ch .4
50GHz
DWDM
Mux
1
2
3
4
5
6
7
8
….
96
2.4Tbps
    Reach extendable with standard, stand-alone EDFAs to >100kms
…
CFP1
CFP2
CFP24
CFP1

## Slide 4: Upgrade Scenario
4 in 100GHz
100G CFP
….
Amplification
Compensation
100GHz
DWDM
Mux
10G SFP
100GHz
DWDM
Mux
50/100 GHz INT
….
….
100GHz
4x25G CFP output
100GHz
10G SFP
Odd channels
Even channels
    Complementing the existing 10Gbps system with 100Gbps upgrades

## Slide 5: Issues to be aware of
  100Gbps DWDM CFP offers 15-20km reach
  The reach can be further extended 10 > 100km but one has to take care:
    Amplification
    Dispersion Compensation
    FEC, error correction option
    Upgrade scenario, fiber types and other co-propagating channel information (10G/ 40G)
More Information:
http://www.cubeoptics.com/competence/100G_Metro_Evolution/

## Slide 6: Contact us!
We look forward to providing you with further information.
Contact:
Steve Jones
+44 (0) 7900 881729 steve.jones@cubeoptics.com
www.cubeoptics.com