## Slide 1: LTE as a Video & TV Distribution Network
THE MOBILE VIDEO ECOSYSTEM
Bob Sleigh
UKNOF27 Manchester 21st Jan 2014

## Slide 2: Mobile Network Capabilities
50 kbps
2.5G/Edge
Interactivity
speeds
Voice, Text
Data Capacity
Email
MMS
Music, Web browsing
Rich Messaging & Communication
3G
HSPA+
Apps, Downloading
Video Streaming
4G/LTE
HSPA
HD Video Streaming
100 kbps
240 kbps
0.7 Mbps
4-6 Mbps
8-12 Mbps
4G+/LTE-A
4K Video & Multi-task
Min Speed?
30-50 Mbps
16-24 Mbps
Gaming / Cloud
Video Conf
100 kbps
250 kbps
340 kbps
1.8 Mbps
21 Mbps
73 Mbps
300 (Cat6) -> 1000 Mbps
100- 150 Mbps (Cat 3/4)
Typical
Peak

## Slide 3: LTE - UK is becoming a global leader
LTE
October 2012 First LTE live in UK
December 2013 over two-thirds of population coverage
…
December 2014? 98% population coverage
LTE-A
November 2013 Techcity LTE-A 300Mb Trial
During 2014 First commercial LTE-A live in UK

## Slide 4: Forecast Mobile Data & Video Demand for UK
Mobile Data
Mobile Video

## Slide 5
What does ‘Good’ look like? How do you benchmark QoE?
Short form or long form
Live, catch up or VOD
Purchased or free
Device type
Buffering or adaptive streaming
Amount of buffering or lower bit rate
Where in the video this occurs
Original quality of the video (SD, HD etc)

## Slide 6
Video Codec Evolution How the evolution in video codec’s can reduce bandwidth
Reduced bit rate and file size but similar resolution
Reduces network traffic
Improved User Experience with lower bandwidth
High Efficiency Video Coding (HEVC) has nearly halved the bit rate and file size of the previous HD standard – Advanced Video Coding (AVC)
Combining the latest compression technology with Adaptive Bit Rate (ABR) technology could provide a reduction in traffic whilst maintaining a higher QoE
HEVC is one of the key elements in the move towards Ultra High Definition TV (UHDTV) which is likely to push the bit rate back up to AVC levels
HEVC (H.265) Video
PSNR – 39.72dB
Bit Rate 610kbps
File Size 3.10MB
AVC (H.264) Video
PSNR – 39.65dB
Bit Rate 1183kbps
File Size 6.01MB

## Slide 7
Adaptive Bit Rate Technologies Using Adaptive Bit Rate (ABR) to manage video traffic
Historically, mobile video streamed at a fixed bitrate
Buffering and loss when connection speed too low
Users preferred lower resolution over buffering
  User could sometimes select video resolution
ABR tailors stream to the device and available bandwidth
Connection speed changes, bitrate adapts in real time
  Reduces buffering
  Better user experience in congestion and at cell edge
  Minimises user interaction
Left unmanaged, ABR can lead to unpredictable data usage
  Content streams at the highest bit rate available
  HD uses significantly more data than SD

## Slide 8
Standardisation - DASH Standardising ABR with Dynamic Adaptive Streaming over HTTP
Multimedia file partitioned into segments
MPD file describes segment information
  timing, URL, media characteristics eg video resolution, bit rates
Delivered to client using HTTP
DASH is audio/video codec agnostic
Segments can contain any media data
But spec provides specific guidance and formats
  MPEG-4 file format
  MPEG-2 Transport Stream
Multiple representations (different resolutions, bit rates)
Selection can be made based on
  Network conditions, device capabilities, user preferences

## Slide 9
Multimedia broadcast technology An example of live sport driving data usage
Man U vs Liverpool
KO 13:30
Arsenal vs Man City
KO 16:00
Half Time
Bandwidth (actual bandwidth removed due to sensitivity)

## Slide 10
Caching mobile video Pro’s and con’s of caching video within a mobile network
Aggregation
Sites
Can be deployed in smaller numbers
Helps with internet bottlenecks
Supports operator optimisation
Suboptimal for YouTube (unless using GGC)
Unless optimisation platform installed limited advantages over using CDN
Low cost delivery
Value add content
Disparate solutions
Complex integration
Devices
(Multiple Millions)
Connectivity Sites (10’s)
Reduces capacity on core infrastructure
Aggregates multiple 1000’s of cell sites
No benefit over aggregation sites.
Efficient use of backhaul
Technology in development
Good for dense environment
Reduces latency
Does not address spectral constraints
Number of users viewing same content
Cell Sites
(10’s of thousands)
Co-location Data Centre London
Hosting costs
Requires redundant capacity
Minor improvement in Latency
Main CDN’s and content providers have a presence
Peering is inexpensive
CDN’s are optimised for video
No significant investment for operator owned and operated infrastructure
No opportunity for operator optimization

## Slide 11
Multimedia broadcast technology How reduce video traffic using broadcast technology
  BBC & Sky predict rise in linear TV over the mobile networks
  MNOs reviewing commercial/technical viability of broadcast technologies
  The current technological standard for LTE is eMBMS
  evolved Multimedia Broadcast Multicast Service
  Huawei - technology centre in Shenzhen for development of eMBMS
  Qualcomm - demonstrated eMBMS with E/// at MWC2012
  Verizon - may do Superbowl 2014 over eMBMS

## Slide 12
Video distribution - Satellite Comparing mobile video delivery with traditional methods
Alignment of technical roadmaps
Control of QoE
Ability to be able to perform end to end testing

## Slide 13
Video distribution - Mobile Comparing mobile video delivery with traditional methods
?????

## Slide 14
Current and future technologies Analysis of current and future Mobile Video technology
There is currently a technology disjoint in the end to end mobile video chain. Without increased communication and knowledge share between the parties technology advances cannot be fully exploited
Content caching
  Device
  Core
  Edge
Video codec evolution
Adaptive Bit Rate
Multimedia broadcast technology
Video optimisation platforms
Content Delivery Networks
  Self build
  Pure play
  Federations
There is no ‘Silver Bullet’ as an operator we will need to a have a constantly evolving ‘tool kit’ of technologies

## Slide 15
Where now? 2014 – When mobile video becomes an ecosystem
Industry discussion and knowledge share is key to a successful mobile video industry
Ensuring Users QoE is not impacted by the ‘Mobile Video Tsunami’ can no longer be seen as something for operators to sort out alone
Any party working in isolation may negatively impact the customer experience
and cost to serve
An end to end understanding of mobile video technologies
will lead to greater innovation from all parties
Use the combined weight of the whole industry to back
mutually beneficial technology e.g. MPEG-DASH
Globally congested mobile networks do not benefit anyone

## Slide 16: Thank you