## Slide 1: Imtech ICT & the Juniper Networks MX BNG
David Clisby, Technical Consultant. JNCIE

## Slide 2: Introduction
Imtech are a System Integrator (we don’t just ship tin)
  Juniper UKI partner of the year
  Juniper UKI Operate Support Services partner of the year
  Vast Experience with Juniper Portfolio
  JNCIE and CCIE Consultants
    Project focussed
    All specialise in Routing and Switching but each also have development areas of interest

## Slide 3: Introduction
My development area currently is JUNOS MX BNG
  Porting E series configuration to MX
  Working closely with SPs to develop NG Broadband products
  Designing new H-QoS models
  Developing Seamless MPLS Backhaul links

## Slide 4: MX BNG
From the Small MX5 to the LARGE MX960
  Scaling numbers vary by model and code version
    Scales more as you move up the range and later the code
  Native PPPoE / LAC
    Available on all platforms
    Scaling license required
  L2TP LNS (LTS in 13.2)
    Available on all platforms (license required)
  H-QoS on MX80 MIC slots and MPC Q and EQ (QX Chip)
    Options of 4 or 8 queues per subscriber
      Defined at the PIC level
      4 Queues provides maximum scaling
      8 Queues halves the subscriber scaling number per PIC

## Slide 5: L2TP LNS
Makes use of Inline Services (si interface)
  MX5 through to MX960
  Anchors L2TP sessions on the MPC Q
  Can use any port based MPC for access interfaces
  Works in a similar way to the tunnel modules on E series
  License required for LNS
  Up to 128K subscribers on an MX960
    With 8 Queues per subscriber using MPC2 EQ

## Slide 6: Subscriber H-QoS
Uses MX Style QoS
  Traffic Control profiles
  Classifiers
  Rewrite rules
  Schedulers
  Scheduler-maps
  Interface-sets
No ‘huge’ learning experience for JUNOS engineers
  Plenty of reference material
  O’Reilly Juniper MX Series book is very useful
    Doesn’t expand on broadband but QoS is well explained
    Useful shell commands

## Slide 7: Seamless MPLS
Will scale to 2K pseudowires per chassis in 13.3R3
  Ideal for MSAN backhaul
No external cabling required
  Loops internally using Tunnel-Services
PPP interfaces ride on top of PWHT
HQoS available for PWHT
Imtech are currently working with Juniper to enhance the scaling of PWHT
Working with Juniper to enhance the NAS-Port-ID

## Slide 8: Radius Integration
Works with the majority of VSAs used with the E series
  New VSA 108 used for Subscriber HQoS

## Slide 9: Supported Code Versions
Juniper branched the code for broadband stability
  11.4X27 First official Broadband feature release
  12.3R3 and above on this feature release (R5,R6…)
  13.3R3 and above (R4, R5…)
What does this mean
  Some services like LTS and PWHT are available today in 13.2
  Juniper won’t officially support until 13.3R3
  Good chance to test and work with Juniper to develop product ahead of GA.

## Slide 10: Questions?
Imtech ICT
Viables 3
Jays Close
Basingstoke
Hampshire
Tel. +44 1256 312 350
Fax +44 1256 312 377
www.imtechICT.co.uk