## Slide 1
Segment Routing:
An Architecture build with SDN in mind and addressing the evolving network requirements
Brian Meaney
Cisco SP Consulting Team

## Slide 2
Application Enabled Forwarding
  Each engineered application flow is mapped on a path
  A path is expressed as an ordered list of segments
  The network maintains segments
Simple: less Protocols, less Protocol interaction, less state
  No requirement for RSVP, LDP
Scale: less Label Databases, less TE LSP
  Leverage MPLS services & hardware
Forwarding based on MPLS label (no change to MPLS forwarding plane)
Label distributed by the IGP protocol with simple ISIS/OSPF extensions
50msec FRR service level guarantees via LFA
Leverage multi-services properties of MPLS
Millions of Applications flows
A path is mapped on a list of segments
The network only maintains segments
No application state
The state is no longer in the network but in the packet
Segment Routing
Basic Capabilities and Characteristics

## Slide 3
65
A packet injected anywhere with top label 65 will reach Z
Nodal/Prefix Segment: label allocated from the SR registry to each node. Globally significant. For example Z is given label 65.
9001
Adjacency Segment: Node automatically allocates a local label for each adjacency. Locally significant. For example Label 9001 allocated for adjacency O.
A packet injected at node C with label 9001 is forced through datalink CO
A
B
C
M
N
O
Z
D
P
A
B
C
D
Z
M
N
O
P
Segment Routing
Basic Operation and Segment Types
Source Routing: The source chooses a path and encodes it in the packet header as an ordered list of segments.
Segment: An identifier for any type of instruction i.e. "go to node C using the shortest path"

## Slide 4
Any explicit path can be expressed i.e. ABCOPZ
A
B
C
M
N
O
Z
D
P
9001
Packet to Z
65
9001
Packet to Z
65
Packet to Z
Packet to Z
65
Packet to Z
65
9001
72
Packet to Z
65
9001
72
72
72
65
65
Segment Routing
Segment Routing Label usage
A
B
C
D
Z
M
N
O
P

## Slide 5
Network conditions reported to collector, accessible to App
Congestion threshold triggers app to request Prem Cust. to Prem Path Mapping
WAN Controller computes SR path;
Programs:
<SR label stack via Protocol> <Prem Cust. Classifier >
1
2
WAN (SR)
Off-Net
R1
R2
R3
4
Premium
Normal
Congested!!
R7
4
High Priority Customer App
3
Collector & modelling
Programming
Visualization &
Analytics
Bandwidth
Orchestration
NB API
BGP-LS, SNMP, I2RS
PCEP
CL
CL
Segment Routing
Usecase : Premium Content to Premium Path using Segment Routing via Path Computation
WAN Controller
Notes: Chris metz use case

## Slide 6
A centralized Controller should be able to instruct an ingress PE or content source within the domain to use a specific egress PE and a specific external interface to reach a particular destination
Centralized Controller called the EPE Controller
Egress Border router is EPE-enabled border router -> EPE traffic steering
Input policy at the source host/ingress border router -> “EPE Policy”
PeerNode SID (SID bound to an eBGP Peer), PeerAdj SID (SID bound to an external interface), PeerSet SID (local SID bound to set of eBGP peers)
Segment Routing: Egress Peer Engineering (EPE)
Problem statement :
http://www.ietf.org/archive/id/draft-filsfils-spring-segment-routing-central-epe-02.txt

## Slide 7
AS1
AS2
AS3
AS4
B
C
D
E
BGP-LS
or BGP-LU
Controller
A
9.9.9.9/32
Node C configures EPE for eBGP Peers
Node C allocates PeerNode SID to each peer
  Peer D Label 24002
  Peer E Label 24003
Node C installs PeerNode SIDs in FIB
The controller learns the BGP Peering SID’s and the external topology of the egress border router (option of Interface Characteristics)
BGP-LU
(RFC3107)
Controller can program the ingress node A to steer traffic to 9.9.9.9/32 via egress node C and AS3 (peer E) – NLRI, NHOP, Label, AS Path,
BGP policy
Peer D: label 24002
Peer E: label 24003
Segment Routing
Usecase : Egress Peer Engineering (EPE)
RP/0/RSP0/CPU0:router_C#show mpls forwarding labels 24002 24003
Local Outgoing Prefix Outgoing Next Hop Bytes
Label Label or ID Interface Switched
------ ----------- ------------------ ------------ --------------- ------------
24002 Unlabelled No ID Te0/3/0/0 99.3.19.9 0
24003 Unlabelled No ID Te0/1/0/0 99.3.9.9 0

## Slide 8
AS1
AS2
AS3
AS4
B
C
D
E
A
9.9.9.9/32
End Result : Ingress node pushes label stack on packets to 9.9.9.9/32
  {prefix-SID(egress node C), peerNode-SID(AS3 peer E)}
RP/0/RP0/CPU0:router_A#show cef 9.9.9.9/32
9.9.9.9/32, version 551, internal 0xa000001 0x0 (ptr 0x72cc6d08) [1], 0x0 (0x72c625fc), 0xa08 (0x72fa10f0)
Updated Sep 25 15:56:43.105
Prefix Len 32, traffic index 0, precedence n/a, priority 4
via 1.1.1.3, 3 dependencies, recursive [flags 0x6000]
path-idx 0 NHID 0x0 [0x73069570 0x0]
recursion-via-/32
next hop 1.1.1.3 via 16003/0/21
local label 24003
next hop 99.1.6.6/32 Te0/2/0/0 labels imposed {16003 24003}
peerNode-SID(AS3 peer E)
Prefix SID (egress Node C)
Payload
24003
16003
Payload
24003
Payload
Segment Routing
Usecase : Egress Peer Engineering (EPE)

## Slide 9
Usecase : Egress Peer Engineering (EPE)
Cache Farm : BW optimized peering
Y
Z
X
Cache
Cache Ctrl
MPLS
MPLS
YANG
Cache
MPLS
YANG
Cache
MPLS
MPLS
YANG
Cache
MPLS
YANG
RT1
RT2
B
A
172.0.1.1
172.0.2.1
WAN
172.1.X.X
RT3
RT4
loop0
200
101
102
103
loop0
202
loop0
202
loop0
204
a.a.a.0/24
IP dest a.a.a.x
101
200
IP dest a.a.a.x
101
To a.a.a.a/24
Use 101/200
SNMP:
BW utilization
Responce time
Paket drop
50%
93%
90%
IP dest a.a.a.x
BGP
BGP Local-RIB
IGP topology
Node-SID
EPE-SID
Cache topo
Telemetry
Cache RIB’s
172.0.2.1
Cache RIB’s
172.0.1.1
API
External influence

## Slide 10: IETF & standards
Architecture / Requirement drafts
draft-filsfils-spring-segment-routing-central-epe-02 (Cisco, FB, Yandex)
draft-filsfils-spring-segment-routing-msdc-00 (Cisco, Microsoft, Yandex)
Protocols extentions drafts
draft-keyupate-idr-bgp-prefix-sid-00 (Cisco)
draft-previdi-idr-bgpls-segment-routing-epe-01 (Cisco/Huwai)
draft-gredler-idr-bgplu-epe-01 (Juniper, Microsoft)
More information
www.segment-routing.net