## Slide 1: Distributed Prevention of DoS
Collaboration is key

## Slide 2: DoS Background
What is a Denial of Service attack?
An attempt to consume finite resources, exploit weaknesses in software design or implementation, or exploit lack of infrastructure capacity
Effects the availability and utility of computing and network resources
Attacks can be distributed for even more significant effect
  L7 attacks can be time consuming and involve high levels of manual process to ensure live users remain enabled
The collateral damage caused by an attack can be as bad, if not worse, than the attack itself
Attacks can be sustained for months

## Slide 3: What is Denial of Service?
The main point:
DoS is an Outage!
Slow starvation or volumetric (simple attacks are still hitting the headlines)

## Slide 4: DoS vs. DDoS?
One system is sending the traffic vs many systems are sending the traffic
Does it really matter?
…in what cases?

## Slide 5: Youtube

## Slide 6: Botnets & C&C Servers
Botnet – (Zombie Army) A collection of internet connected programs to perform certain tasks. The can be used to send spam or launch Ddos attacks.
C&C Servers - A botnet's originator (known as a bot herder or bot master) can control all these compromise programs to basically send bad traffic to a destination machine.
x2000 compromised hosts
Control signal
Notes: Botnet ( Robot Network)
C&C Servers – Command and Control servers

## Slide 7: Key Considerations For DDoS Protection
Scalability - How many resources may be brought to bear?
  Different levels of scale depending on positioning
Flexibility - What types of attacks may be mitigated & what techniques may be used?
Specialized Resources, Expertise & Focus - Who or what is analyzing the attacks, what resources are available, and who has the responsibility to coordinate the defense?
What is the full breadth of tools at your disposal?
Cost, not just monetary, but collateral damage (Brand damage)
Insurance or Loss?
Notes: Scalability – Is you detection and mitigation able to handle todays large attacks. Flexibility – Do you have the resources to understand the threat landscape.
Cost – cost !
Post forensics, storage,
Do I have the right tools, do I have too many…

## Slide 8: Contributing factors (what can you influence?)
Not patched Content Management Systems (CMSes)
Available reflectors (DNS, NTP, SSDP)
…with ability to amplify
More bandwidth available
Unpatched embedded devices – version control awareness
Misconfigured nodes
Vulnerable network elements i.e. CPEs
Weak security

## Slide 9: Reflective attacks
Attacks where the an unwilling intermediary is used to deliver the attack traffic
The attacker would normally send a packet with a forged/spoofed source IP address to the intermediary. The forged address is going to be the one of the target. The intermediary will deliver a response which will go to the target instead of the attacker
      Note to audience: think what protocols we can use for that?

## Slide 10: Reflector types
The ones that are of interest and provide reflections are:
  DNS
  NTP
  SNMP
  SSDP
  Other UDP???

## Slide 11: What is DNS resolution?
The process of mapping: www.a10networks. com => 191.236.103.221
…if the answer was cached

## Slide 12: What is DNS reflection?
What happens if an attacker forges the victim address as its source?
…the reflected traffic goes to the target server
… and what if hundreds of misconfigured open DNS resolvers are used?

## Slide 13: What is an amplification attack?
Asymmetric attack where the response is much larger than the original query

## Slide 14: Amplification types
The ones that are of interest and provide reflections are:
  DNS
  NTP
  SNMP
  SSDP
  What else?

## Slide 15: Reflection and Amplification

## Slide 16: What is a subdomain attack?
Direct or Reflection attack where the intermediary and victim spend cycles on nonsense
S: 191.236.103.221 D: 3.3.3.3
What is the IP for
Xyz1234.www.cisco.com?
S: 3.3.3.31 D: 91.236.103.221
NXDOMAIN
Response to legitimate protocol query

## Slide 17: NTP servers
Stratum servers
NTP queries
MONLIST command
  provides a list of clients that have time readings
What’s next?

## Slide 18: Solution?
DNS “Any” Request Filtering
  DNS “Any” requests can be used for a DDoS attack, since they occupy DNS server resources as the target server sends its many records to the requesters.
DNS Request Rate Limiting—by FQDN
  IP address – Limits the rate of queries from a given source.
  Requested domain name – Limits the rate of requests for the same domain name, from any sender, i.e. DNS Birthday attack
  Scope for FQDN rate limiting– Specify how many labels of the FQDN to consider together when applying the rate limit
  Maximum label length – Specify the maximum length for a given label within the FQDN, either at any suffix position or beginning at a specific suffix position.
DNS Request Rate Limiting—by Record Type
NXDomain Inspection and Rate Limiting

## Slide 19: Solution?
Label Inspection and Label Length Limiting
  Limit the label length of the FQDN after a number of suffixes
    Anything greater than suffix x will be limited
Ddos template dns tp-dns
fqdn-label-length 15 suffix 2
fqdn-label-length 10 suffix 3
www.googlegooglegoogle.com
test.www.google.com
randominvalidstring.google.com Does not pass label length 15 after suffix 2 check
alongstring.www.google.com Passes label length 15 after suffix 2 check,
but does not pass label length 10 after suffix 3 check

## Slide 20: Backscatter
What is backscatter and why do I care?
Traffic that is a by-product of the attack
Why is that interesting?
  It is important to distinguish between the actual attack traffic and unintended traffic sent by the victim
  Classify the attacker and victim differently

## Slide 21: Metrics
  Bandwidth (Kbps, Gbps)
  PPS
  QPS
  Storage
  CPU
  Application specific – usually latency
  Bad actors
  Victims
  Geo-temporal

## Slide 22: Good Internet citizenship

## Slide 23: Mitigations (Assumption – preaching to the converted)
Defend yourself
  Anycast
  Some form of IPS/DDoS mitigation gear – inline or asymmetric (service dependent or independent?)
  Overall network architecture
Defend the Internet
  Rate-limiting
  BCP38/140 (outbound filtering) source address validation
  Securely configured DNS, NTP and SNMP servers
  No open resolvers
Talk to other security professionals like yourself
Talk to vendors like A10 Networks

## Slide 24: Are you noticing the imbalance?
Defend yourself/your consumers
Defend the Internet
  Anycast (DNS)
  Some form of IPS/DDoS mitigation gear
  Rate-limiting
  BCP38/140 (outbound filtering) source address validation
  Securely configured authoritative DNS servers
  No open resolvers
  Lots of money
  Effective, scalable, faster to rollout
  Somewhat cheap
  More touch points, slower to rollout

## Slide 25: What’s the point I’m trying to make?
It’s not feasible to mitigate those attacks single handedly all of the time
Companies need to start including “defending the Internet from themselves” as a part of their budget – not only “defending themselves from the Internet”
We need cooperation amongst Service Providers and Security Vendors
  More can always be done, the war continues
  Shared intelligence is key

## Slide 26: In Summary (Assumption – this is part of your strategy already)
Evaluate the quick wins in your own network
  RFC 2827/BCP 38
  If possible filter all outgoing traffic and use proxy
  BCP 140: “Preventing Use of Recursive Nameservers in Reflector Attacks”
Collaborate with your peers to raise the bar collectively
Use high-scale, high performance mitigation infrastructure that defends your network and gives your consumers and peers levels of protection that keep pace and exceed the pace of change
Use dedicated DDoS platforms that understand the in-the-wild attacks
  Don’t exacerbate the situation, reduce the backscatter
Share the key metrics, KPIs and mitigation techniques (public forum?)

## Slide 27: THANK YOU
www.a10networks.com