## Slide 1: The $1,000 Internet Exchange
WARNING: Contains up-and-to-the-right charts
Remco van Mook
UKNOF, September 2015

## Slide 2: Before we start
This talk is about setting up not-for-profit, locally run, community-owned exchanges. Applicability in other scenarios may vary.
I’m not trying to push any vendor in particular – the examples given in this presentation are exactly that, examples.
There’s a big difference between setting up a new exchange from scratch and ‘parachuting in’ a satellite of an existing exchange
Your Mileage May Vary – local regulations can have a large impact!

## Slide 3: Back in 2001
I bought 2 switches for an IXP
16x 1GE GBIC
48x 10/100M UTP
4x 1000W power supply
Over $100K price tag
And after a lot of hard work, I got 20 paid customers and 1Gbps of traffic
There was no market to research!

## Slide 4: Back to 2015
There are plenty of IXPs around in all shapes and sizes
Market research is feasible
Higher speed Ethernet has been commoditized to pieces
Plenty of opportunity to learn from other people’s mistakes

## Slide 5: WHAT to do if you’re a new IXP
Market Research
Build a Community
Build a Platform
(Figure out the content providers)

## Slide 6: Market research
I’ll Tell You What You Want

## Slide 7: Market Research
Data from Euro-IX, covering 204 IXPs from all over the world
Data from July 2015 – hot off the press!
Omitted all IXPs with no current traffic data (approx. 50)
How much traffic should a starting IXP expect/design for?

## Slide 8: Global – ALL IXPs
Chart: 
20 Gbps
54th percentile

## Slide 9: NON-EUROPEAN IXPs
Chart: 
20 Gbps
69th percentile!

## Slide 10: Asiapac IXPs
Chart: 
| NPIX | IX-Australia / SA-IX | IX-Australia / QLD-IX | BDIX | PhopenIX | IX-Australia / WAIX | AMS-IX HK | IX-Australia / VIC-IX | MyIX | SGIX | JPIX Osaka | JPNAP Tokyo II | NIXI | TWIX | IX-Australia / NSW-IX | JPNAP Osaka | JPIX Tokyo | JPNAP Tokyo I | HKIX
Traffic | 593.92 | 703.488 | 4352 | 5120 | 7956.48 | 12113.92 | 12959.744 | 19148.8 | 22528 | 34836.48 | 34918.4 | 35287.04 | 46080 | 46632.96 | 56145.92 | 93276.16 | 344381.44 | 422328.32 | 497782.784
20 Gbps
42nd percentile!

## Slide 11: AfricaN IXPs
Chart: 
| Benin-IX | MOZ-IX | UIXP | IXPN | TIX - Tanzania | RINEX | CAIX | CINX | JINX | NAP Africa
Traffic | 51.2 | 409.6 | 942.08 | 1392.64 | 1413.12 | 1466.368 | 1587.2 | 6144 | 23859.2 | 46499.84
Chart: 
20 Gbps
80th percentile!

## Slide 12: EUROPEAN IXPs
Chart: 
20 Gbps
40th percentile!

## Slide 13: Market research conclusions
Traffic over 20Gbps is unlikely* for a startup
Design for an initial 15-20 customers
Initial revenue is low (if any)
* yes, there are exceptions, in places with highly developed local infrastructure and a lot of pressure from content providers, like FL-IX.

## Slide 14: Paradigm for new IXPs
First, grow to scale.
Then, scale to grow.

## Slide 15: Paradigms for helping new IXPs
Sponsor meeting rooms, not big gear
Facilitate LOCAL community building
Give them YOUR international contacts

## Slide 16: Build a community
We could spend a day on this..

## Slide 17: Guidelines
Be Inclusive
Be Pragmatic
(try to) Be Neutral

## Slide 18: Select your setup
The 4 S-es of IXPs:
Switches, Servers, Software and Space

## Slide 19: Requirements List
Capable of 20Gbps peak, 8Gbps average traffic
20-30 customer ports
10Mbps, 100Mbps, 1Gbps, multiple 1Gbps
Portal/website
Quarantine VLAN
Route server
Arpwatch
Central location with good connectivity options

## Slide 20: Bursts, Buffers and port speeds
TL;DR – Don’t offer 10Mbps or 100Mbps ports. You will drop traffic.
Slightly longer explanation:
  Switches are for forwarding traffic, not storing it
  Cheap switches have modest buffers for storing traffic
  Bursts of traffic from a 1G or 10G port towards a 10Mbps port will exhaust those
  If a switch is out of buffers, it will drop traffic
  Same thing goes for high port utilization!
Keep your port speed variance under 2 orders of magnitude!

## Slide 21: Switch options
 | Traffic | Ports | Est. price (USD) | Max Power (W) | Example
Entry | 0-20G | 24 10/100/1000T | $347 | 32 | HP V1910-24G
 |  | 4 1G SFP |  |  | 
Entry+ | 0-20G | 48 10/100/1000T | $480 | 60 | HP V1910-48G
 |  | 4 1G SFP |  |  | 
Basic | 0-40G | 24 10/100/1000T | $837 | 34 | HP 1950 24xGbE 2xSFP+
 |  | 2 1G/10G SFP+ |  |  | 
 |  | 2 1G/10G UTP |  |  | 
Basic+ | 0-40G | 48 10/100/1000T | $1,330 | 54 | HP 1950 48xGbE 2xSFP+
 |  | 2 1G/10G SFP+ |  |  | 
 |  | 2 1G/10G UTP |  |  | 
Fiber | 0-40G | 24 1000 SFP | $1,860 | 60 | HP 5130-24G-SFP-4SFP+ EI
 |  | 8 10/100/1000T |  |  | 
 |  | 4 1G/10G SFP+ |  |  | 
10G | 41-250G | 48 1G/10G SFP+ | $10,800 | 260 | HP 5900AF-48XG-4QSFP+
 |  | 4 40G QSFP+ |  |  | 

## Slide 22: SERVER OPTIONS
 | Est. price (USD) | Typical Power (W) | Example
Entry | $502 | 25 | Supermicro dual core Atom, 4GB, 2x1T disk
Basic | $1,539 | 120 | Dell R320, 4C Xeon, 16GB, 2x1T disk
Pimp | $6,225 | 250 | Dell R530, 12C Xeon, 64GB, 2xSSD, 4x2T disk

## Slide 23: SOFTWARE
A recent FreeBSD/Linux distribution (take your pick)
IXP Manager (https://github.com/inex/IXP-Manager/wiki)

## Slide 24: SPACE
A mutually convenient, EXISTING space with EXISTING connectivity options
Assure neutral cable entry, roof rights and so on
The IXP requirements are modest compared to the connecting equipment
There’s no such thing as a free lunch

## Slide 25: Business case
Technical Infrastructure Only!

## Slide 26
“Half a million dollars will always be missed.”

## Slide 27: assumptions
No organizational cost assumed – just the gear and keeping it running!
No import duties, taxes, VAT, license fees
It will take you 3 years to fill your ports
Power cost is $0.40/kWh
All datacenter costs are included in power cost
Revenue is projected based on port-months
1G port cost: $50 setup, $10 per month
10G port cost: $250 setup, $50 per month

## Slide 28: Setup 1
Single site, local customer equipment, unknown uptake, no 10G
Per site:
  1 “Entry” level switch: $350
  1 “Entry” level server: $502
  Cabling: $ 60
  Cable management: $ 40
  TOTAL $952
(20 customer ports, 1G copper, 67W power)
DONE

## Slide 29: SETUP 1
Investment: $952
Power draw: 67W
Customer ports: 20x1G
 | Port-months | Revenue | Investment | Power cost | Margin
Year 1 | 30 | $550 | $952 | $232 | -$634
Year 2 | 90 | $1,150 | $0 | $232 | $918
Year 3 | 180 | $2,300 | $0 | $232 | $2,068
Total |  | $4,000 | $952 | $695 | $2,353

## Slide 30: Setup 2
Expandable to 10Gbps / multiple Sites, local equipment
Per site:
  1 “Basic” level switch: $808
  1 “Entry” level server: $502
  Optics: $100
  Cabling: $100
  Cable management: $ 80
  TOTAL $1,590
(20 customer ports, 1G copper; 2 10Gbps ports, 69W power)

## Slide 31: SETUP 2
Investment: $1590
Power draw: 69W
Customer ports: 20x1G, 2x10G
 | Port-months 1G | Port-months 10G | Revenue | Investment | Power cost | Margin
Year 1 | 30 |  | $550 | $1,590 | $238 | -$1,278
Year 2 | 90 | 6 | $1,700 | $50 | $238 | $1,412
Year 3 | 180 | 18 | $3,200 | $50 | $238 | $2,912
Total |  |  | $5,450 | $1,690 | $715 | $3,045

## Slide 32: Setup 3
Expandable to 10Gbps / multiple Sites, mostly remote customer equipment
Per site:
  1 “Fiber” level switch: $1,860
  1 “Basic” level server: $1,539
  Optics: $ 300
  Cabling: $ 200
  Cable management: $ 80
  TOTAL $3,979
(20 customer ports 1G SMF; 8 1G copper; 4 10Gbps ports, 210W power)

## Slide 33: SETUP 3
Investment: $3,979
Power draw: 210W
Customer ports: 28x1G, 4x10G
 | Port-months 1G | Port-months 10G | Revenue | Investment | Power cost | Margin
Year 1 | 42 | 6 | $1,220 | $3,979 | $726 | -$3,485
Year 2 | 126 | 18 | $2,660 | $50 | $726 | $1,884
Year 3 | 252 | 36 | $5,070 | $50 | $726 | $4,244
Total |  |  | $8,950 | $4,129 | $2,177 | $2,644

## Slide 34: Setup 4
10G capable, local and remote customer connections, multiple sites
Per site:
  1 “10G” level switch: $10,800
  1 “Basic” level switch: $ 808
  1 “Pimp” level server: $ 6,225
  1 “Basic” level server: $ 1,539
  Optics: $ 1,300
  Cabling: $ 500
  Cable management: $ 250
  TOTAL $21,422
(44 customer ports 1G/10G SMF; 24 1G copper; 4 40Gbps ports, 744W power)

## Slide 35: SETUP 4
Investment: $21,422
Power draw: 744W
Customer ports: 36x1G, 36x10G
 | Port-months 1G | Port-months 10G | Revenue | Investment | Power cost | Margin
Year 1 | 54 | 54 | $5,940 | $21.422 | $2,571 | -$18,053
Year 2 | 162 | 162 | $12,420 | $450 | $2,571 | $9,399
Year 3 | 324 | 324 | $24,840 | $900 | $2,571 | $21,369
Total |  |  | $43,200 | $22,772 | $7,714 | $12,714

## Slide 36: DUMPSTER DIVING
10G capable, local and remote customer connections, multiple sites
Per site:
  1 Brocade MLX-16, 6 4x10GE cards, 2 24x100/1000 cards, 3,500W $0
  2 HP Proliant DL360 Gen5, Dual quad-core Xeon, 16GB, 500W each $0
  Optics: $0
  Cabling: $0
  Cable management: $0
  TOTAL $0
(24 customer ports 1G copper; 24 1G SMF; 24 10Gbps ports, 4,500W power)

## Slide 37: Dumpster Diving
Investment: $0
Power draw: 4,500W
Customer ports: 48x1G, 24x10G
 | Port-months 1G | Port-months 10G | Revenue | Investment | Service | Power cost | Margin
Year 1 | 72 | 36 | $4.620 | $500 | $25.000 | $15.552 | -$36.432
Year 2 | 216 | 108 | $9.660 | $500 | $25.000 | $15.552 | -$31.392
Year 3 | 432 | 216 | $19.320 | $500 | $25.000 | $15.552 | -$21.732
Total |  |  | $33.600 | $1.500 | $75.000 | $46.656 | -$89.556
FAILED

## Slide 38: Dumpster Diving
Investment: $0
Power draw: 4,500W
Customer ports: 48x1G, 24x10G
1G port cost: $250 setup, $50 per month
10G port cost: $500 setup, $200 per month
 | Port-months 1G | Port-months 10G | Revenue | Investment | Service | Power cost | Margin
Year 1 | 72 | 36 | $16.800 | $500 | $25.000 | $15.552 | -$24.252
Year 2 | 216 | 108 | $38.400 | $500 | $25.000 | $15.552 | -$2.652
Year 3 | 432 | 216 | $76.800 | $500 | $25.000 | $15.552 | $35.748
Total |  |  | $132.000 | $1.500 | $75.000 | $46.656 | $8.844

## Slide 39: A $100K switch setup
10G capable, local and remote customer connections, multiple sites
Per site:
  1 Big Vendor switch, 48x1G ports, 24x10G ports, 1,880W $99,470
  1 “Pimp” level server: $ 6,225
  1 “Basic” level server: $ 1,539
  Optics: $ 1,300
  Cabling: $ 500
  Cable management: $ 250
  TOTAL: $109,284
(24 customer ports 1G copper; 24 1G SMF; 24 10Gbps ports, 2,250W power)

## Slide 40: A $100K switch setup
Investment: $109,284
Power draw: 2,250W
Customer ports: 48x1G, 24x10G
 | Port-months 1G | Port-months 10G | Revenue | Investment | Service | Power cost | Margin
Year 1 | 72 | 36 | $4,620 | $109,284 | 0 | $7,776 | -$112,440
Year 2 | 216 | 108 | $9,660 | $450 | $24,500 | $7,776 | -$23,066
Year 3 | 432 | 216 | $19,320 | $900 | $24,500 | $7,776 | -$13,856
Total |  |  | $33.600 | $110.634 | $49,000 | $23,328 | -$149,362
FAILED

## Slide 41: A $100K switch setup
Investment: $109,284
Power draw: 2,250W
Customer ports: 48x1G, 24x10G
1G port cost: $300 setup, $65 per month
10G port cost: $1,500 setup, $275 per month
 | Port-months 1G | Port-months 10G | Revenue | Investment | Service | Power cost | Margin
Year 1 | 72 | 36 | $27,180 | $109,284 | 0 | $7,776 | -$89,880
Year 2 | 216 | 108 | $56,340 | $450 | $24,500 | $7,776 | $23,614
Year 3 | 432 | 216 | $112,680 | $900 | $24,500 | $7,776 | $79,504
Total |  |  | $196.200 | $110.634 | $49,000 | $23,328 | $13,238

## Slide 42: Figuring out the content side

## Slide 43: “Build it and we will come”*
Getting content providers adds enormous value to your IXP
But it comes at a price – which is a separate business case!
Typical requirements:
  free IP transit, free space & power
The upside:
  total IP transit cost for the community goes down
  Much improved user experience
*As long as it’s free (for us).

## Slide 44: Final remarks
You don’t need a huge budget
You DO need a solid community (inclusive, pragmatic, neutral)
Don’t be afraid to upgrade
Just about everything else is more important than the IXP hardware
If you want resilience, build more IXPs

## Slide 45: THANK YOU
Please come see me after the session or send e-mail!
With special thanks to Euro-IX for providing IX traffic data!
Remco van Mook
remco.vanmook@gmail.com