## Slide 1: Large BGP Communities
David Freedman
david.freedman@uk.clara.net
Claranet
Not so

## Slide 2: In brief.
BGP Communities Attribute (RFC 1997, Aug 1996)
  Designed for Internet
  Broad support in BGP implementations.
  32 bits, commonly expressed as “16-bit ASN : 16-bit VALUE”
  No space for ASN32 
BGP Extended Communities Attribute (RFC 4360, Feb 2006)
  Designed for L2/3VPN
  Limited support in BGP implementations, slow adoption in newcomers.
  64 bits, commonly expressed as “8/16-bit TYPE : 48/56-bit VALUE”
  The VALUE further expressed in subsequent extensions
    RFC5668 (Oct 2009) specifies an ASN32 TYPE
      subsequent value of “32-bit ASN : 16-bit VALUE” – Not ideal 

## Slide 3: So what other options for ASN32 users?
Flexible Communities Attribute (draft-lange-flexible-bgp-communities, Dec 2002)
  Complex expression, essentially “16-bit TYPE: 32-bit ASN : up-to-2040-bit VALUE”
  No consensus or implementations.
Wide Communities Attribute (draft-ietf-idr-wide-bgp-communities, Jul 2010)
  Extremely complex expression, “kitchen sink” approach, 16 bit LENGTH -> up to 65KB VALUE!
  No consensus or implementations.
Large Communities Attribute (draft-ietf-idr-large-community, Sep 2016)
  Simple (by comparison) expression, “32-bit ASN : 32-bit VALUE1 : 32-bit VALUE2”
  Consensus, (from both operators, and the IETF), implementations (both commercial and open source), and accepted to be published as an RFC (currently awaiting a number).

## Slide 4: Large BGP Community Examples
Canonical representation is $ME: $ACTION: $YOU
No namespace collisions or use of reserved ASNs
Enables operators to use 32-bit ASNs in $ME and $YOU values
RFC 1997 (Current) | Large BGP Communities | Action
65400:peer-as | 2914:65400:peer-as | Do not Advertise to peer-as in North America (NTT)
0:peer-as | 6667:0:peer-as | Do not Announce to Route Server peer-as (AMS-IX)
65520:nnn | 2914:65520:nnn | Lower Local Preference in Country nnn (NTT)
2914:410 | 2914:400:10 | Route Received From a Peering Partner (NTT)
2914:420 | 2914:400:20 | Route Received From a Customer (NTT)

## Slide 5: BGP Speaker Implementation Status
Visit http://largebgpcommunities.net/implementations/ for the Latest Status
Implementation | Software | Status | Details
Arista | EOS | Planned | Feature Requested BUG169446
Cisco | IOS XR | Planned | Engineering Release, rumour has Second Half 2017
cz.nic | BIRD | ✔ Done! | BIRD 1.6.3 (commit)
ExaBGP | ExaBGP | ✔ Done! | PR482
Juniper | Junos OS | Planned | Second Half 2017
MikroTik | RouterOS | Won’t Implement Until RFC | Feature Requested 2016090522001073
Nokia | SR OS | Planned | Third Quarter 2017
OpenBSD | OpenBGPD | ✔ Done! | OpenBSD 6.1 (commit)
OSRG | GoBGP | ✔ Done! | PR1094
rtbrick | Fullstack | Planned | February 2017
Quagga | Quagga | ✔ Done! | Patch Provided for 1.1.0 875
Ubiquiti Networks | EdgeOS | Planned | Internal Enhancement Requested
VyOS | VyOS | Requested | Feature Requested T143

## Slide 6: Tools and Ecosystem Implementation Status
Implementation | Software | Status | Details
DE-CIX | pbgpp | ✔ Done! | PR16
FreeBSD | tcpdump | ✔ Done! | PR213423
Marco d’Itri | zebra-dump-parser | ✔ Done! | PR3
OpenBSD | tcpdump | ✔ Done! | OpenBSD 6.1 (patch)
pmacct.net | pmacct | ✔ Done! | PR61
RIPE NCC | bgpdump | ✔ Done! | Issue 41
tcpdump.org | tcpdump | ✔ Done! | PR543 (commit)
Yoshiyuki Yamauchi | mrtparse | ✔ Done! | PR13
Wireshark | Dissector | ✔ Done! | 18172 (patch)
Visit http://largebgpcommunities.net/implementations/ for the Latest Status

## Slide 7: Large BGP Communities Beacon Prefixes
The following prefixes are announced with AS path 2914_15562$
  192.147.168.0/24 (looking glass)
  2001:67c:208c::/48 (looking glass)
  Large BGP Community: 15562:1:1
route-views>sh ip bgp 192.147.168.0
BGP routing table entry for 192.147.168.0/24, version 98399100
Paths: (39 available, best #30, table default)
Not advertised to any peer
Refresh Epoch 1
701 2914 15562
137.39.3.55 from 137.39.3.55 (137.39.3.55)
Origin IGP, localpref 100, valid, external
unknown transitive attribute: flag 0xE0 type 0x20 length 0xC
value 0000 3CCA 0000 0001 0000 0001
rx pathid: 0, tx pathid: 0
COLOCLUE1 11:06:17 from 94.142.247.3] (100/-) [AS15562i]
Type: BGP unicast univ
BGP.origin: IGP
BGP.as_path: 8283 2914 15562
BGP.next_hop: 94.142.247.3
BGP.med: 0
BGP.local_pref: 100
BGP.community: (2914,410) (2914,1206) (2914,2203) (8283,1) BGP.large_community: (15562, 1, 1)
Cisco IOS Output (Without Large BGP Communities Support)
BIRD Output (With Large BGP Communities Support)
Notes: Cisco IOS IPv6 propagation issue: https://mailarchive.ietf.org/arch/msg/idr/5S_zrTTJlfiPx-K1nxRqCGaM7us
Huawei route propagation issue: https://mailarchive.ietf.org/arch/msg/idr/aLnjhPEJGmf6LDJtVpPAM80T6xM

## Slide 8: Network Operator To Do List
The entire network ecosystem needs to support Large BGP Communities in order to provision, deploy and troubleshoot.
Ask your routing vendors and implementers for software support.
  Cisco: waiting for IOS-XR, but they have no plan for IOS(XE) and NX-OS.
  Juniper have started already, but only Junos OS is planned.
  Brocade and Huawei, no commitments, why??
Update your tools and provisioning software
Extend your routing policies, and openly publish this information
Train your technical staff

## Slide 9: Questions?
Visit http://LargeBGPCommunities.net/ for the Latest Info
Further questions -> myself or job@ntt.net