## Slide 1: Segment Routing (SR) Introduction and Tutorial
Adrian Farrel (afarrel@juniper.net)

## Slide 2: Take-Aways
Some historical context
What Segment Routing is trying to achieve
Basic building blocks
How it works in different SR environments
Minimal control plane
What you might do with SR and how you might deploy it
Do not expect:
  Too many details of how it works
  Every possible use case or future application
  A sales pitch (for the technology or for a vendor’s solution)

## Slide 3: Traffic engineering

## Slide 4: Purpose of TE
TE is concerned with performance optimization of operational networks
Control of how traffic flows through a network
Optimise:
  Amount of traffic the network carries
    Traffic is money
  Utilisation of resources
    Resources cost money
  The quality of service delivered
    Bandwidth, latency,…
    Reliability
Avoid specific issues:
  Planned maintenance
  Suspect resources
  Untrusted parts of the network

## Slide 5: Strict Paths in TE
Encode path information in the packet
  Packet header enumerates every node in the path
  No path information stored in the network
  Example: IPv4 with Strict Source Routing Option
    Not much used
Store path information in the network
  Packet header contains exactly one path identifier
  No further path information is encoded in the packet
  Example: RSVP-signaled MPLS

## Slide 6: Loose Paths in TE
Path is divided into segments
  Segment contains one or more router hops
Packet header lists each segment that the packet traverses
  But it does not necessarily enumerate every node
Network contains enough state to forward the packet through multi-node segments
Examples
  IPv4 Loose Source Routing Option
    Not much used
  IPv6 Routing Extension Header
    Not much used

## Slide 7: Segment Routing: A New Approach to TE
Path information is placed in the packet header
No control plane signaling or state
History
  Ideas first brought to the IETF in 2013
  Source Packet Routing in Networking (SPRING) working group
    Chartered October 2013
    500 members of the mailing list
  Only one RFC on Segment Routing so far
    RFC 7855 – Problem Statement
  Around 50 Internet-Drafts in progress
    Input from all the big vendors and a lot of the big operators

## Slide 8: Segment Routing Objectives
Deliver simple TE in packet networks
Leverage shortest path forwarding
Steer packets away from shortest paths for TE reasons
  Load balance in the network
  Create disjoint end-to-end paths
  Repair after failure
Achieve this without complexity in the network
  Remove signaling protocols and associated state
  Leverage existing forwarding paradigms (IP and MPLS)
  Leverage existing routing protocols (IGPs and BGP)

## Slide 9: Terminology
SR Domain - A collection of SR capable devices
  Roles: Ingress, transit, egress
SR Path - Can be different from least cost path
  Contains one or more SR Segments
SR Segment - Connects two points in SR domain
  Can traverse one or more router hops
  Is represented by a Segment Identifier (SID)
Segment Identifier (SID)
  Node-local or domain-wide (a.k.a., global) significance

## Slide 10: Pictorial Terminology
Ingress
Egress
Segment A
Segment B
Segment C
SR Path
SR Domain
IGP Shortest Path

## Slide 11: Basic Segment Types
Adjacency (single router hop)
  Represents an IGP adjacency
Prefix (one or more hops)
  Represents IGP least cost path to a prefix
Anycast (one or more hops)
  Represents IGP least cost path to a non-unique prefix
Binding
  Represents a tunnel (e.g., RSVP-signaled LSP)

## Slide 12: The SR TE Approach
SR segments define different types of path
  Some traverse one router hop
  Some traverse multiple router hops
SR header is inserted into each packet
  Lists each segment that a packet traverses
  But not necessarily each node
Network contains enough information to route a packet through a multi-hop segment
  This information is advertised by the IGP
    Or installed some other way
      Central controller with a southbound protocol
        Such as BGP-LU

## Slide 13: Three Encapsulation Environments
MPLS
  SR header is an MPLS label stack
  Each label in the stack represents a segment
IPv6
  SR Header is an IPv6 header with a Segment Routing Extension Header (SRH)
  SRH contains a list of IPv6 addresses
  Each IPv6 address represents a segment
MPLS-over-UDP
  MPLS SR label stack encapsulated in UDP-over-IP
  Routed through IPv4 or IPv6

## Slide 14: MPLS Forwarding

## Slide 15: Local SIDs / Global SIDs
SIDs are not labels
  But they are encoded (carried) in labels
Some SIDs have node-local significance
  Nodes allocate local SIDs and to local labels
  No need for domain-wide co-ordination
Some SIDs have domain-wide significance
  SIDs are allocated in a manner similar to that used for private IP (RFC 1918) addresses
  Domain-wide coordination required (using the IGP)
    Each node reserves a block of labels
      The SR Global Block (SRGB)
    Global label equals SRGB base value plus SID

## Slide 16: R1 to R4 : Adjacency Segments
R1
R2
R3
R7
R4
R5
R6
R1 IGP advertisement
Local label:81, link to R2
Local label:82, link to R4
R2 IGP advertisement
Local label:81, link to R1
Local label:82, link to R3
Local label:83, link to R5
R3 IGP advertisement
Local label:81, link to R2
Local label:82, link to R6
Local label:83, link to R7
R7 IGP advertisement
Local label:81, link to R3
Local label:82, link to R6
R4 IGP advertisement
Local label:81, link to R1
Local label:82, link to R5
R5 IGP advertisement
Local label:86, link to R2
Local label:87, link to R4
Local label:88, link to R6
R6 IGP advertisement
Local label:81, link to R3
Local label:82, link to R5
Local label:83, link to R7
82
82
87
pay load
83
82
82
87
pay load
82
87
pay load
pay load
87
pay load
82
83
82
82
87
pay load

## Slide 17: Any Node to R7: Using Prefix Segment
R1
R2
R3
R7
R4
R5
R6
R2 IGP advertisement
SRGB Base: 100
R3 IGP advertisement
SRGB Base: 500
R7 IGP advertisement
SRGB Base: 100
Prefix SID: 7
R5 IGP advertisement
SRGB Base: 200
R6 IGP advertisement
SRGB Base: 300
107
pay load
207
pay load
507
pay load
307
pay load
pay load
pay load
Shortest path to R7

## Slide 18: R1 to R4 via R7 : Prefix Segment
R1
R2
R3
R7
R4
R5
R6
R1 IGP advertisement
SRGB Base: 100
R2 IGP advertisement
SRGB Base: 100
R3 IGP advertisement
SRGB Base: 500
R7 IGP advertisement
SRGB Base: 300
Prefix SID: 7
R4 IGP advertisement
SRGB Base: 100
Prefix SID: 4
R5 IGP advertisement
SRGB Base: 200
R6 IGP advertisement
SRGB Base: 400
204
pay load
Shortest path to R7
Shortest path to R4
107
304
pay load
507
304
pay load
404
pay load
304
pay load
pay load

## Slide 19: IPv6 Forwarding

## Slide 20: Modes
Encapsulating mode
  SR ingress router encapsulates payload packet in an IPv6 header
  Source node includes a routing extension header between the IPv6 header and payload
  (This is what the specs say)
Simplified mode
  SR ingress inserts a routing extension header between the payload IPv6 header and payload data
  (This is what the prototypes implement)
In both cases:
  The routing extension header carries the stack of SIDs

## Slide 21: Segment Routing Header (SRH) : (1 of 6)
Source
2001:db8:0:1::1
SRv6 Ingress
2001:db8:0:1::2
SRv6 Egress
2001:db8:0:1::4
SRv6 Router
2001:db8:0:1::3
Destination
2001:db8:0:1::5
SR Domain
255
TCP Header/Payload
40
2001:db8:0:1::5
2001:db8:0:1::1
TCP
Destination Address
Source Address
Hop Limit
Next HDR
Payload Length
DSCP
Flow Label
Ver
IPv6
HEADER
TCP Header and Payload

## Slide 22
Segment Routing Header (SRH) : (2 of 6)
255
Destination Address
Source Address
Hop Limit
Next HDR
Payload Length
DSCP
Flow Label
Ver
IPv6
HEADER
Segment
Routing
Extension
Header
Payload
(TCP/IPv6)
HDR Type
56
Length
TCP
Next HDR
4
Seg Left
Flags
Last Entry
Segment 0
Tag
Segment 1
Segment 2
2001:db8:0:1::4
2001:db8:0:1::3
2001:db8:0:1::2
136
2001:db8:0:1::3
SRH
1
2
2001:db8:0:1::2
Source Address
2001:db8:0:1::1
Destination Address
2001:db8:0:1::5
Ver
DSCP
Flow Label
Payload Length 40
Hop Limit 255
Next HDR TCP
TCP Headed and Payload
Source
2001:db8:0:1::1
SRv6 Ingress
2001:db8:0:1::2
SRv6 Egress
2001:db8:0:1::4
SRv6 Router
2001:db8:0:1::3
Destination
2001:db8:0:1::5
SR Domain

## Slide 23
Segment Routing Header (SRH) : (3 of 6)
Source
2001:db8:0:1::1
SRv6 Ingress
2001:db8:0:1::2
SRv6 Egress
2001:db8:0:1::4
SRv6 Router
2001:db8:0:1::3
Destination
2001:db8:0:1::5
SR Domain
254
Destination Address
Source Address
Hop Limit
Next HDR
Payload Length
DSCP
Flow Label
Ver
IPv6
HEADER
Segment
Routing
Extension
Header
Payload
(TCP/IPv6)
HDR Type
56
Length
TCP
Next HDR
4
Seg Left
Flags
Last Entry
Segment 0
Tag
Segment 1
Segment 2
2001:db8:0:1::4
2001:db8:0:1::3
2001:db8:0:1::2
136
2001:db8:0:1::3
SRH
1
2
2001:db8:0:1::2
Source Address
2001:db8:0:1::1
Destination Address
2001:db8:0:1::5
Ver
DSCP
Flow Label
Payload Length 40
Hop Limit 255
Next HDR TCP
TCP Headed and Payload

## Slide 24
Segment Routing Header (SRH) : (4 of 6)
Source
2001:db8:0:1::1
SRv6 Ingress
2001:db8:0:1::2
SRv6 Egress
2001:db8:0:1::4
SRv6 Router
2001:db8:0:1::3
Destination
2001:db8:0:1::5
SR Domain
253
Destination Address
Source Address
Hop Limit
Next HDR
Payload Length
DSCP
Flow Label
Ver
IPv6
HEADER
Segment
Routing
Extension
Header
Payload
(TCP/IPv6)
HDR Type
56
Length
TCP
Next HDR
4
Seg Left
Flags
Last Entry
Segment 0
Tag
Segment 1
Segment 2
2001:db8:0:1::4
2001:db8:0:1::3
2001:db8:0:1::2
136
2001:db8:0:1::4
SRH
0
2
2001:db8:0:1::2
Source Address
2001:db8:0:1::1
Destination Address
2001:db8:0:1::5
Ver
DSCP
Flow Label
Payload Length 40
Hop Limit 255
Next HDR TCP
TCP Headed and Payload

## Slide 25
Segment Routing Header (SRH) : (5 of 6)
Source
2001:db8:0:1::1
SRv6 Ingress
2001:db8:0:1::2
SRv6 Egress
2001:db8:0:1::4
SRv6 Router
2001:db8:0:1::3
Destination
2001:db8:0:1::5
SR Domain
252
Destination Address
Source Address
Hop Limit
Next HDR
Payload Length
DSCP
Flow Label
Ver
IPv6
HEADER
Segment
Routing
Extension
Header
Payload
(TCP/IPv6)
HDR Type
56
Length
TCP
Next HDR
4
Seg Left
Flags
Last Entry
Segment 0
Tag
Segment 1
Segment 2
2001:db8:0:1::4
2001:db8:0:1::3
2001:db8:0:1::2
136
2001:db8:0:1::4
SRH
0
2
2001:db8:0:1::2
Source Address
2001:db8:0:1::1
Destination Address
2001:db8:0:1::5
Ver
DSCP
Flow Label
Payload Length 40
Hop Limit 255
Next HDR TCP
TCP Headed and Payload

## Slide 26
Segment Routing Header (SRH) : (6 of 6)
Source
2001:db8:0:1::1
SRv6 Ingress
2001:db8:0:1::2
SRv6 Egress
2001:db8:0:1::4
SRv6 Router
2001:db8:0:1::3
Destination
2001:db8:0:1::5
SR Domain
254
TCP Header/Payload
40
2001:db8:0:1::5
2001:db8:0:1::1
TCP
Destination Address
Source Address
Hop Limit
Next HDR
Payload Length
DSCP
Flow Label
Ver
IPv6
HEADER
TCP Header and Payload

## Slide 27: Advanced types of SID

## Slide 28: Multiple Points of Presence
An Anycast SID identifies a set of nodes via a non-unique prefix
Choice is made as an IGP shortest path first to the nearest member of the prefix set
May use ECMP
Helps survive failures and allows load balancing
Set of nodes are usually geographically close
Final segment to destination
First segment to any of three nodes
Second segment to any of two nodes

## Slide 29: Identifying SR Paths or Tunnels
Binding SIDs are bound to (i.e., identify) other SR paths or tunnels
This allows one SR path to include another SR path or a tunnel by reference
If Binding SID identifies another SR path then the SR forwarding operation is:
  Step beyond the Binding SID (decrement “Segments Left” or pop label)
  Insert additional labels for the identified SR path
If Binding SID identifies a tunnel then the forwarding operation is:
  Step beyond the Binding SID (decrement “Segments Left” or pop label)
  Encapsulate the packet and send it down the tunnel
Useful for scaling the SID stack at the packet ingress
Useful for traversing legacy networks

## Slide 30: Benefits and Drawbacks to SRv6
Segment routing is a very powerful concept
  Many use cases and many advantages
SRv6 header might be “quite large”
  16 bytes per SID
  This causes MTU issues
  Some silicon may face challenges and we want SR to be widely available
Standardization issues around IPv6 header options mean that a real specification is still some way away
  We need standards to ensure interoperability
Two SR approaches will be expensive
  Both have to be developed and tested even if you only buy one of them

## Slide 31: MPLS-SR-over-UDP

## Slide 32: Main Objectives
Get all of the Segment Routing function
Tunnel MPLS-SR over an IPv6 network
  E.g., connect two MPLS-SR data centers
Slot into a native IPv6 network
  Don’t need to use MPLS forwarding (some people don’t like it!)
  Phased introduction with non-SR routers
Simplify SRv6
  Address the scaling concerns (reduce header size)
  Avoid standardization controversy
  Use existing technologies and mechanisms
  Avoid expense/complexity of two SR solutions

## Slide 33: MPLS-SR-over-UDP
We already know how to carry MPLS over UDP (RFC 7510)
  Very useful for “bridging” MPLS islands (such as data centers)
New IETF work:
  draft-bryant-mpls-unified-ip-sr
  Carry MPLS-SR in UDP
  Very simple way to get all the SR function in an IPv6 network
  Get SR in IPv4 “for free”
Src = Sending SR capable node
Dst = Next SR capable node
Next protocol = UDP
Stack of SIDs exactly like it is an MPLS SR packet
Unchanged IP header and data
I.e. encapsulated packet
IP Header
MPLS SIDs Label Stack
IP Header
Payload
UDP Header
Src Port = Entropy
Dst Port = MPLS-in-UDP

## Slide 34: MPLS-SR-in-UDP Processing
IGP and control plane just like MPLS-SR
Source processing is just like MPLS-SR
  But encapsulate in UDP and IP to first router identified by first SID
Legacy transit nodes
  It is just an IP packet, so simply forward it
SR-capable transit nodes
  Process MPLS-SID stack as normal
  Encapsulate in UDP and IP and send to router identified by next SID
Final hop just strips outer header and forwards payload packet

## Slide 35: SR Control Plane

## Slide 36: SR IGPs
LSDB provides information required for CSPF computation
LSDB provides information required to create SR FIB entries
ISIS and OSPF have been enhanced to flood SR information throughout the IGP domain
SR requires an IGP and little else!

## Slide 37: Path Computation
SR ingress imposes label stack for the path
Someone has to work out the path to use
  It’s the normal TE problem
Performed on SR ingress router
Or on central controller
  PCE-based
Or imposed by operator as config

## Slide 38: FIB Creation (MPLS)
On each node, for each global SID
  Create a FIB entry that swaps the label (if required) and forwards through the IGP shortest path
On each node, for each local SID
  Create a FIB entry that pops a label and forwards through the correct link
LSDB provides information for FIB creation
(SRv6 forwarding is just IPv6 forwarding)

## Slide 39: Central Controller
Benefits
  Central control has global view of reserved bandwidth
    Not available at any other point in the network
  Facilitates analytics driven policy
    Controller receives telemetry
    Based on telemetry, controller alters policy
Risks
  Concentrated point of failure / congestion
  Potential performance bottle neck
  Risks mitigated by redundant controllers
    May require some form of synchronization
?

## Slide 40: Controller Protocol Options
Controller acquires LSDB
  Controller participates (passively) in IGP
  BGP-LS exports LSDB to controller
Controller sends segment list to ingress router
  PCEP
  BGP
  Programmable RPD
Controller imposes policy at ingress router
  What traffic to place on a SR path
  Flowspec additions to PCEP or BGP

## Slide 41: Some Use Cases for sR

## Slide 42: PCE With Segment Routing
PCC
LSDB
BGP-LS
ASBR
PE
PCE
3
Service Request
1
IGP
4
Push Path and Flowspec
5
Classify traffic Push SR SID stack
6
Forward Traffic
2

## Slide 43: Segment Routing in the Data Center
VM
Egress server
VM
Ingress server
Egress VM
Egress TOR
ECMP
MPLS SID Egress VM
Payload
MPLS SID Egress Server
MPLS SID Egress TOR
Transmitted packet “Loose hop” load balances over ECMP through spine switches
BGP-LU used to coordinate SIDs/labels in the network
Controller builds paths
Controller pushes paths
Controller programs egress server

## Slide 44: Routing Between Data Centers
draft-drake-bess-datacenter-gateway
draft-farrel-spring-sr-domain-interconnect
Gateways already advertise reachability to prefixes in the DC sites
Gateways already advertise Tunnel Encapsulation attributes
Two new features
  All gateways advertise on behalf of all other gateways
    Can now resolve dual homing paths
  New “SR tunnel” type : Binding SID
    Can now build end-to-end SR paths
Ingress DC Site
Egress DC Site
AS1
AS2
AS3
GW1
GW2
GW3
PE
PE
PE
PE
PE
ASBR
ASBR
ASBR
ASBR

## Slide 45: Use Case : Tunnelling SR Across a Non-SR Core
IPv6 Header
MPLS SIDs Label Stack
IPv6 Header
Payload
UDP Header
MPLS SIDs Label Stack
IPv6 Header
Payload
MPLS SIDs Label Stack
IPv6 Header
Payload
SR-in-UDP Tunnel
IP Network
SR Domain
SR Domain
Border Router
Border Router

## Slide 46: Use Case : SR in a Mixed Mode IP Network
IP Network
Legacy IP Router
SR-Capable Router Not In SID Stack
Native IP Forwarding
SR-Capable Router In SID Stack
SR Forwarding Path

## Slide 47: Conclusion

## Slide 48: Conclusion
SR moves state from the network to the packet
  Simplifies protocols
Some problems remain to be addressed
  OAM, Fast Reroute
Optimisations on early proposals are possible
Operational experience is required

## Slide 49
Questions?
afarrel@juniper.net