## Slide 1: DHCPv6 Operational Challenges
Tom Coffeen, IPv6 Evangelist
UKNOF January 2015

## Slide 2: Agenda
IPv6 is here! (Really, we mean it this time…)
DHCPv6 (i.e., Oh, look what IPv6’s dragged in!)
Stuff that’s (more or less) working
  Prefix delegation
  DHCPv6 fingerprinting
Stuff that’s (more or less) borked
  Failover
  Sanity in mixed autoconfig environments
Conclusion

## Slide 3: IPv4 is depleted…

## Slide 4: IPv6 is Here…

## Slide 5: IPv6 is…Over There…
UK Percentage of IPv6 Users
0.33%

## Slide 6: Some IPv6 Network Operator Measurements
Source: http://www.worldipv6launch.org/measurements/
63%
46%
51%
31%

## Slide 7: UK IPv6 Network Operator Measurements
Source: http://www.worldipv6launch.org/measurements/
Notes: We present measurements of network operator participants in World IPv6 Launch, based on data received from major website participants, as described in more detail below. We present a simple average of the data received, and list all networks with measurements from at least two sources, with a simple average above 0.1%. The network operator participants list includes some networks that measured above the threshold leading up to June 6th 2012, but for which we have insufficient measurement data to list here.
Akamai, Facebook, Google, LinkedIn, Yahoo

## Slide 8: DHCPv6 – What’s (More or Less) Working
DHCPv6 Prefix Delegation

## Slide 9: DHCPv6 Relay – ISC 4.3
Custom provisioning of DHCPv6 info for a particular client or client type or circuit ID
Classes can now be created based on DHCPv6 relay-provided options (rather than just client-provided options)

## Slide 10: DHCPv6 Relay – ISC 4.3

## Slide 11: DHCPv6 Relay – ISC 4.3

## Slide 12: DHCPv6
DHCPv6 Fingerprinting

## Slide 13: DHCPv6 Fingerprinting

## Slide 14: DHCPv6 Fingerprinting

## Slide 15: DHCPv6 Fingerprinting

## Slide 16: DHCPv6 Fingerprinting

## Slide 17: DHCPv6 Fingerprinting
IPv4 DHCP Option Request (Option 55)
DHCPv6 Option Request (Option 6)
≈
Typically, fewer options appear under Option 6 in a DHCPv6 SOLICIT
Other elements may be required to validate the device type or system
  Vendor Class field (where present)
  Timing how often the client sends a SOLICIT message
  In dual-stack environments, correlation with the IPv4 fingerprint
  The Client Identifier field in a DHCPv6 SOLICIT

## Slide 18: DHCPv6 Fingerprinting

## Slide 19: DHCPv6 Fingerprinting
SOLICIT, 1, 6, 23, 24, 8, and 3
=
=
  Fedora 17

## Slide 20: DHCPv6 Fingerprinting and BYOD
BYOD
or GTFO

## Slide 21: DHCPv6 Fingerprinting and BYOD
  Actionable data
    (Very basic) Security
      Is this type of device allowed on the network? (i.e., will it be allowed an IP address assignment via DHCP)
    Reporting
      What devices are connecting (or attempting to connect)?
  Passive -- no additional transactional overhead
    compare with nmap host OS detection

## Slide 22: DHCPv6 Fingerprints
Currently, 198 unique fingerprints for DHCP
None for DHCPv6
  Likely due to a lack of general IPv6 deployment in environments where fingerprinting is potentially most useful (i.e., enterprise/corporate networks)
  Thus, BYOD not generally a challenge for IPv6 (yet…)

## Slide 23: DHCPv6 – What’s Borked
DHCPv6 Failover

## Slide 24: DHCPv6 Failover
  Often repeated that it’s not needed (unless you’re doing PD)
    Many enterprises are insisting on it
      “We do it this way in IPv4 and we want to be able to do it the same way in IPv6…”
  Still no standards
  DHCPv6 Failover Requirements
    draft-ietf-dhc-dhcpv6-failover-requirements-07
  DHCPv6 Failover Design
    draft-ietf-dhc-dhcpv6-failover-design-04
  Still no proprietary implementation:
Notes: Not for reasons of session persistence

## Slide 25: DHCPv6 Failover
  Workarounds:
      Split prefixes
        Take a /64 and split it into two /65s, one per DHCPv6 server; e.g.:
        2001:db8:1:1:0000::/65
        2001:db8:1:1:8000::/65
        2001:db8:1:1::/64
            Use DHCPv6 Preference option (primary server at 255, secondary at 0)
            Drawback: Over time, uneven distribution of leases between servers
          Additional workarounds in RFC 6853 - DHCPv6 Redundancy Considerations
Notes: Not for reasons of session persistence

## Slide 26: DHCPv6 – What’s Borked
SLAAC/DHCPv6 Interaction

## Slide 27: DHCPv6 – Autoaddressing Review
  SLAAC
  Routers advertise prefixes that identify the subnet(s) associated with a link, while hosts generate an "interface identifier" that uniquely identifies an interface on a subnet. An address is formed by combining the two.

## Slide 28: DHCPv6 – Autoaddressing Review
  DHCPv6 (stateful)
    The Dynamic Host Configuration Protocol for IPv6 (DHCP) enables DHCP servers to pass configuration parameters such as IPv6 network addresses to IPv6 nodes. It offers the capability of automatic allocation of reusable network addresses and additional configuration flexibility.

## Slide 29: DHCPv6 – Autoaddressing Review
  DHCPv6 (stateless)
  Used by nodes to obtain configuration information, such as the addresses of DNS recursive name servers, that does not require the maintenance of any dynamic state for individual clients. A node that uses stateless DHCP must have obtained its IPv6 addresses through some other mechanism, typically stateless address autoconfiguration.

## Slide 30: DHCPv6 – Autoaddressing Review

## Slide 31: Autoaddressing – Renumbering scenarios
Address from
Autoaddressing
Method 1
Release/replace
Address’ from
Autoaddressing
Method 1
Address from
Autoaddressing
Method 1
Address from
Autoaddressing
Method 2
Address from
Autoaddressing
Method 1
Address from
Autoaddressing
Method 2
Release/replace
Retain/add

## Slide 32: DHCPv6/SLAAC Interaction
Host State | Input | Behavior
Host has not acquired any addresses | No RA | Some popular OSes acquire DHCPv6 addresses.
Host has not acquired any addresses | RA with M=0, O=1 | Some popular OSes acquire other info from DHCPv6 addresses. Others do so only if A=1.
Host has acquired address from DHCPv6 only | RA with M=0 | Some OSes release DHCPv6 immediately. Some release upon expiry.
Host has acquired address from SLAAC only | RA with M=1 | Some OSes release DHCPv6 immediately. Some release only if SLAAC address expires and can’t be refreshed.

## Slide 33: DHCPv6/SLAAC Interaction
Test, test, then test some more…

## Slide 34: Questions?
tcoffeen@infoblox.com
twitter: @ipv6tom

## Slide 35: References
ISC DHCP 4.3.0 is now online!
  https://www.isc.org/blogs/isc-dhcp-4-3-0-is-live/
Dynamic Host Configuration Protocol for IPv6 (DHCPv6), RFC 3315, IETF, Jul. 2003
Chatter on the Wire: A look at DHCPv6 traffic, by Eric Kollmann, Nov. 2010
  http://chatteronthewire.org/download/chatter-dhcpv6.pdf