## Slide 1: Anycast on a shoestring
Nat Morris - @natmorris
Thursday 22nd January 2015 – UKNOF30, London

## Slide 2: About me
Consultant, Esgob Ltd
Team leader, Cumulus
Board member, UKNOF
Based in West Wales
Aspiring lighthouse keeper

## Slide 3: Anycast 101
Simple concept:
  Announce the same address space from multiple locations
  Multiple paths in BGP, best one selected based on policy
Benefits:
  Increased reliability
  Load balancing
  Improved performance
  Localized impact of DoS attacks

## Slide 4: Summary
Fancied deploying a DNS Anycast service
Motivated by:
  Bill Woodcock, PCH
    SANOG8: “Best Practices in DNS Anycast Service-Provision”
  Dave Knight, ICANN (now Dyn)
    RIPE64: “Dense Anycast Deployment of DNS Authority Servers”
Gain more experience automating distributed environments.

## Slide 5: Thoughts
Can I do it without spending too much?
What to offer?
  Initially only secondary DNS
  IPv4 + IPv6
  Free service - no SLA, no Revenue
Does Claire need to find out?
    Must be sub $1000/yr running cost

## Slide 6: Requirements
Separation from existing management network - AS30746
Had spare PI /24 + /48
Applied for new ASN - got AS60564
Need highly automated framework
Wanted to play with new tools
Open source everything
  https://github.com/esgob

## Slide 7: Network
Each anycast node:
  Announce /24 + /48 via BGP
  Static default route to the provider (accept no routes)
Node 1
AS60564
Upstream A ASxxx
BGP Announce
193.47.147.0/24
2001:067c:1b43::/48
Node 2
AS60564
Upstream B ASxxx
BGP Announce
193.47.147.0/24
2001:067c:1b43::/48
Node 3
AS60564
Upstream C ASxxx
BGP Announce
193.47.147.0/24
2001:067c:1b43::/48
Node 4
AS60564
Upstream D ASxxx
BGP Announce
193.47.147.0/24
2001:067c:1b43::/48
/30 + /64

## Slide 8: Network
All management traffic inside OpenVPN
  Additional RFC1918 loopback per node
  No need for TSIG from AXFR to anycast nodes
  Protects beanstalk traffic, API, collectd, zone transfers
Node 1
AS60564
Upstream A ASxxx
Node 2
AS60564
Upstream B ASxxx
Node 3
AS60564
Upstream C ASxxx
Node 4
AS60564
Upstream D ASxxx
Management GW

## Slide 9: DNS zone transfers
AS30746
axfr.esgob.com
Anycast nodes
ns1.esgob.com
Zone transfer
Master servers operated by others
ns0.esgob.co.uk
(only my zones)
Zone transfer
AS60564
Supports notifies from masters
Zone transfer

## Slide 10: Store everything in JSON
Data stored in RethinkDB
  Distributed JSON document database
  Free form, easy to add attributes

## Slide 11: Application design
REST API - Python + Flask framework
cronjob + rsync free zone
Beanstalk - Message queue
  Add/change/removal of zones via API triggers job to be added to queue
  Daemons on AXFR + Anycast nodes wait for jobs
  New zones live on all nodes with 5 seconds
RethinkDB
REST
API
Python + Flask
Website
Python + Flask
Scripts / Daemons
BeanstalkD
job
job
Config files
Jinja2 templates
Redis
Users

## Slide 12: Where to host the anycast nodes?
Can’t cost too much each month
  Ruled out renting co-lo / dedicated servers
Need a wide reach
Virtual machines
  Swap with friends?
Low cost hardware

## Slide 13: Mythic Beasts
UK clueful hosting company
£7/month = £84/yr = $141/yr
  512mb RAM, 1 CPU, 10gb HDD, 75gb BW
Bought a VM, opened a support ticket
  BGP not listed on the website.
  Me: “I have a /24 + /48 of PI, can you set me up a BGP session? see AS60564 + AS-ESGOB-ANYCAST”
  Them: “Peer with these IPs, sessions are ready!”
Too easy!

## Slide 14: Quest to find more friendly VM hosts
LowEndBox.com
  Blog / adverts for VM providers, all < $10 month
  Usually OpenVZ based
  Need KVM/XEN/VMWare to support Quagga/BIRD
LowEndTalk.com
  Message board, various small scale VM hosts
Google
  “vps bgp session”

## Slide 15: Anynode in Detroit
Listing on LowEndTalk
  Asked if they could support BGP.
  Yes on any VPS!!
$80/yr, 1 CPU, 512mb, 40gb HDD, 500gb BW

## Slide 16: Indian bargin!
LeapSwitch, based in Pune, India.
  New VPS host, saw an offer advertised
$120/yr, 1gb RAM, 20gb HDD, 500gb BW

## Slide 17: Growing - Oct 2013
Up to 4 VMs
  London A (on existing KVM server)
  London B
  Detroit
  India
Spinning up VM taking about 10 minutes
  Add JSON entry into RethinkDB
  Install Debian
  Install Puppet (Collectd, BIND, Quagga, custom daemons etc)
  Done
  Pub!

## Slide 18: Friends - Oct 2013
Offers to host VMs for free from:
  Edinburgh @ Fluency
  Boston @ TorwardEx
One swap:
  Bremen, Germany @ Fremaks
Quickly up to 7 nodes after 1 month

## Slide 19: Friends
“We can host something, but not a VM”
Various issues:
  Network engineers didn’t have access to VM hosts
  No VM infrastructure at all
  All VMs routed by hypervisor, can’t bridge to BGP routers
Solution…
  Raspberry PI, $35
  512mb / 16gb SD Card
  800mhz (overclocked)

## Slide 20: Raspberry Pi
Sent RPI to Belfast – David Farrell @ Tibus
Ran NSD3 great, ~200qps
Adding / removing zones with NSD3 required service restart ☹
Swapped to PowerDNS, testing went ok
pdns_control segfault’ing on ARM
Gave in and moved to BIND

## Slide 21: Time to peer - Jan 2014
Offer of a node at SFMIX from Matt Peterson
San Francisco based IXP
Couldn’t turn this down.
Zero U install
Needed 2 NICs, IX + OOB
  FitPC2i - perfect ☺
  Atom 1.6ghz, 1gb RAM, 16gb SSD
  $150 on eBay
Peering with:
  HE.net, ISC, Unwired, PCH
  Layer42, Lookout, DigitalOcean

## Slide 22: Pi problems
Puppet slow + loading zones taking too long
More offers to host h/w nodes
  Manchester, Andy Davidson @ Allegro
Gigabyte BRIX
  Quad Core, 1.8ghz, 4gb RAM, 30gb MSATA
Swap out Belfast Pi

## Slide 23: Still growing today
12 nodes live, 6 in build
As of 3rd Nov 2014

## Slide 24: Fun along the way
First BGP customer for some of the VM hosts:
  Assisted educating them…
  Prefer transit routes over customers, eek
  No BGP filters / route-maps or prefix lists - Ahhhhh!
Some hosts don’t have communities
  Helping people get those implemented
RIPE Atlas
  Scheduled measurements to look at latency + CHAOS id.server
RIPEstat
  Using the REST API to query visibility of a /48 anchor from each instance, 15mins to get working.

## Slide 25: Market for VMs with BGP sessions

## Slide 26: Discoveries
Easy to find budget anycasters
  Webhost forums / LowEndTalk / bgp.he.net
“Interesting” deployment methods
  Shared /24
    Dedicated IP, custom fwd/rev DNS, slaved zones
  Hosted /24
    Same as above but customer provides /24 to announce
  Shared /24, /32 tunneled
    Dedicated IP, tunneled by anycaster to customer via GRE
  Single /24
    Anycaster only has one /24, website + mail + mgmt in same space. DNS answered at edge, other IPs tunneled to another VM/dedicated box.

## Slide 27: Discoveries
Not all budget DNS hosting companies host every zone at the edge
  Some host zones centrally and cache at the edge
Some tunnel all DNS traffic back to a location:
  Looks like anycast
  Poor DNS performance
  GRE from edge to a single auth server
  Selling /32 GRE tunnels to customers!

## Slide 28: Not just DNS?
Simple HTTP/HTTPS service to assist debugging
  local.esgob.com
  local4.esgob.com / local6.esgob.com
Returns JSON via lighttpd on each node
nat@enw:~ $ curl http://local.esgob.com
{
"city": "London",
"country": "England",
"countryiso": "gb",
"flag": "england",
"locationdisplay": "England, London, B",
"ref": "ql7f823b"
}

## Slide 29: What next?
Keep honest – host every zone at the edge
Finish web interface
Make the Github repos consumable:
  Produce install instructions
  Getting started guide
Support: Multi master, TSIG inbound
Mix of routing and DNS daemons
  configurable per node via JSON in RethinkDB
  BIND, NSD4, KNOT, Quagga, BIRD + ExaBGP
Looking for friendly hosts:
  Europe, Africa, India, Asia, South America, anywhere!

## Slide 30: As of today...
Currently costing just under $480/yr - Claire compliant!

## Slide 31: Take aways
Low barrier to entry - VM with BGP full table $40/yr
Don’t become part of the problem
  Ensure your customers aren’t hijacking prefixes
  Always use IRR prefix lists on cust BGP sessions
Using anycast can improve service delivery to your customers
Automate all things!
Have fun and share your experiences

## Slide 32: Questions?
https://noc.esgob.com
@esgobltd
https://nat.ms
@natmorris