## Slide 1: The Top 5 Things You need to keep in Mind when preparing your IPv6 Addressing Plan
Tom Coffeen, Infoblox
Veronika McKillop, UK IPv6 Council
UKNOF 35, Glasgow
9 September 2016

## Slide 2: Abstract
One of the first steps in an IPv6 deployment project is to obtain an IPv6 prefix for your organisation and create an IPv6 addressing plan. Thanks to the growth of IPv6 deployment globally, there is more experience and new best practices are created that can assist with such a task.
This session will present the top 5 major points you need to consider and focus on when writing your addressing plan. The aim is to provide the attendees with guidance and suggestions.

## Slide 3: Agenda
Obtaining an IPv6 Prefix
Subnetting your IPv6 allocation and assignments
Working with standard IPv6 subnet sizes
“Nibble boundary” rules
ISP approach to addressing CPEs
Examples of IPv6 addressing plans

## Slide 4: 1. Obtaining an IPv6 prefix
Notes: It comes as point no.2, as first we have think about how large prefix we need to obtain and then we go to obtain it from our LIR/RIR.
[Question] Or does it make a sense to put it in as no. 1?

## Slide 5: Obtaining an IPv6 Prefix (1)
ISPs obtain a prefix for:
  themselves and
  to sub-allocate it to their customers (as an LIR)
ISPs request their prefix from the RIR
  How large allocation do you need?
    /29 is now typical (or larger)
  What size of prefixes will you hand out to your customers?
    Typical /48 per customer site
    For BB subs the current best-practise is /56
Notes: $ whois -h whois.ripe.net 2003::/19
inet6num: 2003::/19
netname: DE-TELEKOM-20050113
country: DE
org: ORG-DTA2-RIPE
[...]
$ whois -h whois.ripe.net 2a01:c000::/19
inet6num: 2a01:c000::/19
netname: FR-TELECOM-20051230
country: FR
org: ORG-FT2-RIPE
[...]
$ whois -h whois.ripe.net 2a08::/19
inet6num: 2a08::/19
netname: UK-MOD-20160701
country: GB
org: ORG-DMoD1-RIPE
[...]
Followed by:
$ whois -h whois.ripe.net 2001:2000::/20
inet6num: 2001:2000::/20
netname: SE-TELIAEU-20040510
country: EU
org: ORG-TA45-RIPE
[...]
$ whois -h whois.ripe.net 2a01:2000::/20
inet6num: 2a01:2000::/20
netname: IT-INTERBUSINESS-20060516
country: IT
org: ORG-IA34-RIPE
[...]

## Slide 6: Obtaining an IPv6 Prefix (2)
The Enterprise view
  Most likely not much experience dealing with RIRs
  The multihoming requirement (and challenge)
  Selecting Provider Independent vs. Provider Assigned
  Let go of an unnecessary “conservation” mindset.
    An enterprise can and should get a “right-sized” allocation
Notes: $ whois -h whois.ripe.net 2003::/19
inet6num: 2003::/19
netname: DE-TELEKOM-20050113
country: DE
org: ORG-DTA2-RIPE
[...]
$ whois -h whois.ripe.net 2a01:c000::/19
inet6num: 2a01:c000::/19
netname: FR-TELECOM-20051230
country: FR
org: ORG-FT2-RIPE
[...]
$ whois -h whois.ripe.net 2a08::/19
inet6num: 2a08::/19
netname: UK-MOD-20160701
country: GB
org: ORG-DMoD1-RIPE
[...]
Followed by:
$ whois -h whois.ripe.net 2001:2000::/20
inet6num: 2001:2000::/20
netname: SE-TELIAEU-20040510
country: EU
org: ORG-TA45-RIPE
[...]
$ whois -h whois.ripe.net 2a01:2000::/20
inet6num: 2a01:2000::/20
netname: IT-INTERBUSINESS-20060516
country: IT
org: ORG-IA34-RIPE
[...]

## Slide 7: Obtaining an IPv6 Prefix (3)
Out-of-region announcements
  No actual RIR policy that prohibits this
  Some organizations running networks in other regions will want to obtain a regional IPv6 allocation as a precaution
  Check with upstream ISP the accepted prefix length announcements
    Usually /48 is ok (for now)
Notes: $ whois -h whois.ripe.net 2003::/19
inet6num: 2003::/19
netname: DE-TELEKOM-20050113
country: DE
org: ORG-DTA2-RIPE
[...]
$ whois -h whois.ripe.net 2a01:c000::/19
inet6num: 2a01:c000::/19
netname: FR-TELECOM-20051230
country: FR
org: ORG-FT2-RIPE
[...]
$ whois -h whois.ripe.net 2a08::/19
inet6num: 2a08::/19
netname: UK-MOD-20160701
country: GB
org: ORG-DMoD1-RIPE
[...]
Followed by:
$ whois -h whois.ripe.net 2001:2000::/20
inet6num: 2001:2000::/20
netname: SE-TELIAEU-20040510
country: EU
org: ORG-TA45-RIPE
[...]
$ whois -h whois.ripe.net 2a01:2000::/20
inet6num: 2a01:2000::/20
netname: IT-INTERBUSINESS-20060516
country: IT
org: ORG-IA34-RIPE
[...]

## Slide 8: Examples of IPv6 Allocations
Largest allocations
  In the RIPE region*:
    /19 Deustche Telecom, France Telecom, UK MoD
    /20 Telia Sonera, Telecom Italia
  In the ARIN region:
    Service providers:
      /20 Comcast
    Enterprises:
      /24 US Veterans Administration
*Source: RIPE NCC database https://apps.db.ripe.net/search/
Notes: $ whois -h whois.ripe.net 2003::/19
inet6num: 2003::/19
netname: DE-TELEKOM-20050113
country: DE
org: ORG-DTA2-RIPE
[...]
$ whois -h whois.ripe.net 2a01:c000::/19
inet6num: 2a01:c000::/19
netname: FR-TELECOM-20051230
country: FR
org: ORG-FT2-RIPE
[...]
$ whois -h whois.ripe.net 2a08::/19
inet6num: 2a08::/19
netname: UK-MOD-20160701
country: GB
org: ORG-DMoD1-RIPE
[...]
Followed by:
$ whois -h whois.ripe.net 2001:2000::/20
inet6num: 2001:2000::/20
netname: SE-TELIAEU-20040510
country: EU
org: ORG-TA45-RIPE
[...]
$ whois -h whois.ripe.net 2a01:2000::/20
inet6num: 2a01:2000::/20
netname: IT-INTERBUSINESS-20060516
country: IT
org: ORG-IA34-RIPE
[...]

## Slide 9
2. SUBNETTING YOUR IPv6 Allocation AND ASSIGNMENTS

## Slide 10: What to consider when subnetting your IPv6 allocation
Be sure to request a large enough allocation at the outset
  Rule of thumb: /48 per site (for an Enterprise)
  /56 per BB CPE (for an ISP)
Don’t fall into the IPv4 mindset
  No subnetting beyond the /64
Prefix | Subnet groups per /32 | /48 subnets per group
/32 | 1 | 65,536
/36 | 16 | 4,096
/40 | 256 | 256
/44 | 4,096 | 16
/48 | 65,536 | 1
Notes: [VMcK : could add here another slide] ?

## Slide 11
3. WORKING WITH STANDARD IPv6 Subnet SIZES

## Slide 12: The “best size” for an IPv6 subnet?
Enterprise – site allocation size: /48
Point-to-point links and LAN interfaces: /64 or /127
  Subnets smaller than /64 have appeared in some deployments for very specific use cases
Loopbacks
  One /64 and all loopbacks from it
  Many /64s and keeping the Interface ID the same
  In either case, /128 per loopback
    (equivalent to /32 in IPv4)
LO1
2001:db8:2112:3::1/128
WAN1
2001:db8:2112:2::2/64
WAN2
2001:db8:2112:2::3/64
LAN1
2001:db8:2112:1::1/64

## Slide 13
4. Nibble boundary rule

## Slide 14: “Nibble boundary” benefits
2001:db8:1234:5678::/64
  Nibble = 4 bits = 1 HEX character
Keep the addressing plan tidy
Easy to recognise what portion of prefix is assigned and what we are working with
Assists hierarchy of the plan, easier summarisation and security policies

## Slide 15: Nibble boundaries when subnetting within a site
Prefix | Subnet groups per /48 | /64 subnets per group
/48 | 1 | 65,536
/52 | 16 | 4,096
/56 | 256 | 256
/60 | 4,096 | 16
/64 | 65,536 | 1

## Slide 16: Nibbles make IPv6 prefixes more legible
Subnet bits a multiple of 4 | 
Prefix: | 2001:db8:1::/48
Range: | 2001:db8:1:0000:0000:0000:0000:0000 2001:db8:1:ffff:ffff:ffff:ffff:ffff
Subnet bits not a multiple of 4 | 
Prefix: | 2001:db8:1::/49
Range: | 2001:db8:1:0000:0000:0000:0000:0000 2001:db8:1:7fff:ffff:ffff:ffff:ffff 2001:db8:1:8000:0000:0000:0000:0000 2001:db8:1:ffff:ffff:ffff:ffff:ffff

## Slide 17: Mapping locations or functions into IPv6 address prefixes using nibbles
2001:db8:1:LXXX::[/52 - /64]
Location (16 sites)
2001:db8:1:[0-f]nnn::/52
Interface subnets (4096 per location)
2001:db8:1:n[0-f][0-f][0-f]::/64
Prefix | Assignment
2001:db8:1:0000::/52 | Reserved
2001:db8:1:1000::/52 | Building 1
2001:db8:1:2000::/52 | Building 2
… | …
2001:db8:1:f000::/52 | [Location 16]
Prefix | Assignment
2001:db8:1:1000::/64 | Reserved
2001:db8:1:1001::/64 | VLAN1
2001:db8:1:1002::/64 | VLAN2
… | …
2001:db8:1:1fff::/64 | [Subnet 4096]
CAUTION! It’s possible to overdo this approach…
  There is a trade-off between the operational benefits of the approach and the flexibility of your addressing plan for growth and extensibility

## Slide 18
5. CPE addressing

## Slide 19: ISP approach to CPE addressing
We started with /48 (RFC 3177)
  Made obsolete by RFC 6177
Now /56 per CPE is the best practise
But the IETF Homenet working group is reconsidering /48
  Prefix colouring (?)
What do you think of SP Wi-fi and /64 per host?
Notes: RFC 3177: This document provides recommendations to the addressing registries (APNIC, ARIN and RIPE-NCC) on policies for assigning IPv6 address blocks to end sites. In particular, it recommends the assignment of /48 in the general case, /64 when it is known that one and only one subnet is needed and /128 when it is absolutely known that one and only one device is connecting.
RFC 6177: RFC 3177 argued that in IPv6, end sites should be assigned /48 blocks in most cases. The Regional Internet Registries (RIRs) adopted that recommendation in 2002, but began reconsidering the policy in 2005. This document obsoletes the RFC 3177 recommendations on the assignment of IPv6 address space to end sites. The exact choice of how much address space to assign end sites is an issue for the operational community. The IETF's role in this case is limited to providing guidance on IPv6 architectural and operational considerations. This document reviews the architectural and operational considerations of end site assignments as well as the motivations behind the original recommendations in RFC 3177. Moreover, this document clarifies that a one-size-fits-all recommendation of /48 is not nuanced enough for the broad range of end sites and is no longer recommended as a single default.

## Slide 20: Other Influences in the Industry
IETF Homenet & ISP’s IPv6 Addressing
  This WG focuses on supporting next-generation services on unmanaged home networks
    In the center of their work is IPv6
  Multiple ISP connections to the home
    Example: broadband, VPN router, smart meters, home security etc.
    Terminated at a CPE (6rd, DHCPv6-PD, MAP, static IPv6 etc.)
  Not really impacting the ISP IPv6 addressing as it’s behind the CPE
    Rather realize the potential of prefix coloring & IPv6 Segment Routing
  Homenet presentation @ UKNOF 27 (January 2014)
IETF v6 Ops & Unique IPv6 Prefix Per Host
  Large scale environments with the need to assign IPv6-prefix per host (E.g. SP Wi-Fi)
  Advantages:
    Monitoring the prefix instead of IPv6 address
    Host isolation (prefix has an Off-link flag set), limitation in ND communication
  Think about it from the perspective of the IPv6 prefix allocation from your RIR/LIR
  How many /64 are you going to need?
    This will impact the required allocation size
  presentation @ UKNOF 33 (January 2016)
/56
/60
/48
© V.McKillop, 2015
For Your
Reference
Notes: [BRIEF] Picking the right size of prefix to delegate for Homenet considerations
[BRIEF] Possibility and potential impact of /64 per host (draft-ietf-v6ops-unique-ipv6-prefix-per-host)

## Slide 21
Examples of Addressing plans

## Slide 22: A large enterprise plan summary
5 RIRs with IPv6 – 5 /32s (one per RIR)
Region gets a /36 (15 /36s held in reserve)
Core has core networks and external DMZs; /40s
Countries have sites: i.e., grouping of buildings or single buildings at the same location; /40s
Sites are /56s of /48s for applications; i.e., DHCP client(s), customer/printing/etc. environments
Applications are /48s and they contain /64s (subnets)

## Slide 23: ISP addressing plan (1)

## Slide 24: ISP addressing plan (2)

## Slide 25: ISP addressing plan (3)

## Slide 26
Summary & Resources

## Slide 27: Summary
Obtaining an IPv6 Prefix
  ISP vs. Enterprise; PI vs. PA
Subnetting your IPv6 allocation and assignments
  The right size for your organization’s initial allocation
Working with standard IPv6 subnet sizes
  /64s, /48s, /128s, (possibly also /127s)
“Nibble boundary” rules
  Legibility of unique prefixes
ISP approach to addressing CPEs
  /56 vs. /48
Examples of IPv6 addressing plans
  Enterprise
  ISP

## Slide 28: Resources
IPv6 Address Planning
  Tom Coffeen, O’Reilly (http://shop.oreilly.com/product/0636920033622.do)
How to write an IPv6 Addressing Plan
  Veronika McKillop, Cisco Live breakout session BRKRST-2267
  Recording: www.ciscolive.com/online (register for free and search for the session code)
Create an Addressing Plan
  RIPE NCC https://www.ripe.net/publications/ipv6-info-centre/deployment-planning/create-an-addressing-plan