Merchant Silicon – Are switches… routers ?
Merchant Silicon – Are switches… routers ?
Alex Nichol, Arista Technical lead

---
Arista Overview
Arista Overview
Company founded 2004, first product launch 2008
- Public trading company, IPO June 2014- $5B market cap
- 5 Million+ 10Gbe ports shipped, 3000 + customers
- Leading the GbE to 10GbE data center transition
- 2nd in Data Center switching/routing based on Market Share
Single OS
Fully programmable
LINX OS
Full Custom
Merchant Silicon
YoY market Share growth
Crehan Research Inc – Q2 2016

---
What do we mean by Merchant silicon ?
What do we mean by Merchant silicon ?
ASIC Design approach
  - Top down approach
  - Focusing on the silicon functionality rather performance
  - Designed around pre-defined building block and libraries
  - Designed for functionality, not optimized for performance and cost
Full Custom Design
  - Bottom up approach
  - Designed at the component level,
  - Allowing optimal clock rate/performance, lowest power, highest density
  - Delivers the optimal performance but can be costly process
  - Speed time cycle and reduce cost
    - Development done by third-party silicon manufactures not networking vendors
    - Broadcom, Intel, Dune, Fulcrum etc
  - Hence the term Merchant silicon

---
Merchant Silicon – Design trade-offs
Merchant Silicon – Design trade-offs
Designing merchant silicon – multi-dimension challenge trade-off within a fixed footprint
    - Pins 10G (for 10G/40G support) or 25G (for 10G/25G/50G/100G) – defining the throughput requirements
    - Layer 2/3 forwarding logic, tunnel support (GRE. MPLS, VXLAN etc)
    - Number of Pins on the silicon, defining the number ports, off- chip resources and fabric links if it’s a multi-chip fabric design
    - Table sizes, MAC table (Exact match table), ARP tables (LEM), LPM for Layer 3 tables
SERDES (Ports)
Buffer Memory (~12MB)
L2 (MAC) hash table
L3 (LPM) m-trie
TCAM (ACL etc.)
Forwarding logic

---
Merchant Silicon Landscape, its Evolution
Merchant Silicon Landscape, its Evolution
T+
T2
T2+
TH
Petra
Arad
Jericho
8x10G
6x40G
6x100G
64x10G
32x40G
32x100G
T3?
64x100G
TH2?
Jericho2?
14x100G
8x10G
64x10G
1RU
SoC architecture
High density 10/25G
 ?
Multi-chip
Lossless Cell-based
& VoQ architecture
Deep buffers
Ultra-low latency (HFT)
NAT
FM4000
FM6000
25G SerDes
25G SerDes
10G SerDes
10G SerDes

---
Merchant Full Custom approach – Moore’s law
Merchant Full Custom approach – Moore’s law
Network ASIC performance has not increased like CPU performance.
In a 12 year span:
- Network ASIC increased:	10x
- CPU perf has increased:	64x
Performance is based on the design process
ASIC = Application Specific Integration Circuit
Top down design, independent of the layout
Network Vendor focusing on the functionality not the implementation
ASIC supplier does the physical implementation
Difficult to achieve high clock rates and scale
Full Custom design flow
Bottom up approach, chip vendor focus on potential implementation
Chip design starts with the clock rate objective
Data paths optimise to achieve the clock rates
Only way to achieve high clock rates
Only the Full custom Chip will allows us to scale for the future
Performance
Time
CPUs 2X/2Y = 64X/12Y
ASIC - LAN 1G to 10G 10X/12Y
ASIC - WAN Routers: 4X/12Y
Why has Networking not kept up with Moore’s Law?
Switching (Merchant Full Custom): 2X/2Y
[Speaker Notes: This is evolution of Merchant silicon – has seen the introduction of Moore’s law into networking – network switch density increasing every 2 years rather perviously very 4-5 years Semi - ASIC – use Fabless develops – integrate each of the layers from a library and vendor integrates their own unique layer for application FPGA – larger and more power than a standard ASIC due to the flexibilty/multi-purpose – VHDL and Verilog are the programing language options]

---
Bringing Merchant Silicon to the Routing Market
Bringing Merchant Silicon to the Routing Market
Look at the routing market
  - The domain of the latest vendor ASIC
  - Changing with the latest – Merchant silicon
Time 
Capability 
Merchant Silicon
capabilities
Routing Feature Complexity

---
Evolution
of 100GE
Densities
Evolution
of 100GE
Densities
96 x 100GE, 3W per 10G port
36 x QSFP 100GE per LC
432 x 100G per chassis
64 x QSFP 40GE in 2RU
48 x QSFP 100GE & 4 x 40G
2015
Today
48x10GE - 2x100GE
12 x QSFP 100GE & 24 x 40G

---
Evolution
of 100GE
Densities
Full Internet table
Evolution
of 100GE
Densities
96 x 100GE, 3W per 10G port
36 x QSFP 100GE per LC
432 x 100G per chassis
Full Internet table
64 x QSFP 40GE in 2RU
48 x QSFP 100GE & 4 x 40G
2015
Today
Full Internet table
48x10GE - 2x100GE
12 x QSFP 100GE & 24 x 40G

---
Evolution
of 100GE
Densities
Full Internet table
Evolution
of 100GE
Densities
96 x 100GE, 3W per 10G port
36 x QSFP 100GE per LC
432 x 100G per chassis
Full Internet table
64 x QSFP 40GE in 2RU
48 x QSFP 100GE & 4 x 40G
2015
Today
Full Internet table
< $3000 per 100G port
48x10GE - 2x100GE
12 x QSFP 100GE & 24 x 40G

---
Merchant Silicon Use Cases for Service Providers
Merchant Silicon Use Cases for Service Providers
NFV / Cloud / DC
Internet / content peering
WAN / Aggregation
IP Services Edge Routing
Internet Peering and Transit
Leaf-spine for 10,000’s servers
Wire speed L2 & L3
VXLAN and eVPN
Flexible 40/100G uplinks
Ease of migration
Ultra deep buffers
Non-blocking 10G & 100G
Large forwarding tables
Alternative to legacy
Dense 100G Capacity
Ultra deep buffers
Power efficient
L2, L3 Services, MPLS-Lite
Segment Routing
10/40/100G Aggregation
Power efficient
Very cost effective bandwidth
Ultra deep buffer architecture
DC and NEBS