## Slide 1: Zen Internet Building For Ultrafast
Andy Furnell <andy.furnell@zeninternet.co.uk>
Technical Architect
Zen Internet

## Slide 2: About Zen
1995
ESTABLISHED
INDEPENDENT PRIVATELY OWNED ISP
FY 15/16
£57M
TURNOVER
2017
450
WHOLESALE & CHANNEL PARTNERS
2013
£3.5M
NETWORK INVESTMENT
2008
MOVED TO SANDBROOK HOUSE
1999
25
EMPLOYEES
2001
PARTNER
PROGRAMME
LAUNCHED
2002
10K
CUSTOMERS
OVER
BROADBAND CONNECTIONS
110K
OVER
2016
£4M
NETWORK INVESTMENT
Notes: 21 years
19x which awards
Wholesale since 2012
2010 sponsors

## Slide 3: ISP Network Capacity 101
What our customers think we should do
What our FD thinks we should do
Notes: Quietest possible
Busiest possible, make best use

## Slide 4: ISP Network Capacity 101
What our customers think we should do
What our FD thinks we should do
What the engineering team think we should do
Notes: Trains are better

## Slide 5: ISP Network Capacity 101
What our customers think we should do
What our FD thinks we should do
What the engineering team think we should do
What we actually do
Notes: Balance time vs cost vs quality

## Slide 6: Managing Capacity 1. Know Your Users
Individuals
Peak:mean 7.5:1
Local Exchange
Peak:mean 4:1
Regional Aggregation
Peak:mean 1.6:1
Notes: Different overheads at different aggregation points
Larger underlying traffic -> more efficient

## Slide 7: Managing Capacity 2. Know Your Failures
Step 1. Model your network
Step 2. Break Some Stuff
Step 2. Break some stuff
Step 3. Record how it broke
Step 4. Find your high watermarks
and some more stuff…
and some more stuff…
More details coming soon at https://engineering.zen.co.uk/

## Slide 8: Managing Capacity 3. Predict The Future
Mar-2015
Mar-2017
Mar-2016
+80% year on year growth
Future bandwidth = Subscriber growth * Peak avg growth * Fudge factors
Mar-2018
Source: Cisco VNI http://www.cisco.com/c/en/us/solutions/service-provider/visual-networking-index-vni/index.html
Notes: Cisco +25% cagr
Zen +80% cagr

## Slide 9
Peak average demand
Notes: Underlying traffic

## Slide 10
Peak average demand
Design inefficiencies
Vendor reality distortion
Notes: LAGs that don’t balance
Boxes choke @64 byte packets

## Slide 11
Peak average demand
Design inefficiencies
Vendor reality distortion
Resiliency
Notes: At least a +1

## Slide 12
Peak average demand
Design inefficiencies
Vendor reality distortion
Resiliency
Peak max demand
Exceptional peaks
1mbit here
4.5mbit here
Notes: when politicians start playing games on a Tuesday

## Slide 13
Peak average demand
Design inefficiencies
Vendor reality distortion
Resiliency
Peak max demand
Exceptional peaks
1mbit here
4.5mbit
7mbit here
7.5:1
33:1
FTTP 330/30
FTTC 80/20
Notes: Ultrafast – ~4x uplift, double the overhead

## Slide 14: Oops, We Broke The Network!
A £4M investment to meet the growing needs of our customers:
Expand and refresh our LLU footprint
  201 → 400 exchanges
  Deeper integration with Openreach
  Support service quality improvements, greater operational ownership
  Cost savings
Refresh our core network technology
  Significant scaling challenges ahead
  40G/slot generation kit becoming long in the tooth
  21 years of accumulated legacy awesome

## Slide 15: LLU Expansion Anatomy Of An LLU Deployment
Ethernet Switch
£500+
Backhaul
£1/mbps/yr+
Power and Cooling
£1250
£200/yr
Rack and Space
£6500
£1000/yr
GEA Cablelink
£4000-6000
Notes: Previously covered
15k investment per exchange
Multiple cablelinks (plus NGA2 cablelinks)

## Slide 16: LLU Expansion Anatomy Of An LLU Deployment
Ethernet Switch
£500+
Backhaul
£1/mbps/yr+
Power and Cooling
£1250
£200/yr
Rack and Space
£6500
£1000/yr
GEA Cablelink
£4000-6000
Highlights
~£15,000 investment per exchange
11,000 man hours spent since May-16
Average time to deliver: 7 months
  LLU colo – 3 months
  Cablelink – 1 month
  Backhaul – 3 months
  Testing, integration, migrations – 3+ months

## Slide 17: Core Network Refresh What Did We Build?
Completely virtualised network
  MPLS end to end
  Decoupled service and transport layer
  Modular approach
Notes: MPLS to the exchange
Standardised transport services
Automated failover
React to changes in traffic

## Slide 18: Core Network Refresh What Did We Build?
Completely virtualised network
  MPLS end to end
  Decoupled service and transport layer
  Modular approach
Scalable and highly available
  Horizontal scale to 10n volumes
  Built to fail (fast)
More bandwidth
More services

## Slide 19: The 5th Largest LLU Operator In The UK
400 unbundled exchanges
7.9M properties passed
110k DSL/FTTx tails
770G GEA capacity
500G LLU backhaul capacity
2.7T core network capacity

## Slide 20: Core Network Refresh Reflections
It’s not (just) about the technology
Right size your choices
Test, test, and test again
(and find someone who will support you with that)
Notes: Right size technology – big capability, small box
Who do you want to work with?
Test – 1.5s failover of 110k DSL subs

## Slide 21: Observations
It’s not (just) about the technology
Right size your choices
*Not to scale
Test, test, and test again
(and find someone who will support you with that)
Notes: Right size vendors – small/friendly. Service led, personal approach
CSR – happy staff, happy customers, happy suppliers, leads through to customer experience
Wholesale test capability

## Slide 22: And Now For The Hard Sell…
One of the largest and most sophisticated networks in the UK
Metered and unmetered, managed and layer 2 wholesale ADSL/FTTC/G.Fast/FTTP offerings
Committed to ultrafast broadband since 2012 launch
Thoroughly nice people 
Notes: Wholesale since 2013
Ultrafast 1.3% market share, stuck with it

## Slide 23: Thankyou