## Slide 1: None of us really knew what we were doing, we just made it up as we went along.
(Part 2 – You were threatened with this)
A further wander down
memory lane stopping off at
the UK Internet in 1998
(give or take a bit)
Paul Thornton
paul@prtsystems.ltd.uk
UKNOF37
Manchester
20 April 2017
Notes: Do we know what we’re doing now?

## Slide 2
What did the ISPs of the day offer?
How did they do it?
Whose kit did they use?
Did it even work?
PRTsystems
www.prtsystems.ltd.uk
Previously at UKNOF34

## Slide 3
Infrastructure!
How the LINX scaled to 1G.
The important buildings of the day.
The headaches...
PRTsystems
www.prtsystems.ltd.uk
New and improved for this year:

## Slide 4
Digital archaeology is hard 
PRTsystems
www.prtsystems.ltd.uk
But a small aside before that...

## Slide 5
Digital archaeology is hard 
PRTsystems
www.prtsystems.ltd.uk
But a small aside before that...
dd: /dev/nsa0: Input/output error 0+0 records in 0+0 records out 0 bytes transferred in 48.053826 secs (0 bytes/sec)
Notes: It took it 48 seconds to establish that things were not going to work out!
The most reliable storage is my original 1993-era IBM 0663 1G SCSI hard drive.
Think about long-term data storage.

## Slide 6
“There is no sensible way that the LINX can grow to much more than around 100 members.”
Paul Thornton (1998)
Lets put this into perspective: Thomas Watson from IBM said there was a market for maybe 5 computers worldwide!
PRTsystems
www.prtsystems.ltd.uk
AS5459
Notes: And at the time, content providers and tier-2 ISPs as we now know them couldn’t join.

## Slide 7
Exchange points were few and far between.
MAE-EAST and MAE-WEST in US.
NetNod, LINX and AMS-IX the only choices in Europe.
Everything was expensive!
PRTsystems
www.prtsystems.ltd.uk
Interconnection

## Slide 8
Present in Telehouse North only.
7 switches interconnected with 100M FDDI:
2x Catalyst 5000
2x Plaintree 4800
3x Catalyst 1200
These switches were 10/100 + FDDI.
PRTsystems
www.prtsystems.ltd.uk
LINX in 1998
Notes: More on FDDI later

## Slide 9
Present in Telehouse North only.
8 switches interconnected with 100M FDDI:
2x Catalyst 5000
2x Plaintree 4800
3x Catalyst 1200
These switches were 10/100 + FDDI.
PRTsystems
www.prtsystems.ltd.uk
LINX in 1998
Notes: More on FDDI later

## Slide 10
Present in Telehouse North only.
8 switches interconnected with 100M FDDI:
2x Catalyst 5000
2x Plaintree 4800
3x Catalyst 1200
These switches were 10/100 + FDDI.
PRTsystems
www.prtsystems.ltd.uk
LINX in 1998
Notes: This is the actual switch0.linx.net

## Slide 11
Present in Telehouse North only.
8 switches interconnected with 100M FDDI:
2x Catalyst 5000
2x Plaintree 4800
3x Catalyst 1200
These switches were 10/100 + FDDI.
PRTsystems
www.prtsystems.ltd.uk
LINX in 1998
Notes: This isn’t a 4800, it’s the larger chassis – but was the only photo I could find.

## Slide 12
PRTsystems
www.prtsystems.ltd.uk
LINX in 1998
Shamelessly borrowed from Keith’s NANOG15 presentation
Notes: More – much more – on FDDI later...

## Slide 13
53 members (October)
300Mbit/sec average traffic, 400Mbit/sec peak.
9,000 routes out of a global table of 55,000
PRTsystems
www.prtsystems.ltd.uk
LINX in 1998
Notes: Graph stolen from Keith’s January 1999 NANOG update.
More on the blip at the beginning of November later...

## Slide 14
LINX joining process was convoluted, and somewhat counter-productive. Contained the infamous “Three Traceroutes” requirement.
Excluded content providers and smaller ISPs.
Led directly to formation of LoNAP.
PRTsystems
www.prtsystems.ltd.uk
LINX in 1998
Notes: L2 services sold by INS/Xara to NY got around the three traceroutes rule.
LoNAP formed in March 1998.

## Slide 15
100M FDDI interconnect too limiting, and members were asking about 1G connections.
New LINX topology involved 1G capable switches – Packet Engines PowerRail and Extreme Summit series.
PRTsystems
www.prtsystems.ltd.uk
LINX upgrade to 1G

## Slide 16
This was the first PR5200 switch at LINX – mixture of 10/100, 1G and FDDI ports.
Shortly afterwards, Packet Engines acquired by Alcatel.
PRTsystems
www.prtsystems.ltd.uk
LINX upgrade to 1G
Notes: Powerrail had excellent hardware.

## Slide 17
Extreme are still going strong and still have a presence at LINX.
This particular Summit 48 was the first Extreme switch added into the LINX LAN.
PRTsystems
www.prtsystems.ltd.uk
LINX upgrade to 1G
Notes: This was the original switch7 Summit 48.

## Slide 18
FDDI had inherent protection, but gig-E didn’t – we had much debate about the merits of STP.
This was one of the occasions where Keith and I had a ‘full and frank exchanges of technical viewpoints’!
These normally resulted in a good architectural compromise though.
PRTsystems
www.prtsystems.ltd.uk
LINX upgrade to 1G

## Slide 19
I remember the initial migration well. It wasn’t a fantastic success.
The first weekend of November: long nights and packet-loss filled days – a number of issues with LINX network and member connections.
The maintenance work and subsequent downtime made the UK national press...
PRTsystems
www.prtsystems.ltd.uk
LINX upgrade to 1G

## Slide 20
PRTsystems
www.prtsystems.ltd.uk
LINX upgrade to 1G
... but not the tech newsletter of the day.

## Slide 21
This underlined a bit of a recurring theme.
Switch vendors didn’t understand the load that IXPs placed on their equipment.
LAN-centric flow expected: Servers to lots of lower speed clients. Meshy nature of IXPs quickly shows up shortcomings.
PRTsystems
www.prtsystems.ltd.uk
LINX upgrade to 1G
Notes: Cat 5000 especially prone to this, but all of the hardware suffered from some form of this problem in one way or another.

## Slide 22
LINX originally had a /23 of IPv4 PI space
This was soon deemed to be much too small.
So we became a RIPE LIR and acquired a /19 of PA space.
Which was duly carved up, and the peering LAN renumbered...
PRTsystems
www.prtsystems.ltd.uk
Addressing challenges
Notes: This was the first ‘great renumbering’ in 1998/1999.

## Slide 23
PRTsystems
www.prtsystems.ltd.uk
Addressing challenges
Notes: LINX members will recall a large renumber to extend the Juniper peering LAN from a /23 to a /22
It was designed that way in the first place!

## Slide 24
PRTsystems
www.prtsystems.ltd.uk
Addressing challenges
The peering LANs had a /21 reserved for them from day one.
It wasn’t my fault you had to renumber again after all.
Notes: LINX members will recall a large renumber to extend the Juniper peering LAN from a /23 to a /22
It was designed that way in the first place!

## Slide 25
LINX also hosted the original k.root-servers.net machines for the RIPE NCC.
PRTsystems
www.prtsystems.ltd.uk
Key Infrastructure
Notes: The marmite jar shall remain a mystery for those not aware of the secret brotherhood of marmite

## Slide 26
And the .UK primary nameserver, ns0.nic.uk for Nominet.
PRTsystems
www.prtsystems.ltd.uk
Key Infrastructure
Notes: This was a quality Sun clone inherited from PSINet UK.

## Slide 27
DNS traffic was interesting.
Levels were quite low (average of 2Mbit/sec out from k.root, and 150Kbit/sec out from ns0.nic.uk in November 1998).
Looking at queries / responses (for operational reasons, of course) was enlightening.
PRTsystems
www.prtsystems.ltd.uk
Key Infrastructure

## Slide 28
Snapshot of 100K queries every 10 mins in August 1998 to k.root yielded the following averages over an hour:
19% of requests led to an NXDOMAIN – mostly due to queries for things like ‘WORKGROUP.’ from Windows machines.
6% of queries originated from RFC1918 space.
PRTsystems
www.prtsystems.ltd.uk
Key Infrastructure
Notes: I can’t imagine this is any better today.

## Slide 29
LINX also built a PoP in the new Redbus Interhouse building on Millharbour, now known as Telecity LON1 Equinix LD Digital Realty LHR19
Dark fibre between there and Telehouse North.
LINX and AMS-IX both went multi-site at about the same time.
PRTsystems
www.prtsystems.ltd.uk
LINX has left the building

## Slide 30
The London scene was thin:
Telehouse North (of course) – but still a lot of DR DR space.
Telehouse Metro recently opened (1997) in City.
Redbus Interhouse Millharbour (1998).
PRTsystems
www.prtsystems.ltd.uk
Speaking of DCs...
Notes: TFM1 and TFM2 don’t look very different...

## Slide 31
And there wasn’t much elsewhere either...
Manchester – original Telecity Williams House
Some other provider-specific facilities, but still thought of more as single-occupancy ‘computer centres’ than a datacentre as we’d consider it today.
PRTsystems
www.prtsystems.ltd.uk
Speaking of DCs...

## Slide 32
Ethernet had yet to win the “use me for everything” race.
ATM, frame relay, PoS used for WANs.
Typical speeds still 155M / 622M for backbones. 2M down for customers.
PRTsystems
www.prtsystems.ltd.uk
Connectivity Technology
Notes: Ethernet chipsets not commodity. 1GE switches still only just coming online at a reasonable price

## Slide 33
Even on the LAN, Ethernet/IP wasn’t a given.
FDDI / Token Ring still very much in use for physical communication – but expensive.
IPX / Appletalk were still protocols of choice.
PRTsystems
www.prtsystems.ltd.uk
Connectivity Technology
Notes: All of those protocols so beloved by CCIE question setters!

## Slide 34
There were the light-hearted moments.
Paul’s tip to IXPs:
A sure-fire way to stop people from transmitting MoU violating frames on the peering LAN is to run a live tcpdump on the projector in the background whilst presenting at a member meeting.
PRTsystems
www.prtsystems.ltd.uk
And finally...
Notes: Be sure that the font is large enough that MAC addresses are clearly readable though.

## Slide 35
One member who shall remain nameless, and didn’t remain a member long afterwards, was caught with GRE tunnels to the US over other members’ connections.
Claimed I’d plugged a Cat5 cable into the wrong port on their router to cause this, and issued a press release explaining how the packets therefore went the wrong way!
PRTsystems
www.prtsystems.ltd.uk
And finally...

## Slide 36
LINX hosted RIPE31 in Edinburgh.
The connectivity was provided by LINX, via a GRE tunnel across JANET. Routing used BGP and carried a full table.
The next-hop to the neighbor address in London was learned via the BGP peering session with it. The router had an existential crisis if restarted.
PRTsystems
www.prtsystems.ltd.uk
And finally...
Notes: No, I can’t find the router config.
Its hostname was great-uncle-bulgaria.linx.net though.

## Slide 37
One enterprising startup tried to capitalize on both the Telehouse and LINX name, causing consternation to both; and the engagement of lawyers on all sides.
PRTsystems
www.prtsystems.ltd.uk
And finally...

## Slide 38
Luckily for both parties, PSINet came along and bought them out - both the name and the problem went away.
That project is a story for another year though...
PRTsystems
www.prtsystems.ltd.uk
And finally...

## Slide 39
This series of presentations, diagrams, router configurations and other tidbits I managed to locate can be found at:
http://www.prt.org/history
I know that the LINX marketing department simply adore the 1997-era logo.
PRTsystems
www.prtsystems.ltd.uk
Any Questions?

## Slide 40: Thank you
PRTsystems
Paul Thornton
paul@prtsystems.ltd.uk
UKNOF37
Manchester
20 April 2017