## Slide 1: The Multi-Terabit DDoS Era - Memcached
Sean Newman Director Product Management

## Slide 2: DDoS Still on the increase…
Memcached GitHub 1.35-1.7Tbps
500 Gbps Hong Kong attack France swarmed after terror attack PlayStation & Xbox hit at Christmas
Mirai Botnet OVH / Krebs / DYN 600 Gbps -> 1Tbps
Rio Olympics 540 Gbps
Spamhaus attack: Reported to reach 310 Gbps
2013
2005
2007
2009
2011
2015
2016
First Hacktivists: Zapatista National Liberation Army
DoS for Notoriety
Spammers discover botnets
Estonia: Parliament, banks, media, Estonia Reform Party
1993
Anon hits Church of Scientology
Coordinated US bank attacks: Grew to 200 Gbps, and continue today
ProtonMail
attack
2017
…
2018
Reaper Botnet 2M Devices

## Slide 3: Increasingly Sophisticated IoT Exploits
Mirai – Basic password brute-force
  Pre-populated default user/password pairs
Reaper – Authentication bypass vulnerability
  Empty user and password parameters in URI
Satori/BrickerBot – Huawei Router Vuln (CVE-2017–17215)
  Zero-day vulnerability posted openly on Pastebin
  Injection of commands within a “firmware update”
  Result: Undetected malicious code installed on the device
IoTroop, etc… – Ongoing IoT Challenge
  Low performance devices running lightweight code
  Cheap devices, with focus on function, not secure code

## Slide 4: New Attack Vector – Memcached
General Purpose distributed memory caching system
  Often used to speed up database-driven websites
Default …/etc/sysconfig/ enables service for all to use
  Service on TCP, and crucially UDP, port 11211
  Designed for speed, so access does not require authentication
Standard component of common Linux distributions
  Centos, Ubuntu, etc…
  Including most instances hosted in public clouds
UDP Memcached on the Internet enables reflection attacks
  This reflection vulnerability has been around for >10 years

## Slide 5: WhiteHat PoC Raised Awareness
2Tb/s Exploit demonstrated at Power of Community 2017
  http://powerofcommunity.net/poc2017/shengbao.pdf
Appealing to attackers for scale of amplification possible…
Within a quarter, we started to see the first DDoS attacks

## Slide 6: GitHub Attacked using Memcached
Wednesday 28th February, 2018 – 1.35Tb/s GitHub attack!
Offline for 10 minutes, whilst Akamai figures out mitigation
Within hours Corero customers were being targeted
Four days later, Arbor Networks claimed new largest attack
  1.7Tbps attack against unnamed Arbor customer

## Slide 7: Memcached Attack – Explained
Open memcached port 11211 enables simple telnet access
  stats items command enables simple lookup of memcached ‘slab’ usage
  Typically 42 ‘slabs’ available, #42 is largest @ 10GB in 1MB entries
  Each entry can be filled with data, by any user, and given associated ‘key’
In this case, fetching, with a get, reveals interesting payload
  Entry is filled to within a few bytes of 1MB maximum

## Slide 8: Weaponising Memcached - Searching
Vulnerable memcached Servers
UDP (stats)
UDP (stats)
UDP (stats)
(reply)
(reply)
(reply)
1. Attacker Scans Internet on UDP 11211
2. Builds list of responding IPs
IP 1.1.1.1 IP 2.2.2.2 …. IP n.n.n.n @ ~100Mb/s each
~10k needed for 1Tb/s

## Slide 9: Weaponising Memcached - Staging
3. Attacker Pre-loads cache payload and associated key
~ 1MB to key (a)
Loading thousands of servers is non-trivial exercise
Likely takes 10s of minutes
Vulnerable memcached Servers
UDP (set a)
1MB data (a)
UDP (set a)
1MB data (a)
UDP (set a)
1MB data (a)

## Slide 10: Weaponising Memcached - Activating
4. Attacker Sends “get a…” to each server on the list small message with source spoofed to be that of victim
From 100Mbit link attacker can enable 10k servers in a single second
Vulnerable memcached Servers
UDP (get a a a…)
1MB data (a)
UDP (get a a a …)
1MB data (a)
UDP (get a a a …)
1MB data (a)
1MB data (a) from n servers at ~100Mbit/s

## Slide 11: Weaponising Memcached - Activating
Vulnerable memcached Servers
UDP (get a a a…)
1MB data (a)
UDP (get a a a …)
1MB data (a)
UDP (get a a a …)
1MB data (a)
10,000x amplification = Terabits per second
1MB data (a) from n servers at ~100Mbit/s
4. Attacker Sends “get a…” to each server on the list small message with source spoofed to be that of victim
From 100Mbit link attacker can enable 10k servers in a single second

## Slide 12: Neutralising Memcached
vulnerable memcached servers
RELOAD memcached (attack payloads)
~ 1MB to key (a)
UDP (set a)
UDP (set a)
UDP (set a)
1MB data (a)
1MB data (a)
1MB data (a)
COUNTERMEASURE Respond with UDP (flush_all) to each attacking server
COUNTERMEASURE is 10,000 times more efficient than attacker’s reload – reverse of amplification
UDP (flush_all)

## Slide 13: Neutralising Memcached
Memcached’s flush_all command instantly clears all cache entries
  Provides ability to rapidly diminish sustained attacks
  No data is destroyed, but, need to be aware of any legal implications
Countermeasure can begin immediately with no collateral damage
  Packet rate is minimal (reverse of amplification)
Automated countermeasure generation is trivial…
  netcat
    python -c "print '\0\x01\0\0\0\x01\0\0flush_all\r\n'" | nc -nvvu xxx.xxx.xxx.xxx 11211 > /tmp/null
  /dev/udp
    echo -ne '\0\x01\0\0\0\x01\0\0flush_all\r\n' > /dev/udp/xxx.xxx.xxx.xxx/11211
  Where xxx.xxx.xxx.xxx is the source IP of an attacking memcached
Once amplification is destroyed memcache is useless for DDoS

## Slide 14: Public Memcached Servers in Decline
April 2018
Oct 2017
Number of vulnerable servers is diminishing due to publicity of exploit

## Slide 15: Memcached Vulnerability Fixed?
Memcached authors release latest version with UDP disabled by default

## Slide 16: Summary
DDoS as a whole still on the Increase
  Attack Methods/Vectors more Sophisticated
  No surprise that new vectors such as memcached emerge
Traditional Protection is not effective enough
  Typically too slow to react to avoid damage
Service and Hosting Provider Reputation is at Risk
  Many organisation still believe their provider protects them
Deploying Modern DDoS Protection is an Opportunity
  Removes all DDoS Traffic from your infrastructure
  Differentiates you from your competitors
  Can enable incremental revenue stream by selling on as a service

## Slide 17: Questions?

## Slide 18: Thank You!