## Slide 1: NetDevOps Style Configuration Management for the Network
Stuart Clark Network Automation Evangelist
Cisco Devnet
What it means for network engineers, and why we should care?

## Slide 2: Game Plan
Virlutils Network Simulation
What are Infrastructure as Code and Configuration Management?
Benefits of Configuration Management
Recipes, Manifests, Playbooks, and the Tools
Configuration Management with Ansible Example

## Slide 3: “virl up” Network Simulation Done Right
virlutils makes it easy to start a network simulation
virlutils is written in Python
https://github.com/CiscoDevNet/virlutils

## Slide 4: Why Ansible for the Network?
Agentless
Currently popular in network community
  ie Lots of examples!
Written in Python
Simple to install and get started!
But explore other options as well!
LINX102

## Slide 5: What are Infrastructure as Code and Configuration Management?

## Slide 6: Infrastructure as Code… huh?
“Infrastructure as Code (IaC) is the process of managing and provisioning computer data centers through machine-readable definition files...”
https://en.wikipedia.org/wiki/Infrastructure_as_Code

## Slide 7: Some Principals of ”Network as Code”
Store network configuration in source control systems (ie git)
  Use ”machine readable” formats like YAML, JSON, XML
Treat the source control as single source of truth
  Develop, test, and deploy to prod from same source
Deploy configuration using programmatic APIs and tooling
  Limit manual network configuration
  Explore “Configuration Management” tooling.

## Slide 8: Mechanism = Automation
No more hand to hand combat configuration management
Configuration Management today is about the “tools”
Consistency + Scale Success!

## Slide 9: Characteristics = Desired State
The software and version installed
System attributes like name, address, ownership, etc
Feature specific configurations

## Slide 10: Benefits of Configuration Management

## Slide 11: Quickly Provision Infrastructure
Sequential and Manual

## Slide 12: No More Snowflakes
System Variation

## Slide 13: Version Controlled Infrastructure
Organic Configuration

## Slide 14
Infrastructure as Code
Version Controlled Infrastructure

## Slide 15: Commonalities of Configuration Management Tools
Open Source Foundation
Automation and Orchestration
Idempotent Behavior
Facts, lots of facts
Modules and Libraries

## Slide 16: Matrix of Common Info and Terms
 | Ansible | Puppet | Chef | SaltStack
Language | Python + YAML | Ruby Based | Ruby | Python
Managed Node Requirements | Agentless | Traditionally Agent Based | Agent Based | Agent Based “minions”
Centralized Management | Any computer can be “controller” Optional “Tower” | Puppet Master | Chef Server | Salt Master
What you create | Playbook / Roles | Manifest / Module | Recipe / Cookbook | Pillar / Include

## Slide 17: ”Network as Code” with Ansible for Configuration Management
Ansible Playbook
  Run roles against relevant groups
Ansible Roles
  Align to network roles
Inventory File
  List network devices
  Logically group for configuration
Variable Files
  Device specific details
  General group details

## Slide 18: Starting Network Topology
Physical Topology
  “Core” – IOS XE Routers
  “Distribution” – NX-OS Switches
  “Access” – NX-OS Switches
Network has been cabled already
Management access to devices enabled
  No other configuration completed

## Slide 19: Desired Network Configuration
Layer 3 Links between Core/Dist
  OSPF Area 0 Routing Configured
Distribution configured for VPC Domain
Layer 2 port-channel trunk to access
Set of VLANs Configured
  SVIs at Distribution with HSRP Configured

## Slide 20: Running the code
Bring up the topology – virl up [virlfiles/name]
  Not specifying a virlfile name will import the default one from the current directory
See the simulations are currently running on your server virl ls --all
Check the state of the nodes - virl nodes
  This will display the nodes, name, ip address and state
Once the nodes are available - virl generate ansible
  Creates the default inventory file
  Use virl --help to see the variety of commands that are available

## Slide 21: Advantages of VIRL as the development environment
Robust support for large topologies mimicking production
Simulations can include servers and applications in addition to network
Full data plane within the simulation to test traffic flows and protocol behaviour
Off-load simulation to remote server
But there are definite caveats to consider as well.
For typical uses, not a fully local dev environment
Significant time to instantiate networks
Not an insignificant resource requirement for large topologies

## Slide 22: What did we cover?
What are Infrastructure as Code and Configuration Management?
Benefits of Configuration Management
Recipes, Manifests, Playbooks, Oh My! The Tools
Configuration Management with Ansible Example

## Slide 23: What do do next?
Resources
  Network Automation with Ansible (ansible.com)
  Network Automation wtih Salt (saltstack.com)
  Network Automation with Puppet (puppet.com)
  Network Automation with CFEngine (cfengine.com)
DevNet Learning Labs
  Introduction to Ansible
  Using Ansible with NX-OS Devices
  Introduction to ACI and Ansible
  Home Lab: Using Ansible from your Desktop OS
Blogs and Videos
  What does "Network as Code" Mean?
  Automating Cisco ACI with Ansible Eliminates Repetitive Day-to-Day Tasks
  NetDevOps Video Module

## Slide 24: Got more questions? Stay in touch!
stuaclar@cisco.com
@bigevilbeard
http://github.com/bigevilbeard
@CiscoDevNet
facebook.com/ciscodevnet/
http://github.com/CiscoDevNet
Stuart Clark
developer.cisco.com