## Slide 1: Routing in Fat Trees Engineering Simplicity in IP Fabric
Melchior Aelmans melchior@juniper.net

## Slide 2
IP Fabrics: The Big Picture
  Standardized Form-Factor of Network Capacity
  Next-Gen Evolution Drivers
Next Gen Underlay Routing Protocol Requirements
RIFT Basic Concept
RIFT Advantages
Standards Status
Product Status

## Slide 3
The BIG Picture
Next Gen IP Fabric Evolution Drivers

## Slide 4: IP Fabrics: The Big Picture
The Global Data Center Market Size is Expected to Reach Revenues of around $174 Billion by 2023
    growing at a CAGR of about 4% 2018–2023
Topologies & Technologies are Unifying Towards a “IP Fabric Substrate” in Proximity to Producers and Consumers of Content
Fortune 1000 Generate and Host Content and are Building Own IP Fabrics to Consume Larger and Larger Amounts of “Local” Networking Capacity
Building IP Fabrics Today is Largely High OPEX Artisanal Activity
Most Fortune 1000 Need a ”Standardized Form Factor” for Bandwidth Just Like Storage
We Lack a Standardized ZTP Underlay Technology to Make IP Forwarding in Fabrics as Simple as Ethernet Switching

## Slide 5
WHAT and WHY ?
RIFT/TechClub '19
Hyper-scalers are Extrapolating the Things to Come
  Vast Amount of Bandwidth Close to Producer & Consumer Are Provisioned
    IP Fabrics in DC (Server Farms)
    Metro (Caches and Access)
    Disaggregated Chassis Architectures in Backbone with Regular Fabrics Holding Leaves Together
  Those Topologies are Uniform, Local and Regular
    At the End, Economics of Interconnecting of Crossbars Done in 1950 in Bell Labs are Still Valid
  WAN-Style Traffic Engineering & Protection is Being Replaced by Wide Fan-Out & Distributed Systems Redundancy (Rather Than Chassis & FRR)
    Simpler is Cheaper in Opex _and_ Capex
  Hyper-Scalers are Building Customized High-Opex Solutions to Manage those Fabrics
IP Fabric is Becoming the New “RAM Chip” to Consume Bandwidth
  No’one Configures SSD Wear-Leveling, RAM Banks and CAS/RAS Manually in Every Laptop
  IP Fabrics HW is Largely Commodity Already
    L3 Forwarding is the New L2
  IP Fabrics Must and Will “OPEX Commoditize”
Customers are Hosting Their Content & Critical Business Processes
  Hybrid Cloud for Many Reasons, One of Them to Keep Real-Estate from Hyper-scalers
  Need to Build Own Fabrics
  Hard to Sustain Proprietary OPEX Efforts

## Slide 6
Link State and SPF = Distributed Computation
Topology Elements
  Nodes
  Links
  Prefixes
Each Node Originates Packets with Its Elements
Packets are ”Flooded”
”Newest” Version Wins
Each Node “Sees” Whole Topology
Each Node “Computes” Reachability to Everywhere
Conversion is Very Fast
Every Link Failure Shakes Whole Network (modulo Areas)
Flooding Generates Excessive Load for Large Average Connectivity
Periodic Refreshes (not Strictly Necessary)

## Slide 7
Distance/Path Vector = Diffused Computation
Prefixes “Gather” Metric When Passed Along Links
Each Sink Computes “Best” Result And Passes It on ( Add-Path Changed That )
A Sink Keeps All Copies, Otherwise It Would Have to Trigger “Re-Diffusion”
Loop Prevention is Easy on Strictly Uniformly Increasing Metric
Ideal for “Policy” Rather Than “Reachability”
Scales When Properly Implemented to Much Higher # of Routes Than Link-State

## Slide 8
Current State of Affairs
Several of Large DC Fabrics Use E-BGP with Band-Aids as De-Facto IGP (RFC7938)
  Numbering Schemes to Control “Path Hunting”
    ”Looping Paths” (allow-Own-as Under AS Private Numbering)
    “Relaxed Multi-Path ECMP” Since ECMP over Different AS in EBGP Does Not Work Normally
  Add Paths to Support Multi-Homing, N-ECMP, Prevent Oscillations
  Efforts to Get Around 65K ASes and Limited Private AS Space
  Proprietary Provisioning and Configuration Solutions, LLDP Extensions
  “Violations” of FSM Like Restart Timers and Minimum-Route-Advertisement Timers
  Emerging Work for “Peer Auto-Discovery” and “SPF” Diametrically Opposite to BGP Design Principles
  Reliance on “Update Groups” ~ Peer Groups to Prevent Withdrawal and Path Hunting After Server Link Failures
Others Run IGP (ISIS)
  Generally a “Better” Approach to Faster Convergence
  Current Attempts to Deal with Some “Spot Problems” like Flooding Reduction
Yet Others Run BGP over IGP (Traditional Routing Architecture)
Less Than More Successful Attempts @ Prefix Summarization, Micro- and Black-Holing, Blast Radius Containment
Server Multi-Homing not Possible Using IP Due to Equal Cost and Scaling Constraints, Hence MC-LAG’ed Solutions or EVPN
In Summary: High OPEX Solutions Not Necessarily Viable for Customers Who Cannot or Do Not Want to Build Sophisticated Talent Pool to Deal with Their “Unicorn” Fabrics
RIFT/TechClub '19

## Slide 9
Next Gen IP Fabric Underlay Routing Protocol Requirements

## Slide 10: Next Gen Underlay Protocol Requirements
Problem / Attempted Solution | BGP modified for DC (all kind of “mods”) | ISIS modified for DC (RFC7356 + “mods”) | RIFT Native DC
Peer Discovery/Automatic Forming of Trees/Preventing Cabling Violations | ⚠️ | ⚠️ | ✓
No Need for Internal Addressing, Minimal Amount of Routes/Information on ToRs, Stretches True Routing to the Multi-Homed Host | ✘ | ✘ | ✓
High Degree of ECMP (BGP needs lots knobs, memory, own-AS-path violations) and ideally NEC and LFA | ⚠️ | ✓ | ✓
Non Equal Cost Multi-Path, ECMP Independent Anycast, MC-LAG Replacement | ✘ | ✘ | ✓
Traffic Engineering by Next-Hops, Prefix Modifications | ✓ | ✘ | ✓
See All Links in Topology to Support PCE/SR | ⚠️ | ✓ | ✓
Carry Opaque Configuration Data (Key-Value) Efficiently | ✘ | ⚠️ | ✓
Take a Node out of Production Quickly and Without Disruption | ✘ | ✓ | ✓
Automatic Disaggregation on Failures to Prevent Black-Holing and Back-Hauling | ✘ | ✘ | ✓
Minimal Blast Radius on Failures (On Failure Smallest Possible Part of the Network “Shakes”) | ✘ | ✘ | ✓
Fastest Possible Convergence on Failures | ✘ | ✓ | ✓
State of the Art Security Including Originator Validation and Replay Prevention | ✘ | ✘ | ✓
Simplest Initial Implementation | ✓ | ✘ | ✓✘

## Slide 11
RIFT Basic Concept

## Slide 12: RIFT Concept

## Slide 13
RIFT Advantages

## Slide 14
Automatic De-Aggregation
South Representation with Adjacencies of Red Beta is Reflected by the Green Layer to Alpha
Alpha Red Spine Computes P1 Reachability (Tree that Indicates Next-Hops)
alpha Sees that Beta has no Adjacencies to any of the available Next-Hops to P1
Alpha Disaggregates P1
Left Green Nodes do NOT Propagate Disaggregation Further
When Beta Obtains a Viable Next-Hop to P1, Alpha Automatically Reaggregates

## Slide 15
Northbound Bandwidth Balancing
Zeta Computes Bandwidth Sum to NextHop and Next Level Up
Through A Cumulative 60 Units
Through B Cumulative 70 Units
Default Route Uses That in Some Form to Unequal Load Balance
Perfectly Safe Since RIFT is Loop-Free

## Slide 16: Operational Advantages
Open IETF Standard
  Can Build Hybrid Vendor Fabrics
  Protocol is Well Reviewed and Understood by World-Class Experts
True ZTP
  No Configuration Necessary
  V4 over V6 Forwarding
  Mis-cabling Handled
Can Operate on Asymmetric Bandwidth Fabrics and Handle “Fat Link” Failures By Adjusting Automatically
Can Support and Scale to an Architecture with Multi-Home Servers
  No Need for Service Migration on ToR Upgrades
  Can Talk Directly to Hyper-Visors/Kubernetes GW
BFD is “Built In”
  Can Be Used for Fast Rehash or Early Loss Detection
Runs on UDP
  Trivial Kernel Support on All Platforms
  Allows for Max. Speed Flooding
  Easy to “Multi-Instantiate” for Different Purposes
Minimal Blast-Radius
  Failures/Bring-Up on Fabric Only Affects the Smallest Viable Radius
RIFT Flooding is ~30% of Normal Flat IGP
  Built-In Flood Reduction Reduces Flood Traffic to <20% of Flat IGP
Loop-Free
  Can Utilize All Viable Paths Through Fabric
  Can Support True Anycast
Model Based
  Much Less Possibility for Parser and Formatter Bugs Plaguing Today’s Networking Protocols
Specification is Written for Maximum parallelization
  With Enough Cores IP Switches Should Be Able to Converge @ Speeds Making FRR Unnecessary (Assuming Fast Rehash)
KV Store Allows to Replace Out-Of-Band Applications
  IP/MAC Binding Can Be Flooded to Top-of-Fabric
Sophisticated, Newest Routing Security
Full Fabric Visibility at the Top

## Slide 17
Standardization Progress

## Slide 18: Standardization Progress
RIFT Standards Track IETF Working Group in Revision -12
  Security Area Directorate Early Revision Done and Addressed
  IESG Revisions Being Addressed
  Co-Authors from Cisco, Yandex, Mellanox, HP & Implementing Individuals
  https://tools.ietf.org/html/draft-ietf-rift-rift-12
Applicability Draft
  Co-Authored with operators, e.g. Orange and Yandex
  Under Gen-ART review
  https://tools.ietf.org/html/draft-ietf-rift-applicability-03

## Slide 19
Product Status

## Slide 20: Productization
Implementations
Juniper Networks
  FCS in 19.4R1 64-bit Junos
  Package Installing over 19.4R1 or Newer
  QFX (All Variants), vMX, MX
  cRPD & EVO in progress
  https://www.juniper.net/us/en/dm/free-rift-trial/
Python Open-source by Bruno Rijsman
  https://github.com/brunorijsman/rift-python
Documentation
Day One Book: Routing in Fat Trees (RIFT)
  covering Juniper and open-source implementation
  RIFT Wireshark dissector
  Download free: http://jnpr.nl/rift

## Slide 21: RIFT: Engineering Simplicity in IP Fabric d Questions?
Melchior Aelmans melchior@juniper.net