## Slide 1: Scaling your metro - the journey from 10G to 400G
Will Hargrave
Virtual UKNOF
20th July 2020 | Everywhere

## Slide 2: Typical Internet Exchanges
Ethernet fabric shifting large volumes of traffic in the metro
  What is ”metro”? 10km? 80km? 200km?
  London: longest path between interconnection dense colos is 72km
  Many links are under 10km
Technology choices impact viability
Typically point to point links on dark fibre to enable scaling
  Solutions ideally scale at less-than-linear
We will focus on technologies suitable for Internet Exchanges
  Own infrastructure, scaling, point-to-point, low cost

## Slide 3: ISL Sizing Strategy at LONAP
ISLs must deliver traffic demand, even during fault conditions
We use sflow to report intersite traffic demand
Sum of per-site connected capacity is not very useful
  Wide variation in port utilisations
Custom graphing solution to sum ”LAG” members
  All ISLs are multipath ECMP IP p2ps, no LACP
  Must also check traffic balance within a ‘LAG’
30% traffic growth per year
Notes: Good value ports -> utilization varies

## Slide 5: 2015 era – 10G DWDM
Simpler times
Buy 40km or 80km DWDM SFP+, insert into switch, passive mux
No amplification, dispersion compensation to worry about
n * 10GE – scaled to around 160G in our current setup
Difficulties with ’too many moving parts’ at this scale
  Total of 32 SFP+, 64 fibre cores, 128 connections
  Could be > 256 fibre end-faces to clean even for a modest 16 channel setup

## Slide 7: 100G choices at LONAP
2016:
  Lighting 100G on dark fibre pairs/ 1310nm waves
  Initially ”standard” 100GBase-LR4
2018 onwards:
  Migrated to CWDM4/4WDM10 for 30-50% cost saving
  4WDM10 provides superior optical performance than LR4
  Both require RS-FEC host support (not a problem)
2018-20:
  Need more than 100G per path
  Deployed 100G PAM4 solution – scales to 800G+/pair
  Testing 100G Bidi – scales to 200G/pair

## Slide 8: 100G+ in the metro (10km+)
No straightforward passive 100G DWDM option
Investigated Coherent transponder solutions - many options exist
Coherent can deliver up to 600G/wavelength, over thousands of kilometres at many terabits/pair – prime technology for larger telcos
Flexible modulation
Relatively power-hungry and complex
Relatively poor financial scaling
Opinion: “I don’t feel that these are a great solution for IXPs, is there something cheaper/better at scaling?”

## Slide 9: 100G PAM4
Inphi ”ColorZ”: 2x50G PAM4 λ encoded in a single 100GHz DWDM channel
Standard QSFP28 in switch
  Arista EOS supports DOM extensions to instrument on-optic FEC DSP
Optical specifications:
  Output power of -8dBm and min input power of -2dBm
  Dispersion tolerance +/-6 km on G.652 fibre
  Requires dedicated optical line system to address these challenges
PAM4 modulation

## Slide 10: Open line systems
Vendors start to produce dedicated systems to address these challenges
Minimal configuration required
“Feels like a passive DWDM mux” (but needs power)
Contains optical amplification and dispersion compensation
Components in Smartoptics DCP-M series

## Slide 12: 100G+ in the metro: Shorter links
Many of our links are in the < 10km range
”The grey area”
Do cheaper options exist?
Direct price comparison against MRC charges for additional dark fibre pairs and/or datacentre crossconnects
Testing 100G-Bidi with APC connectors (Flexoptix)
  functions OK for simple links < 2km
  Scales to 200G/pair

## Slide 13: 400G
400G already shipping in quantity, for “LAN” links <10km
  Growing very fast, bandwidth of deployed 400G ports is expected to exceed 100G this year
  Optic cost is very competitive – per-gig cost already cheaper than 100G
Obviously you will need 400G host ports
  but that’s coming quite quickly for LONAP!
In the future coherent ‘ZR’ and ‘ZR+’ pluggables will deliver distances from 10km up to thousands of km. Sampling during 2020.

## Slide 15: 400G LAN options for SMF + 100G breakout
400GBase-FR4 (4x100 PAM4, CWDM grid, 2km reach)
400GBase-LR4 (4x100 PAM4, CWDM grid, 10km reach)
But also:
100GBase-LR (single λ 100G, 1311nm, 10km reach)
  Interoperates with 400GBase-DR4 – breakout 4x100G lanes on an MPO connector
  Already price-competitive vs. ”standard” 4-λ 100GBase-LR4

## Slide 16: 400G LAN options for SMF – CWDM breakout
400GBase-FR4 (4x100 PAM4, CWDM grid, 2km reach)
400GBase-LR4 (4x100 PAM4, CWDM grid, 10km reach)
These optics use 4x100G lasers
What if we could break these out into single 100G lanes?
  Requires CWDM coloured 100G single-λ optics
  Possible PoP architectures with 400G core and 100G-uplinked edge devices
  Scaling existing 100G links to 4x100G
  LONAP will test during 2H 2020

## Slide 17: Possible CWDM 100G breakout architecture

## Slide 18: Summary
Optics world is fast-developing
Some standards are moving quickly towards obsolescence, sometimes without even making it to manufacture
Single-lambda 100G is likely to dominate shorter range interconnection in the future
We can scale cost-effectively

## Slide 19: Thoughts? Comments?