## Slide 1: Seamless SR ARCHITECTURE
Shraddha Hegde
UKNOF-47
April 2021

## Slide 2: Why Seamless SR?
Widely Deployed Distributed network architecture such as Seamless MPLS.
5G, IOT and Network traffic growth bringing Scaling and low latency requirements with E2E view
Natural Upgrade needed from Seamless MPLS architecture to Segment Routing
Lesser protocols and operationally easy
E2E network slicing

## Slide 3: SEAMLESS MPLS ARCHITECTURE
Core 1
Metro1
Metro 3
End to End Services: EVPN, IPVPN, IP
IBGP-LU
PE1
PE2
PE5
PE6
Access
Access
Intra domain TE Controller
IBGP-LU
IBGP-LU
EBGP-LU
EBGP-LU
Large networks segregated into multiple IGP domains
Core is in one IGP domain.
Each of the metros in separate IGP domain
BGP-LU provides E2E connectivity
Services only on access node. Option C connectivity via BGP-LU
Highly scalable architecture
Widely deployed
LDP/RSVP
LDP/RSVP
LDP/RSVP

## Slide 4: SEAMLESS SR: INTRODUCTION
Core
Metro1
Metro 3
SR-MPLS (v4v6)
SR TE-MPLS (v4/v6)
LDP
End to End Services: EVPN, IPVPN, IP
PE1
PE2
PE5
PE6
Access
Access
Independent SR migration in each domain
BGP-LU for E-2-E connectivity
Deterministic labels with BGP Prefix-SID (RFC 8669)
SR-TE Domain
IGP-SR
LDP
draft-hegde-spring-mpls-seamless-sr
ABR1
ABR2
ABR3
ABR4
ABR5
ABR6
ABR7
ABR8

## Slide 5: 5G TRANSPORT REQUIREMENTS
Massive bandwidth
Timing and E2E Latency
Operational Simplicity
High availability
High scalability
E2E Service Differentiation
Application aware routing

## Slide 6: Limitations of BGP-LU/BGP-PREFIX SID
6
Provides a single E2E path
The path selection is based on BGP best path selection, other parameters such
as low latency cannot be used
Multiple loopbacks with BGP-LU need to be used for multiple paths
Service mapping need to be done at every border node
Need a mechanism to simplify for 5G transport

## Slide 7: BGP ClaSSFUL Transport (BGP-CT)
A mechanism for extending color-mapping across multiple ASes.
No need for a controller, but can be used if desired
No need to expose internal topology of a domain to any other domain
Each domain can make its own choice of transport technology independently of what other domains are using
SR-TE, Flex-Algo, RSVP…
BGP-CT acts as the “glue” between domains
BGP-CT is similar to BGP-LU, except that it has {egress PE, color} granularity
Color denotes the “flavor” of the transport e.g. minimum latency, cheapest monetary cost.
See https://datatracker.ietf.org/doc/draft-kaliraj-idr-bgp-classful-transport-planes/

## Slide 8: BGP-CT
PE2: 10.0.0.1
e.g. Color 100 = cheapest cost
Color 200 = minimum latency
PE1
ASBR1
AS2
AS3
AS1
ASBR2
ASBR3
ASBR4
10.0.0.1/32:
Color 100, Label L1
Color 200, Label L2
BGP-CT:
Color 100
Color 100
Color 100
Color 200
Color 200
Color 200
PE1 maps prefixes (according to color community) to the matching color BGP-CT label and local tunnel or flex-algo to ASBR1.
In turn, ASBR2 maps traffic to tunnel or flex-algo to ASBR3 according to the color of the incoming BGP-CT label.

## Slide 9: BGP-CT
9
RED Transport Class
BLUE Transport Class
GREEN Transport Class
Core
Metro1
Metro 3
SR-TE-MPLS (v4/v6)
IBGP-CT
PE1
PE2
PE5
PE6
IBGP-CT
EBGP-CT
EBGP-CT
End to End Colored transport satisfying SLAs
IGP-SR/flex-algo
IGP-SR/flex-algo
BGP-CT NLRI:
Prefix : PE loopback
RD : Distinguisher
Route Target community:
Corresponds to Transport Class
BGP-CT is independent of any VPN. It does not require VPN configuration.

## Slide 10: SEAMLESS SR : CLASSFUL TRANSPORT PACKET FORWARDING
10
Core
Metro1
Metro 3
SR-TE-MPLS (v4/v6)
PE1
PE2
PE5
PE6
Prefix : PE5
RD: 5.5.5.5
RT: red
Label: L1
Nexthop; PE5
Prefix : PE5
RD: 5.5.5.5
RT: red
Label: L2
Nexthop; ABR7
ABR1
ABR2
ABR3
ABR4
ABR5
ABR6
ABR7
ABR8
Prefix : PE5
RD: 5.5.5.5
RT: red
Label: L3
Nexthop; ABR5
Prefix : PE5
RD: 5.5.5.5
RT: red
Label: L4
Nexthop; ABR3
Prefix : PE5
RD: 5.5.5.5
RT: red
Label: L5
Nexthop; ABR1
VPN prefix: v1
RD: X
RT: Y
Ext color comm: Red
Label: Lv1
Data packet
Lv1
L5
Flex-algo label
Data packet
Lv1
L4
Data packet
Lv1
L3
SR-TE Label
SR-TE Label
Data packet
Lv1
L2
Data packet
Lv1
L1
Flex-algo label
Data packet
Lv1

## Slide 11: Resiliency
11
11
11
11
Core
Metro1
Metro 3
PE1
PE2
PE5
PE6
Intra domain TE Controller
Anycast loopbacks used as nexthops
Same BGP-CT label on both ABRs
TI-LFA for the anycast prefixes
ABR1
ABR2
ABR3
ABR4
IBGP
IBGP
IBGP
PE5:
50.50.50.50
Label L1
Pnh: 50.50.50.50
RT: 100:1
PE6:
50.50.50.50
Label L1
Pnh:50.50.50.50
RT: 100:1
Anycast loopback 50.50.50.50
Anycast loopback 40.40.40.40
Anycast loopback 30.30.30.30
ABR3:
50.50.50.50
Label L2
Pnh: 40.40.40.40
RT: 100:1
ABR4:
50.50.50.50
Label L2
Pnh: 40.40.40.40
RT: 100:1
ABR1:
50.50.50.50
Label L3
Pnh: 30.30.30.30
RT: 100:1
ABR3:
50.50.50.50
Label L3
Pnh: 30.30.30.30
RT: 100:1

## Slide 12: USeCASES

## Slide 13: Data sovereignty Use case
Multiple AS
Each AS represents a continent
Data sovereignty
  Avoid node A and C
This “avoid node A& C” constraint is not applicable in AS1 and AS2
AS1
AS2
AS3
B
A
C
D
PE1
PE2
ASBR1
ASBR2
ASBR3
ASBR5
ASBR4

## Slide 14: Data sovereignty Use case
Red LSP created on ASBR4
Since ASBR5 is connected to A & C, Red LSP isn’t created
Red transport class created on all border nodes
Resolution
  AS3: Strict resolution
  AS1 &AS2: Resolve on Red fallback on best
AS1
AS2
AS3
B
A
C
D
PE1
PE2
ASBR1
ASBR2
ASBR3
ASBR5
ASBR4
Red LSP with avoid A&C
Red transport class

## Slide 15: Solution with BGP-CT
AS1
AS2
AS3
A
B
C
D
PE1
PE2
ASBR1
ASBR2
ASBR3
ASBR4
Prefix : PE2
RD: RD1
RT: red
Label: L1
Nexthop; PE2
Prefix : PE2
RD: RD1
RT: red
Label: L2
Nexthop: ASBR4
Prefix : PE2
RD: RD1
RT: red
Label: L3
Nexthop: ASBR3
Prefix : PE2
RD: RD1
RT: red
Label: L4
Nexthop: ASBR2
Prefix : PE2
RD: RD1
RT: red
Label: L5
Nexthop: ASBR1
Data packet
Lv1
L5
IGP label
Data packet
Lv1
L4
Data packet
Lv1
L3
Data packet
Lv1
L2
Data packet
Lv1
L1
Flex-algo label
Data packet
Lv1
IGP label
AS1 and AS2 do not need to create Red Transport Tunnel. BGP-CT will use best effort paths in AS1 and AS2

## Slide 16: USECASES: E2E LOW LATENCY ROUTING
16
Core
Metro1
Metro 3
IBGP
PE1
PE2
PE5
PE6
Agg
Agg
Access
Access
IBGP
IBGP
EBGP
EBGP
Intra-domain latency accumulated
BGP extension to carry accumulated latency metric in AIGP sub-TLV
BGP best path selection at every border node based on accumulated latency metric
Latency metric :10
Acc Latency:
10 +2 =12
Acc Latency:
12 +20 =32
Acc latency:
32+2 =34
Acc Latency:
34 +1=35
Latency metric :10
Accu Latency:
10 +5 =15
Accu latency:
15 +20 =35
Acc latency:
35+5 =40
Acc Latency:
40 +2=42
draft-ietf-idr-performance-routing

## Slide 17: THANK YOU