## Slide 1
BIDI: Building the BBC’s media CDN
2nd November 2020
Alistair Wooldrige
Senior product manager, OTG Media Distribution.
alistair.wooldrige@bbc.co.uk

## Slide 2
Agenda
Introduction
BIDI growth so far
Future plans

## Slide 3
Introduction

## Slide 4
Lots of media to distribute over IP
Introduction

## Slide 5
Video clients
Introduction
TV
66%
PC
10%
Mobile
9%
Tablet
15%

## Slide 6
Segmented media
Introduction
1.m4s
2.m4s
3.m4s
4.m4s
5.m4s
315.m4s
6.m4s
Split into ~4 second segments.
Client downloads segments in advance, over HTTP.

## Slide 7
Segmented Media: Adaptive Bit Rate (ABR)
Introduction
1.m4s
2.m4s
3.m4s
4.m4s
5.m4s
1.m4s
2.m4s
3.m4s
4.m4s
5.m4s
1.m4s
2.m4s
3.m4s
4.m4s
5.m4s
12 Mbps
1080p
5 Mbps
720p
2.8 Mbps
540p
Encoder

## Slide 8
Segmented Media: In action
Introduction

## Slide 9
Pull through caching
Introduction
Asset origin
BBC Media Selector
Which CDN?
On-premises origin cache
CDN A
CDN B
BIDI
HTTP GET
HTTP GET
HTTP GET

## Slide 10
Pull through caching
Introduction
Asset origin
BBC Media Selector
Which CDN?
On-premises origin cache
CDN A
CDN B
BIDI
HTTP GET
HTTP GET
HTTP GET

## Slide 11
Definition
Introduction
BIDI:
BBC Internet Distribution Infrastructure
Image: https://www.flickr.com/photos/vintagehalloweencollector/421733590
Buck Rogers (maybe)
BiDi transceivers (no)

## Slide 12
Why build our own CDN?
Introduction
1) IP distribution future
Consumption is transitioning from broadcast (digital terrestrial, satellite, cable) to over-the-top IP distribution.
2) Quality of Service
Optimise hardware and software for high quality of service. Reduce latency for remote UK audiences.

## Slide 13
Content served by bidi
Introduction
BIDI serves UK public service only, focussing on the high volume video on demand content sets:
VoD (75%)
Non VoD (25%)
DASH (60%)
DASH: Dynamic Adaptive Streaming over HTTP. HLS: HTTP Live Streaming.
HLS (36%)
BBC UK CDN traffic breakdown in September 2020:

## Slide 14
BIDI growth so far

## Slide 15
Timeline: R&D Project
BIDI growth so far
Proof of concept built.
Small amount of production traffic.
Handover and joint trial.
2013
2019
2021
R&D project
2015
2017

## Slide 16
Timeline: Production build
BIDI growth so far
Handover complete.
Production build & rewrite.
2013
2019
2021
R&D project
2015
2017
Build

## Slide 17
BIDI Battery
BIDI growth so far
A BIDI battery is the smallest unit of deployment within a PoP. Built with commodity hardware.
Layer-3 switch, for aggregation and high availability.
2 to 4 caching cells
(commodity servers)
BIDI battery

## Slide 18
BIDI Battery: High availability
BIDI growth so far
N+1 resilience
VIP
ECMP
(single)
203.0.113.2
203.0.113.2
203.0.113.2
Servers advertise same VIP over BGP
203.0.113.0

## Slide 19
BIDI Battery: Deployment options
BIDI growth so far
Clients
Peering
Peering
BBC hosted
ISP aggregation PoP
A
B
ISP aggregation PoP

## Slide 20
BIDI Battery: route learning – which clients to serve
BIDI growth so far
ISP aggregation PoP
ISP router A
ISP router B
eBGP
IP ranges that should be served by this battery
IP ranges
Central “bidibrain”
eBGP

## Slide 21
Getting clients to a BIDI battery
BIDI growth so far
ISP aggregation PoP
Playback
Initial
Cloud hosted
Matchmaker
Media manifest request
HTTP redirect to optimal BIDI battery
All subsequent content requests
Client switches to BIDI battery
Extract client IP.
Longest prefix match from IP ranges advertised to each battery.
Tie break with AS path length.

## Slide 22
Timeline: Scale out
BIDI growth so far
Scale out
2013
2019
2021
R&D project
2015
2017
Build

## Slide 23
BIDI caching cells (servers) in production
BIDI growth so far
Chart: 
| 42278 | 42309 | 42339 | 42370 | 42401 | 42430 | 42461 | 42491 | 42522 | 42552 | 42583 | 42614 | 42644 | 42675 | 42705 | 42736 | 42767 | 42795 | 42826 | 42856 | 42887 | 42917 | 42948 | 42979 | 43009 | 43040 | 43070 | 43101 | 43132 | 43160 | 43191 | 43221 | 43252 | 43282 | 43313 | 43344 | 43374 | 43405 | 43435 | 43466 | 43497 | 43525 | 43556 | 43586 | 43617 | 43647 | 43678 | 43709 | 43739 | 43770 | 43800 | 43831 | 43862 | 43891 | 43922 | 43952 | 43983 | 44013 | 44044 | 44075
In production | 16 | 18 | 18 | 18 | 20 | 20 | 36 | 36 | 36 | 36 | 36 | 36 | 36 | 36 | 36 | 36 | 36 | 36 | 36 | 36 | 36 | 38 | 38 | 38 | 38 | 38 | 38 | 38 | 38 | 38 | 38 | 38 | 38 | 36 | 47 | 47 | 50 | 59 | 59 | 59 | 59 | 59 | 59 | 59 | 59 | 60 | 60 | 60 | 60 | 75 | 78 | 78 | 78 | 78 | 82 | 90 | 93 | 102 | 102 | 102

## Slide 24
BIDI estate size (November 2020)
BIDI growth so far
102 | caching servers
26 | switches
24 | datacentres
3 | ISPs

## Slide 25
Peering locations
BIDI growth so far
Public peering:
LINX LON1 + LON2.
IXManchester.
IXScotland (from Manchester).
LONAP.
Private peering:
Telehouse Docklands West, London.
Digital Realty Sovereign House, London.
Equinix MA1, Manchester.
Equinix LD7, Slough (coming soon).

## Slide 26
BIDI monthly traffic peak
BIDI growth so far
Chart: Throughout (Gbps)
| 42339 | 42370 | 42401 | 42430 | 42461 | 42491 | 42522 | 42552 | 42583 | 42614 | 42644 | 42675 | 42705 | 42736 | 42767 | 42795 | 42826 | 42856 | 42887 | 42917 | 42948 | 42979 | 43009 | 43040 | 43070 | 43101 | 43132 | 43160 | 43191 | 43221 | 43252 | 43282 | 43313 | 43344 | 43374 | 43405 | 43435 | 43466 | 43497 | 43525 | 43556 | 43586 | 43617 | 43647 | 43678 | 43709 | 43739 | 43770 | 43800 | 43831 | 43862 | 43891 | 43922 | 43952 | 43983 | 44013 | 44044 | 44075 | 44105
Traffic peak | 55.3 | 68.09 | 76.4 | 81.3 | 71.69 | 71.5 | 68 | 65 | 80.8 | 83.3 | 91.4 | 99.3 | 103.2 | 89.6 | 127 | 134 | 193.38 | 177.9947 | 167.3666 | 190.5258 | 226.4338 | 249.2326 | 320.6368 | 247.4693 | 242.952 | 310.1794 | 359.5068 | 334.0609 | 346.9529 | 346.6209 | 376.2271 | 334.3023 | 452.2263 | 657.942 | 464.048 | 544.6058 | 653.0892 | 714.6033 | 768.6006 | 815.5865 | 913.3475 | 797.9266 | 845.5836 | 796.3595 | 838.7284 | 898.6294 | 1062.0558 | 974.2936 | 939.232 | 1020.4338 | 954.0139 | 971.3961 | 1038.438 | 1143.2869 | 1101.2146 | 991.475 | 938.8396 | 1079.6465 | 1214

## Slide 27
BIDI monthly traffic peak
BIDI growth so far
Chart: Throughout (Gbps)
| 42339 | 42370 | 42401 | 42430 | 42461 | 42491 | 42522 | 42552 | 42583 | 42614 | 42644 | 42675 | 42705 | 42736 | 42767 | 42795 | 42826 | 42856 | 42887 | 42917 | 42948 | 42979 | 43009 | 43040 | 43070 | 43101 | 43132 | 43160 | 43191 | 43221 | 43252 | 43282 | 43313 | 43344 | 43374 | 43405 | 43435 | 43466 | 43497 | 43525 | 43556 | 43586 | 43617 | 43647 | 43678 | 43709 | 43739 | 43770 | 43800 | 43831 | 43862 | 43891 | 43922 | 43952 | 43983 | 44013 | 44044 | 44075 | 44105
Traffic peak | 55.3 | 68.09 | 76.4 | 81.3 | 71.69 | 71.5 | 68 | 65 | 80.8 | 83.3 | 91.4 | 99.3 | 103.2 | 89.6 | 127 | 134 | 193.38 | 177.9947 | 167.3666 | 190.5258 | 226.4338 | 249.2326 | 320.6368 | 247.4693 | 242.952 | 310.1794 | 359.5068 | 334.0609 | 346.9529 | 346.6209 | 376.2271 | 334.3023 | 452.2263 | 657.942 | 464.048 | 544.6058 | 653.0892 | 714.6033 | 768.6006 | 815.5865 | 913.3475 | 797.9266 | 845.5836 | 796.3595 | 838.7284 | 898.6294 | 1062.0558 | 974.2936 | 939.232 | 1020.4338 | 954.0139 | 971.3961 | 1038.438 | 1143.2869 | 1101.2146 | 991.475 | 938.8396 | 1079.6465 | 1214

## Slide 28
BIDI monthly traffic peak
BIDI growth so far
Chart: Throughout (Gbps)
| 42339 | 42370 | 42401 | 42430 | 42461 | 42491 | 42522 | 42552 | 42583 | 42614 | 42644 | 42675 | 42705 | 42736 | 42767 | 42795 | 42826 | 42856 | 42887 | 42917 | 42948 | 42979 | 43009 | 43040 | 43070 | 43101 | 43132 | 43160 | 43191 | 43221 | 43252 | 43282 | 43313 | 43344 | 43374 | 43405 | 43435 | 43466 | 43497 | 43525 | 43556 | 43586 | 43617 | 43647 | 43678 | 43709 | 43739 | 43770 | 43800 | 43831 | 43862 | 43891 | 43922 | 43952 | 43983 | 44013 | 44044 | 44075 | 44105
Traffic peak | 55.3 | 68.09 | 76.4 | 81.3 | 71.69 | 71.5 | 68 | 65 | 80.8 | 83.3 | 91.4 | 99.3 | 103.2 | 89.6 | 127 | 134 | 193.38 | 177.9947 | 167.3666 | 190.5258 | 226.4338 | 249.2326 | 320.6368 | 247.4693 | 242.952 | 310.1794 | 359.5068 | 334.0609 | 346.9529 | 346.6209 | 376.2271 | 334.3023 | 452.2263 | 657.942 | 464.048 | 544.6058 | 653.0892 | 714.6033 | 768.6006 | 815.5865 | 913.3475 | 797.9266 | 845.5836 | 796.3595 | 838.7284 | 898.6294 | 1062.0558 | 974.2936 | 939.232 | 1020.4338 | 954.0139 | 971.3961 | 1038.438 | 1143.2869 | 1101.2146 | 991.475 | 938.8396 | 1079.6465 | 1214
249,000 | concurrent streams
708,000 | TCP connections (ESTABLISHED)
96.7 % | offload
26 kW | server power draw
0.048 Wh | per episode (27m 15s)

## Slide 29
BIDI offload
BIDI growth so far
Chart: 
| 42339 | 42370 | 42401 | 42430 | 42461 | 42491 | 42522 | 42552 | 42583 | 42614 | 42644 | 42675 | 42705 | 42736 | 42767 | 42795 | 42826 | 42856 | 42887 | 42917 | 42948 | 42979 | 43009 | 43040 | 43070 | 43101 | 43132 | 43160 | 43191 | 43221 | 43252 | 43282 | 43313 | 43344 | 43374 | 43405 | 43435 | 43466 | 43497 | 43525 | 43556 | 43586 | 43617 | 43647 | 43678 | 43709 | 43739 | 43770 | 43800 | 43831 | 43862 | 43891 | 43922 | 43952 | 43983 | 44013 | 44044 | 44075
Offload | 0.97268 | 0.96872 | 0.97647 | 0.98023 | 0.9735 | 0.96651 | 0.9547 | 0.95119 | 0.9286 | 0.95253 | 0.95651 | 0.9308 | 0.9275 | 0.9351 | 0.8897 | 0.9061 | 0.8695 | 0.8379 | 0.8392 | 0.8913 | 0.8944 | 0.9153 | 0.9182 | 0.91 | 0.882 | 0.8623 | 0.8639 | 0.8653 | 0.845 | 0.8229 | 0.8332 | 0.824 | 0.8349 | 0.9063 | 0.911 | 0.9224 | 0.9434 | 0.9602 | 0.9694 | 0.9635 | 0.9567 | 0.9622 | 0.9631 | 0.9541 | 0.9622 | 0.9649 | 0.9622 | 0.9626 | 0.9517 | 0.9506 | 0.9386 | 0.9232 | 0.9379 | 0.928 | 0.9348 | 0.9377 | 0.9364 | 0.9397

## Slide 30
Vod 24 hour working set size
BIDI growth so far
Chart: Working set size (Terabytes)

## Slide 31
 | 4 Gbps | 20 Gbps | >70 Gbps
Processor | 20 cores Dual socket 2.20 GHz / 190 W | 36 cores Dual socket 2.30 GHz / 280 W | 36 cores Dual socket 2.60 GHz / 300 W
RAM | 128 GiB | 256 GiB | 384 GiB
Storage | 1.3 TB SATA 6 x 480 GB SSDs 1 x HW RAID 1+0 | 19.2 TB SATA 10 x 1.92 TB SSDs 10 x HW RAID 0 | 80 TB NVMe 10 x 8 TB SSDs JBOD
Network | 20 Gbps 2 x 10 G NICs | 40 Gbps 2 x dual 10 G NICs | 100 Gbps 1 x 100 G NIC
Cache hardware evolution
BIDI growth so far

## Slide 32
SSD performance – learning the hard way
BIDI growth so far
SSD
Magic controller compression
Pesky RAID controllers
Performance cliff edges
Fast burnout
Write-back caching
High latencies / TRIM.
Disappearing acts.
Testing disks: Lessons from our odyssey selecting replacement SSDs:
https://www.bbc.co.uk/blogs/internet/entries/ce3eff16-228f-49a0-8d4e-d1a013e4895f

## Slide 33
Cache Software evolution
BIDI growth so far
 | 4 Gbps | 20 Gbps | >70 Gbps
Web server | Varnish | httpd (front) nginx httpd (back) | OpenResty (nginx + LuaJIT)
BGP | ExaBGP | ExaBGP | BIRD
Services | Java | Node.js | Python

## Slide 34
Future plans

## Slide 35
SmartShard
Future plans
Popular programmes/streams
Served by all batteries, prioritising the edge.
Unpopular programmes/streams
Served by reduced number of core batteries.
Weighted rendezvous hashing distributes long tail.
80 TB
20 TB
20 TB
Utilisation based spill-over

## Slide 36
IPv6
Still to do:
IPv6 route ingest.
Dual stack addressing.
Actually doing it.
IPv6 and ISP portal
Future plans
ISP portal
Web portal making BIDI information available for embedded ISPs:
Monitoring.
Emergency + scheduled traffic drains.
Route inspector.

## Slide 37
Linear streams
Future plans
Onboard linear streams
Next largest content set.
IP distribution expected to increase.
Less predictable traffic patterns and a high peak/mean ratio.

## Slide 38
MBIDI
Future plans
Smaller 1U chassis
Single socket CPU
96 (logical) cores,
128 x PCIe 4 lanes.
91.8 TB cache storage
6 x 15.3 TB NVMe, PCIe 4.
Dual-port 100 GbE
Next generation caching cell, targeting deeper levels of the network:
Standalone operation.
Smaller unit size.
Increased power efficiency.

## Slide 39
New Slough PoP
Future plans
New BIDI PoP at Equinix LD7, Slough:
Network infrastructure ready.
On-premises origin cache operational.
BIDI planned operational in March 2021.