## Slide 1: Hollow Core Fiber: What is it, and why should you be interested?
Geoff Bennett, Infinera Corp.

## Slide 2
>400 Million km produced annually
>5 Billion km
fiber deployed worldwide
Four Decades of Progress
1 Mb/s  800 Gb/s per transponder
800,000
times increase
1 Mb/s  80 Tb/s per fiber pair
80 Million
times increase
The Foundation of Global Communications
Transported on
Optical Fiber

## Slide 3: If you let signals go everywhere…The inverse square law
Isaac Newton applied this to gravitational forces, but…
At distance, r we have an area for this signal of A
At distance 2r the area is 4A
And at distance 3r the area is 9A
The strength of the signal is inversely proportional to the square of the distance

## Slide 4
How to create an optical waveguide

## Slide 5: How Does Optical Fibre Work?
Cladding
Core
Refractive
Index
Light is guided to stay in the core – hence, waveguide
SiO2
SiO2 + GeO2
Graded Index
Only room for one mode
Single mode fiber
Notes: As light enters the core, it may be travelling at a slight angle, and will hit the refractive index boundary. As long as the angle of incidence is shallow, the boundary will act as a mirror, and reflect the light back into the core at exactly the same angle. This phenomenon is known as Total Internal Reflection, and I’ve given some references to the topic in your Further Reading section. So instead of leaving the fibre, the light is guided down it, bouncing off the sides as it goes.

## Slide 6: Silica Core Optical Fiber: Attenuation vs Wavelength
Visible spectrum (380-700 nm)
Minimum attenuation in the C and L Bands
Note: When I talk about “capacity limits”, I’m assuming C+L operation

## Slide 7: Don’t shout so loud: What is a nonlinear effect?
Imagine you’re listening to music and you keep turning up the volume
It’s similar with optical fiber – above a certain optical power level the signals will distort – adding lots of noise!!
There are several nonlinear effects
Self Phase Modulation
Cross Phase Modulation
Four Wave Mixing
Above a certain volume level the music will become distorted

## Slide 8: Capacity Limits of Today’s Optical Fiber
Super C-Band
Super L-Band
50 Tb/s
50 Tb/s
42 Tb/s
42 Tb/s
Extended C-Band
Extended L-Band

## Slide 9: Capacity at Longer Reach
Super C-Band
Super L-Band
100 Tb/s
1,000 km
Super C-Band
Super L-Band
75 Tb/s
3,000 km
Super C-Band
Super L-Band
50 Tb/s
7,500 km

## Slide 10: Latency: Glass Core vs Air Core
4.897 µs per km
Glass core
Refractive index = 1.46
Air core
Refractive index = 1.000293
3.353 µs per km

## Slide 11: What have I told you about conventional optical fiber?
Optical fiber acts as a waveguide
Single mode operation – no modal dispersion
Attenuation varies with wavelength
  Today’s optical communication is in the C-Band and L-Band
  There is so much more potential capacity in today’s optical fiber, but only at shorter distances because of higher attenuation
Glass is a nonlinear medium – a major limiting factor
Glass core fiber has higher latency than transmission through air

## Slide 12: Which means that…
A wider bandwidth waveguide would increase capacity-reach
A more linear optical waveguide would increase capacity-reach
As a separate market driver (ie. not related to capacity-reach) it would be great to find a waveguide that has lower latency than glass
All of these limitations derive from using fiber with a glass core

## Slide 13
Hollow Core Fiber

## Slide 14: Types of HCF: How they create the waveguide
Hollow Core Fiber
Photonic Bandgap
Anti-Resonant
Dual Nested Anti-Resonant Nodeless Fiber (DNANF)
Seems to be at a “technology dead end”:
For optical communications
For the moment
1991
2011
Today

## Slide 15: HCF is (mostly) a Great British Invention!!
First AR-HCF proposal in 2011 by Dr. AD Pryamikov
First HCF proposal in 1991 was Photonic Bandgap
The most recent breakthroughs have been at Southampton University

## Slide 16: Another evolutionary view
Nested
structures
PBG  ARF
PBG
ARF
125 µm
30 µm
10 µm

## Slide 17: The Big News This Year (Announced at OFC)
<0.22 dB per km at 1310 nm
<0.18 dB per km at 1550 nm
DNANF
vs
<0.35 dB per km at 1310 nm
<0.20 dB per km at 1550 nm
SMF-28e+
<0.31 dB per km at 1310 nm
<0.17 dB per km at 1550 nm
SMF-28 ULL
More spectrum = more capacity

## Slide 18
So what are people using this for?

## Slide 19: Today it’s all about lower latency
Low Latency Financial Services
Distributed DC
Server Performance
5G Fronthaul Network Enhancement

## Slide 20
Future Potential for HCF

## Slide 21: Lower Attenuation Over More Spectrum
Silica core fiber has low attenuation here
HCF has already shown low attenuation here…
…and there may be more to come

## Slide 22: Lower Nonlinear Penalty (potentially)
The NL penalty in HCF may be multiple orders of magnitude lower than silica core fiber
BUT…this may depend on what you fill it with
AIR
INERT GAS
VACUUM
A low NL penalty means we can send much stronger optical signals into the fiber, and boost fiber capacity as a result

## Slide 23: Questions About The Practicality of HCF
Can it be made in quantity?
Does it work with the existing fiber ecosystem?
Deployment guidance vs conventional fiber
  Pull force, bend radius, connector fitting
How will HCF age after deployment?
Are the microstructures vulnerable to in-service deformation? (e.g. in subsea)
How can we amplify over those additional wavebands?
What are the nonlinear advantages of the HCF you choose to deploy?

## Slide 24: A really brief summary of HCF status today
HCF is being deployed today in low latency applications, with multiple field trials in progress
HCF has the future potential to deliver far more fiber capacity with wideband, low nonlinear performance
Between then and now there are quite a few practical challenges with HCF…but most are engineering problems

## Slide 25
THANK YOU
Geoff Bennett
gbennett@infinera.com