## Slide 1
Notes: Mark

## Slide 2: What is WDM? Wave Division Multiplexing

## Slide 3: Point to point connections over Fibre
    Plug in a *transceiver into the switch/router - using a separate fibre for each connection
    *often referred to as ‘Grey’ transceivers – typically wideband 1310 or 1550
Optical Fibre
Optical Fibre
Optical Fibre
Optical Fibre
Location A
Location B
Great if you have lots of fibre

## Slide 4
What if you don’t have enough fibre capacity?
Or what about combing more connections over one fibre?
You could dig & install more fibre ....
You could rent more fibre ....

## Slide 5: What if we could combine the Colours (lambdas)?
    If we combined (Mux) the matching colours onto a single fibre pair, we could put many connections on that fibre.
    We call that Multiplexing (combining) and DeMultiplexing (separating)
    Matching Colours (Lambdas) at each end
Optical Fibre
Location A
Location B
Mux/Demux
Mux/Demux

## Slide 6: Types of WDM
Coarse Wavelength Division Multiplexing (CWDM) 18 channels – ITU-T G.694.2
Dense Wavelength Division Multiplexing (DWDM) more than 100 channels - ITU-T G.709
DWDM channels are located towards the end of the CWDM spectrum. Therefore you can combine CWDM and DWDM on the same link.
CWDM
DWDM
Wavelength
1271
1291
1311
1331
1351
1371
1391
1411
1431
1451
1471
1491
1511
1531
1551
1571
1591
1611
18 Channels
100+ Channels
C Band - 1528.77 nm to 1563.86 nm

## Slide 7: What about PON?
You can run WDM in conjunction with PON, Incl OTDR port
ITU-T G.984.5 (05/2018) Recommendation

## Slide 8: WDM Types Mux/DeMux
Dual fibre optical multiplexer/demultiplexer
Uses two separate fibre connections for transmission (TX) and reception (RX).
The number of wavelengths therefore is identical to the number of TX/RX channels.
Single fibre optical multiplexer/demultiplexer
Requires a single fibre for both transmission (TX) and reception (RX).
The number of required wavelengths therefore is double the number of TX/RX channels.

## Slide 9: WDM Types OADM
Dual fibre optical add/drop multiplexer
East and West connection each uses a separate fibre for transmission (TX) and reception (RX).
The number of add/drop channels is identical to the number of wavelengths.
Single fibre optical add/drop multiplexer
East and West connections each only require a single fibre for TX and RX.
The number of add/drop channels therefore is double the number of wavelengths.

## Slide 10: Project Example
Neutral Host
USA
Customer requirements
Metro access DWDM link
Reach 40 – 60 km
Up to 5 intermediate drop nodes with 8 redundant services
Monitoring channels at each node

## Slide 11: Passive vs Active WDM
Active Transport System
    Conversion from client (“grey transceivers”) to line (“coloured transceivers”) signals by transponder cards
    Requires additional hardware, eg a chassis with redundant power and management card
    Often cards fixed to service type & speed
    Ideal if you need remote demarcation device
Passive Transport System
Agnostic to service type, eg 1G, 10G, 25G, 100G, 400G….
No conversion, coloured transceivers are plugged straight into terminal equipment
Fewer active elements => higher reliability, lower latency
Transceivers are managed by terminal equipment (Switch/Router etc.)
Passive WDM >80% power savings vs Active system

## Slide 12: Source: xHaul Technology & Economics (macro-cell centric) A Sutton

## Slide 13: What about…..
Transponder
Muxponder
Amplification
Dispersion Compensation
Optical Protection
Power supplies
Management
Transponding Mux
Dispersion Comp.
Amplification
Optical Protection
Management
WebGUI
CLI
SDN/NetConf
EMS
Muxponder
Enclosures
Transponder
These are important if building an Optical Transport System, but not strictly WDM

## Slide 14: Parts that are often included in WDM Systems
Transponder
      Transponds one wavelength (lambda) to another wavelength (lambda)
Muxponder
      Multiplexes more than 1 wavelength onto 1 wavelength, (eg 4 x 100G onto 1 x 400G)
Dispersion Compensation
      Cancelling/limiting the chromatic dispersion
Amplification
      Amplifies signal. Most Amp’s work around 1550, You can amplify at 1310
Optical Protection
      Automatic switch over to another fibre. Quicker than L2/3 re-route
You can choose:
Vendor lock-in
or
Open Line System

## Slide 15: Project Example – ISP backhaul (PON network)
ISP
United Kingdom
WDM Units
  Passive DWDM ‘Single Fibre’
Active Units
  EDFA modules
  Dispersion Compensation
  modules

## Slide 16: So how do you get higher speeds …100G, 400G etc?

## Slide 17: Modulation formats
Direct Detect: NRZ
Direct Detect: PAM4
Coherent: QAM
Uses two states 1 and 0 in amplitude.
Higher attenuation allowed compared to PAM4.
Base modulation for direct detect for up to 25G per lane.
Uses four states 00,01,10 and 11 in amplitude.
Allows double the data rate compared to NRZ with same baud rate.
Standard modulation for direct detect > 25G per lane.
Uses multiple states in amplitude and phase.
Allows higher data rate for similar baud rate than NRZ and PAM4
Coherent requires more complex modulation and demodulation than direct detect.

## Slide 18: Dispersion & Attenuation
Dispersion on PAM4 signal
Attenuation 25G NRZ signal
86 ps/nm dispersion
no dispersion
-5dBm @ receiver
-10dBm @ receiver
Dispersion causes Jitter on signal limiting reach.
PAM 4 signal is more sensitive to dispersion and attenuation than NRZ.

## Slide 19: Dispersion & Attenuation for fibers
Lowest attenuation for single mode 1550nm.
Attenuation for different fibers
Dispersion depending on reach
Acceptable dispersion for 100Gb/s PAM 4 is -40 - +20ps/nm.
Dispersion is lowest in 1310nm range
Dispersion is limiting possible wavelength area for direct detect.

## Slide 20: Conclusions
Deploying WDM is much cheaper & quicker than installing new fibre
An active WDM system can make sense in certain circumstances, eg demarcation point
A passive WDM system can make sense in certain circumstances, eg agnostic to data rate, services that run over it
Decide if you want a vendor tie-in (everything from one vendor) or Open Line Systems
Transceivers/Transponders define the speed – not WDM
      All vendors use the same ITU WDM grids

## Slide 21: Many thanks steve.jones@hubersuhner.com +44 7900 881 729

## Slide 22: Backup slides

## Slide 23: Direct Detect vs. Coherent Receiver
Vpd
TIA
Out-
Out+
CDR
PIn
IPD
PD
Data outputs
Out+
Out-
clock
PIn
Chromatic Dispersion Compensation
Frequency Offset Compensation
Carrier Phase recovery
Polarization Demultiplexing
Decoding….
Ppolx
Ppoly
90°
90°
0°
0°
IxI
IxQ
IyI
IyQ
Digital Signal Processor (DSP)
Laser
Hybrid coupler
Hybrid coupler
Balanced detectors
Polarization splitter
Direct Detect Receiver
Coherent Receiver
Out+
Out-

## Slide 24: Coherent or Incoherent – Outline & Basics
    Direct Detect
    Simple modulation (Amplitude NRZ / On-off keying to Pulse Amplitude PAM4)
    Hence simpler (lower cost) electronics
    Sensitive to dispersion effects
    Coherent
    Advanced modulation (QPSK, 8QAM,.. 64QAM to PM-QPSK), Amplitude, Phase and Polarization (12x capacity / lambda)
    Hence requiring high-end (higher cost) additional analogue electronics (additional laser oscillators, DSP chips etc)
    Compensates dispersion effects
Dispersion effects grow with data rate and distance
The higher the bit rate &/ distance, the more DD is replaced by Coherent

## Slide 25: Coherent vs Direct Detect Summary
Direct detect
Coherent
Transition area
For higher reach and data rate, direct detect is getting more and more complex increasing price and power consumption.
  DSP is required for equalization.
  Dispersion needs to be compensated.
For higher data rate spectral efficiency is getting more important.
Also coherent is significant improving price and power consumption due to integration and smaller IC structures.
For transition area also other parameters are important for choice of available transceivers like available wavelengths, switches…
Power consumption Im-DD transceiver projection